3GPP TSG-RAN WG2 #121bis-e	R2-230xxxx

E-meeting, April 2023

Agenda Item:	6.10.1

Source:	OPPO

Title:	[Draft] [AT121bis-e][416][Relay] Paging monitoring by L2 relay (OPPO)

Document for:	Discussion, Decision

# Introduction

This document is a report on the following email discussion:

- [AT121bis-e][416][Relay] Paging monitoring by L2 relay (OPPO)

Scope: Discuss R2-2302576 and conclude on the proposals.

Intended outcome: Report to CB session

Deadline: Monday 2023-04-24 2359 UTC

# Contact Information

| Company | Name | Email Address |
| --- | --- | --- |
| OPPO | Qianxi Lu | qianxi.lu@oppo.com |
| Xiaomi | Xing Yang | Yangxing1@xiaomi.com |
| Ericsson | Nithin Srinivasan | nithin.srinivasan@ericsson.com |
| vivo | Boubacar Kimba | kimba@vivo.com |

# Discussion

## L2 U2N Relay + ranPagingInIdlePO

For the interaction between L2 U2N Relay and ranPagingInIdlePO feature, 2576 stated that

<2576 Start>

Based on TS 38.304, the UE may use different ways to derive i_s, based on both UE capability and network capability

In RRC_INACTIVE state, if the UE supports inactiveStatePO-Determination and the network broadcasts ranPagingInIdlePO with value "true", the UE shall use the same i_s as for RRC_IDLE state. Otherwise, the UE determines the i_s based on the parameters and formula above.

Currently, L2 Relay UE does not support the option of using ‘the same i_s as for RRC_IDLE state.

We understand there are 2 ways to conclude on this issue.

- Keep the current spec as it is, which means RAN node would not force an L2 Relay UE to monitor paging for a L2 remote UE by using the same i_s as for RRC_IDLE state. Considering RAN node has only per-cell flag of ranPagingInIdlePO to enable/disable this feature, the only way-out is RAN node, when enabling L2 SL relay feature, disable the ranPagingInIdlePO feature.

- Force L2 Relay UE to perform the paging using the same i_s as for RRC_IDLE state. This way-out requires a huge change to the spec, since it means the remote UE which supports inactiveStatePO-Determination should only camp on relay UE which also support inactiveStatePO-Determination, and thus it means a revision to discovery message for relay UE to broadcast its capability. Furthermore, the remote UE has to notify the relay UE on the support of inactiveStatePO-Determination.

So at the current stage, it is suggested to go for solution-1.

RAN2 clarifies L2 U2N SL Relay UE paging monitoring for L2 Remote UE using i_s as for RRC_IDLE state is not supported in Rel-17.

<2576 Stop>

Q1-1: Do you agree with P1 in 2576, i.e., R2 not pursue supporting paging monitoring by RRC_INACTIVE UE using i_s as for RRC_IDLE state in L2 U2N Relay scenario?

- Agree

- Disagree

| Company | Agree/Disagree | Comments |
| --- | --- | --- |
| OPPO | Agree | Otherwise, there is a need for huge additional work. |
| Xiaomi | Agree |  |
| Ericsson | Agree |  |
| vivo | Agree |  |

Q1-2: If agree with Q1-1, how do you think to capture the conclusion?

- Option-1: Chairman Note

- Option-2: Capture in spec (if this option is selected, please clarify which spec to impact)

| Company | Option | Comments |
| --- | --- | --- |
| Xiaomi | Option 1 |  |
| Ericsson | Option 1 | If the current spec is not broken, there is no need to capture what we do not support |
| vivo | Option 1 |  |

Q1-3: If disagree with Q1-1, how do you think to enable the solution?

- Option-1: A revision to discovery message for relay UE to broadcast its capability on supporting inactiveStatePO-Determination. Furthermore, the remote UE has to notify the relay UE on the support of inactiveStatePO-Determination.

- Option-2: Other (if this option is selected, please clarify what is the solution)

| Company | Option | Comments |
| --- | --- | --- |

## L2 U2N Relay + eDRX

For the interaction between L2 U2N Relay and eDRX based paging, 2576 stated that

<2576 Start>

Based on TS 38.304, the UE may use DRX or eDRX for paging monitoring

In RRC_IDLE state, if eDRX is configured by upper layers, i.e., TeDRX, CN, according to clause 7.4:

-	If TeDRX, CN is no longer than 1024 radio frames:

-	T = TeDRX, CN;

-	else:

-	During CN configured PTW, T is determined by the shortest of UE specific DRX value, if configured by upper layers, and the default DRX value broadcast in system information.

In RRC_INACTIVE state, if eDRX is configured by RRC, i.e., TeDRX, RAN , and/or upper layers, i.e., TeDRX, CN, as defined in clause 7.4:

-	If both TeDRX, CN and TeDRX, RAN are no longer than 1024 radio frames, T = min{TeDRX, RAN, TeDRX, CN}.

-	If TeDRX, CN is no longer than 1024 radio frames and no TeDRX, RAN is configured, T is determined by the shortest of UE specific DRX value configured by RRC and TeDRX, CN.

-	If TeDRX, CN is longer than 1024 radio frames:

-	If TeDRX, RAN is not configured:

-	During CN configured PTW, T is determined by the shortest of the UE specific DRX value (s), if configured by RRC and/or upper layers, and a default DRX value broadcast in system information. Outside the CN configured PTW, T is determined by the UE specific DRX value configured by RRC;

-	else if TeDRX, RAN is no longer than 1024 radio frames:

-	During CN configured PTW, T is determined by the shortest of the UE specific DRX value, if configured by upper layers and TeDRX, RAN, and a default DRX value broadcast in system information. Outside the CN configured PTW, T is determined by TeDRX, RAN.

Where the yellow part highlights the cases where eDRX cycle would be used.

Considering currently, L2 U2N Relay would not know the eDRX cycle but just the DRX cycle (no longer than 256 radio frame)

SL-PagingInfo-RemoteUE-r17 ::=                SEQUENCE {

sl-PagingIdentityRemoteUE-r17                 SL-PagingIdentityRemoteUE-r17,

sl-PagingCycleRemoteUE-r17                    PagingCycle                                        OPTIONAL  -- Need M

}

PagingCycle ::=                     ENUMERATED {rf32, rf64, rf128, rf256}

In order to support the eDRX for L2 remote UE, similar to the issue above, it requires the remote UE which supports eDRX should only camp on relay UE which also support in eDRX, and thus it means revision to discovery message for relay UE to broadcast its capability. Furthermore, the remote UE has to notify relay UE on the support of eDRX.

Given that the RAN node has the capability to turn off the eDRX feature

SIB1-v1700-IEs ::=               SEQUENCE {

[…]

eDRX-AllowedIdle-r17         ENUMERATED {true}                                                      OPTIONAL,  -- Need R

eDRX-AllowedInactive-r17     ENUMERATED {true}                                                      OPTIONAL,  -- Cond EDRX-RC

[…]

}

It is suggested to avoid co-configuration of L2 SL Relay and eDRX-based paging delivery.

RAN2 clarify L2 U2N SL Relay UE paging monitoring for L2 Remote UE using the eDRX paging cycle is not supported in Rel-17.

<2576 Stop>

Q2-1: Do you agree with P2 in 2576, i.e., R2 not pursue supporting eDRX-based paging monitoring for L2 U2N remote UE by L2 U2N Relay UE?

- Agree

- Disagree

| Company | Agree/Disagree | Comments |
| --- | --- | --- |
| OPPO | Agree | Otherwise, there is a need for huge additional work. |
| Xiaomi | Agree |  |
| Ericsson | Agree |  |
| vivo | Agree |  |

Q2-2: If agree with Q2-1, how do you think to capture the conclusion?

- Option-1: Chairman Note

- Option-2: Capture in spec (if this option is selected, please clarify which spec to impact)

| Company | Option | Comments |
| --- | --- | --- |
| Xiaomi | Option 1 |  |
| Ericsson | Option 1 | If the current spec is not broken, there is no need to capture what we do not support |
| vivo | Option 1 |  |

Q2-3: If disagree with Q2-1, how do you think to enable the solution?

- Option-1: A revision to discovery message for relay UE to broadcast its capability on supporting eDRX-based paging. Furthermore, the remote UE has to notify the relay UE on the eDRX cycle.

- Option-2: Other (if this option is selected, please clarify what is the solution)

| Company | Option | Comments |
| --- | --- | --- |

# Conclusion

We have the following proposals:

Proposal 1	xxx.

# Reference

- R2-2302576	Discussion on paging monitoring by SL L2 U2N Relay	OPPO	discussion	Rel-17	NR_SL_relay-Core, NR_redcap-Core, TEI17