3GPP TSG-RAN WG2 #121bis-e	R2-22xxxxx

Online, 17 – 26 April, 2023

Agenda Item:	7.9.4

Source: 	LG Electronics Inc.

Title: 	Report of [AT121bis-e][419][Relay] Remaining high-priority proposals on multi-path (LG)

Document for:	Discussion and decision

# Introduction

This is the trigger of the following email discussion:

[AT121bis-e][419][Relay] Remaining high-priority proposals on multi-path (LG)

Scope: Discuss the remaining HP proposals from R2-2303857.

Intended outcome: Report to CB session

Deadline: Monday 2023-04-24 2359 UTC

This email discussion aims to discuss the remaining high proposals from R2-2303857, noting that RAN2 made the following agreements during the first day of RAN2#121bis-e as follows:

Agreements:

The concept of the ‘primary path and primary RLC entity’ is adopted for each MP split bearer configuration according to the existing definition.

In case of duplication, PDCP control PDU only transmits on the primary RLC entity same as legacy.

Non-split SRB1 and 2 over indirect path is not supported in Scenario 2.

Split SRB1 and 2 are supported in Scenario 2 and primary path of the split SRB 1 and 2 is always on direct path.

If UE-UE link failure is detected on indirect path in Scenario 2, the remote UE can report UE-UE link failure to gNB over direct path.  Details of the reporting mechanism can be further discussed.

# Discussion

### Issue A: Proposal 3 from R2-2303857 for indirect path addition from direct path

RAN2 recently discussed the proposal 3 without any agreement as follows:

Proposal 3: Upon RRCReconfiguration message for indirect path addition from direct path, the remote UE sends the RRCReconfigurationComplete message to gNB via the added indirect path for both scenario 1 and 2, when split SRB1 is configured. Discussion: CATT have some concern because this would diverge from the legacy mechanism, so they foresee considerable spec impact. Nokia understand that the reason we did this in Rel-17 was that there was no other option, but here we have both paths, and they think the gNB should control which path is used. E.g., direct path may be faster. InterDigital agree with P3; they think we cannot really compare to legacy operation because it is not two separate cell groups, and this is needed for the idle/inactive relay. ZTE agree with the principle of the proposal, but they think it could be more specific about the conditions; they see that it should be when split SRB1 with duplication (or with primary path as indirect path) is configured. Apple agree with Nokia; considering P1.8A, they think we should follow the legacy operation and leave the path up to network implementation. Huawei understand that the intention is that the complete message goes on the indirect path when duplication is configured. They understand that we have an FFS on whether the primary path can be the indirect path. Qualcomm agree with the proposal as it is, and they assume that if the relay is a Rel-17 relay, the remote UE must use the indirect path.

As recently discussed, some companies agree the proposal in principle with a specific condition, while other companies think that it can be up to network configuration/implementation.

For better understanding companies’ views and more progress, companies are requested to provide their views on the following questions related to the RRCReconfigurationComplete message for indirect path addition from direct path:

Question A1.1: Is there any case that the remote UE sends the RRCReconfigurationComplete message to gNB via the added indirect path for Scenario 1 upon reception of RRCReconfiguration message for indirect path addition from direct path?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes |  |
| OPPO | Yes | At least when split SRB1 is configured with duplication. |
| Apple | Yes |  |
| vivo | Yes |  |
| CATT | Yes | When split SRB1 is configured with duplication or the primary path of split SRB1 is configured to indirect path. |
| ASUSTeK | Yes |  |
| Huawei, HiSilicon | Yes | Split SRB1 with duplication. |
| NEC | Yes | Same view as OPPO |
| ZTE | Yes |  |
| Qualcomm | Yes | Split SRB1 with duplication. |
| InterDigital | Yes | When split SRB1 is configured. We should consider this even for non-duplication in order to trigger the relay UE to move to RRC_CONNECTED. |
| Nokia | Yes |  |
| Fujitsu | Yes |  |
| Lenovo | Yes |  |
| Spreadtrum | Yes |  |
| CMCC | Yes |  |
| Ericsson | Yes |  |
| Samsung | Yes |  |

Question A2.1: (If yes in A1.1) Can you provide condition(s) in which the remote UE sends the RRCReconfigurationComplete message to gNB via the added indirect path for Scenario 1 upon reception of RRCReconfiguration message for indirect path addition from direct path?

For example (not exclusive)

- when split SRB1 with duplication is configured

- when primary path is configured as indirect path

- when relay UE serves as Rel-17 relay

- when gNB directs the RRC message to the indirect path

- Any other?

| Company | Condition(s) | Comment |
| --- | --- | --- |
| Xiaomi | - when split SRB1 with duplication is configured - when primary path is configured as indirect path - when non-split SRB1 is configured on indirect path |  |
| OPPO | ‘when split SRB1 with duplication is configured’ | Whether ‘- when primary path is configured as indirect path’ is also valid depends on the conclusion of scenario-1. |
| Apple | Up to gNB configuration - when split SRB1 with duplication is configured - when primaryRLCentity of split SRB1 is on indirect path - when non-split SRB1 is configured on indirect path |  |
| vivo | when split SRB1 with duplication is configured | We prefer that both primary path of split SRB1 and non-split SRB1 are always configured on direct path, which is more aligned with PCell concept and unified between scenario-1 and scenario-2 |
| CATT | -Split SRB1+duplication - when primary path of split SRB1 is configured as direct path | CATT’s contribution R2-2302603 P12 shows more detailed information on this topic. |
| ASUSTeK | - when split SRB1 with duplication is configured - when relay UE serves as Rel-17 relay |  |
| Huawei, HiSilicon | - when split SRB1 with duplication is configured |  |
| NEC | Up to the configuration of SRB1 by gNB, for example, split or non-split SRB1 on indirect path. |  |
| ZTE | - when split SRB1 with duplication is configured - when primary path is configured as indirect path |  |
| Qualcomm | when split SRB1 with duplication is configured | Other conditions are not concluded so far. |
| InterDigital | - when split SRB1 with duplication is configured - when split SRB1 is configured without duplication (regardless of the primary path) - when non-split SRB1 is configured on indirect path | We think we should make an exceptional case to send the complete message over the indirect path even when split SRB1 is configured with the primary path on the direct to address the relay UE in IDLE/INACTIVE. |
| Nokia | - When split SRB1 with duplication is configured; - if split SRB1 without duplication is configured, when the relay UE is not in RRC_CONNECTED and the gNB configures to transmit the RRCReconfigurationComplete message via the indirect path | if split SRB1 without duplication is configured, when the relay UE is not in RRC_CONNECTED and the gNB configures to transmit the RRCReconfigurationComplete message via the indirect path |
| Fujitsu | when split SRB1 with duplication is configured when primary path is configured as indirect path when non-split SRB1 is configured on indirect path |  |
| Lenovo | when split SRB1 with duplication is configured | ‘split SRB1 with duplication’ is align with legacy for DC. |
| Spreadtrum | when split SRB1 with duplication is configured when primary path is configured as indirect path when non-split SRB1 is configured on indirect path |  |
| CMCC | when split SRB1 with duplication is configured |  |
| Ericsson | when split SRB1 with duplication is configured |  |
| Samsung | -When split SRB1 with duplication is configured -When primary path is configured as indirect path if it is allowed |  |

Question A3.1: Is there any case that the remote UE sends the RRCReconfigurationComplete message to gNB via the direct path for Scenario 1 upon reception of RRCReconfiguration message for indirect path addition from direct path?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes |  |
| OPPO | See comment | This depends on how much complexity we tend to introduce to allow this possibility – if it comes with change on discovery message and enhancement on report by remote UE to network, it is not justified.. |
| Apple | Yes | gNB can configure non-split SRB1 only on direct path, or split-SRB1 but primary RLC entity is in direct path. |
| vivo | Yes |  |
| CATT | Yes |  |
| ASUSTeK | Yes |  |
| Huawei, HiSilicon | Yes |  |
| NEC | Yes | Up to the configuration of SRB1 by gNB, no need to introduce solutions with extra spec impact rather than the SRB1 configuration |
| ZTE | Yes | If the gNB configure the remote UE with direct bearer type or split bearer with direct path as primary path for SRB1, remote UE can only send the RRCReconfigurationComplete message to gNB via the direct path. |
| Qualcomm | Yes | Depends on SRB1 configuration |
| InterDigital | Yes |  |
| Nokia | Yes |  |
| Fujitsu | Yes |  |
| Lenovo | Yes |  |
| Spreadtrum | Yes |  |
| CMCC | Yes |  |
| Yes |  |  |
| Samsung | Yes |  |

Question A4.1: (If yes in A3.1) Can you provide condition(s) in which the remote UE sends the RRCReconfigurationComplete message to gNB via the direct path for Scenario 1 upon reception of RRCReconfiguration message for indirect path addition from direct path?

For example (not exclusive)

- when split SRB1 with duplication is configured

- when primary path is configured as direct path

- when gNB directs the RRC message to the direct path

- when non-split SRB1 is configured on direct path

- when relay UE serves as Rel-18 relay and is in RRC_CONNECTED

- Any other?

| Company | Condition(s) | Comment |
| --- | --- | --- |
| Xiaomi | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Apple | Up to gNB configuration - when split SRB1 with duplication is configured - when primaryRLCentity of split SRB1 is on direct path - when non-split SRB1 is configured on direct path |  |
| vivo | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path | In the last two cases, the new PC5 RRC trigger is used to inform the target relay UE into RRC_CONNECTED. |
| CATT | - when split SRB1 with duplication is configured - when primary path of split SRB1 is configured as direct path - when non-split SRB1 is configured on direct path |  |
| ASUSTeK | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path - when relay UE serves as Re-18 relay and is in RRC_CONNECTED | We think the following two cases are applicable only when gNB knows relay UE is Rel-18 Relay before adding it to remote UE: - when primary path is configured as direct path; - when non-split SRB1 is configured on direct path. |
| Huawei, HiSilicon | The reconfiguration complete message should always be sent on direct path, including: - when split SRB1 with duplication is configured - when primary path is configured as direct path (and we prefer that primary path can only be configured on direct path) - when SRB1 is non split |  |
| NEC | Up to the configuration of SRB1 by gNB, for example, split or non-split SRB1 on direct path. |  |
| ZTE | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Qualcomm | All the list conditions |  |
| InterDigital | - When non-split SRB1 is configured on the direct path | In all the other cases, the complete message should go on the indirect path to allow the relay UE in IDLE/INACTIVE to move to CONNECTED. |
| Nokia | -when split SRB1 with duplication is configured -if split SRB1 without duplication is configured, when the relay UE is in RRC_CONNECTED -if split SRB1 without duplication is configured, when the relay UE is not in RRC_CONNECTED but the gNB configures to transmit the RRCReconfigurationComplete message via the direct path | If the relay UE is in RRC_CONNECTED, we see no reason to send the RRCReconfigurationComplete message to the indirect path. If the relay UE is not in RRC_CONNECTED, and the remote UE sends the RRCReconfigurationComplete message to the direct path, the remote UE sends the PC5-RRC message to bring the relay UE to RRC_CONNECTED. To control the path to send the RRCReconfiugrationComplete, RAN2 needs to discuss further whether primary path is used or another indication is necessary. |
| Fujitsu | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Lenovo | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Spreadtrum | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| CMCC | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Ericsson | when split SRB1 with duplication is configured when primary path is configured as direct path Non-split SRBs is always configured on the direct path | The primary path should always be on the PCell and hence, the direct path |
| Samsung | -when split SRB1 with duplication is configured -when primary path is configured to direct path -when non-split SRB1 is configured at the direct path |  |

Question A1.2: Is there any case that the remote UE sends the RRCReconfigurationComplete message to gNB via the added indirect path for Scenario 2 upon reception of RRCReconfiguration message for indirect path addition from direct path?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes |  |
| OPPO | Yes |  |
| Apple | Yes |  |
| vivo | Yes |  |
| CATT | Yes |  |
| ASUSTeK | Yes |  |
| Huawei, HiSilicon | Yes |  |
| NEC | Yes |  |
| ZTE | Yes |  |
| Qualcomm | Yes |  |
| InterDigital | Yes |  |
| Nokia | Yes |  |
| Fujitsu | Yes |  |
| Lenovo | Yes |  |
| Spreadtrum | Yes |  |
| CMCC | Yes |  |
| Ericsson | Yes |  |
| Samsung | Yes |  |

Question A2.2: (If yes in A1.2) Can you provide condition(s) in which the remote UE sends the RRCReconfigurationComplete message to gNB via the added indirect path for Scenario 2 upon reception of RRCReconfiguration message for indirect path addition from direct path?

For example (not exclusive)

- when split SRB1 with duplication is configured

- when primary path is configured as indirect path

- when gNB directs the RRC message to the indirect path

- Any other?

| Company | Condition(s) | Comment |
| --- | --- | --- |
| Xiaomi | - when split SRB1 with duplication is configured |  |
| OPPO | - when split SRB1 with duplication is configured |  |
| Apple | when split SRB1 with duplication is configured |  |
| vivo | - when split SRB1 with duplication is configured |  |
| CATT | when split SRB1 with duplication is configured |  |
| ASUSTeK | - when split SRB1 with duplication is configured |  |
| Huawei, HiSilicon | - when split SRB1 with duplication is configured |  |
| NEC | - when split SRB1 with duplication is configured |  |
| ZTE | - when split SRB1 with duplication is configured |  |
| Qualcomm | - when split SRB1 with duplication is configured |  |
| InterDigital | - when split SRB1 with duplication is configured | Legacy DC behavior is acceptable here since the relay UE in IDLE/INACTIVE is not supported. |
| Nokia | - when split SRB1 with duplication is configured | As it has been agreed that primary path of split SRB1/2 is always on the direct path, thus “when primary path is configured as indirect path” is not a valid case. |
| Fujitsu | - when split SRB1 with duplication is configured |  |
| Lenovo | - when split SRB1 with duplication is configured |  |
| Spreadtrum | - when split SRB1 with duplication is configured |  |
| CMCC | - when split SRB1 with duplication is configured |  |
| Ericsson | when split SRB1 with duplication is configured |  |
| Samsung | -when split SRB1 with duplication is configured |  |

Question A3.2: Is there any case that the remote UE sends the RRCReconfigurationComplete message to gNB via the direct path for Scenario 2 upon reception of RRCReconfiguration message for indirect path addition from direct path?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes |  |
| OPPO | See comment | This depends on how much complexity we tend to introduce to allow this possibility – if it comes with change on discovery message and enhancement on report by remote UE to network, it is not justified.. |
| Apple | Yes |  |
| vivo | Yes |  |
| CATT | Yes |  |
| ASUSTeK | Yes |  |
| Huawei, HiSilicon | Yes |  |
| NEC | Yes | Up to the configuration of SRB1 by gNB, no need to introduce solutions with extra spec impact rather than the SRB1 configuration |
| ZTE | Yes |  |
| Qualcomm | Yes |  |
| InterDigital | Yes |  |
| Nokia | Yes |  |
| Fujitsu | Yes |  |
| Lenovo | Yes |  |
| Spreadtrum | Yes |  |
| CMCC | Yes |  |
| Ericsson | Yes |  |
| Samsung | Yes |  |

Question A4.2: (If yes in A3.2) Can you provide condition(s) in which the remote UE sends the RRCReconfigurationComplete message to gNB via the direct path for Scenario 2 upon reception of RRCReconfiguration message for indirect path addition from direct path?

For example (not exclusive)

- when split SRB1 with duplication is configured

- when primary path is configured as direct path

- when gNB directs the RRC message to the direct path

- when non-split SRB1 is configured on direct path

- Any other?

| Company | Condition(s) | Comment |
| --- | --- | --- |
| Xiaomi | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Apple | Up to gNB configuration - when split SRB1 with duplication is configured - when primaryRLCentity of split SRB1 is on direct path - when non-split SRB1 is configured on direct path |  |
| vivo | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path | In scenario-2, before the remote UE receives RRCReconfiguration with multi-path configuration, the relay UE has already entered in RRC_CONNECTED. Hence, the path of RRCReconfigurationComplete is not important. |
| CATT | The remote UE should always send RRCReconfigurationComplete message to gNB via the direct path for Scenario 2 |  |
| ASUSTeK | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Huawei, HiSilicon | The reconfiguration complete message is always sent via direct path, as it was agreed that non-split SRB cannot be configured on indirect path, and primary path cannot be indirect path in scenario 2. |  |
| NEC | Up to the configuration of SRB1 by gNB, for example, split or non-split SRB1 on direct path. |  |
| ZTE | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Qualcomm | All the list conditions |  |
| InterDigital | All the time | In our understanding, there is no case where non-split SRB is configured over the indirect path for scenario 2, so regardless of split or non-split SRB (with/without duplication), the complete will always go over the direct path. |
| Nokia | -when split SRB1 with duplication is configured -when primary path is configured as direct path -when non-split SRB1 is configured on direct path | It means, the RRCReconfigurationComplete message should always be transmitted via direct path for scenario 2. |
| Fujitsu | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Lenovo | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path | Complete message should be sent on direct path all the time since primary path has to be configured in direct path. |
| Spreadtrum | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| CMCC | - when split SRB1 with duplication is configured - when primary path is configured as direct path - when non-split SRB1 is configured on direct path |  |
| Ericsson | when split SRB1 with duplication is configured | The following agreements already cover this scenario: Non-split SRB1 and 2 over indirect path is not supported in Scenario 2. Split SRB1 and 2 are supported in Scenario 2 and primary path of the split SRB 1 and 2 is always on direct path. |
| Samsung | -when split SRB1 with duplication is configured -when primary path is configured at direct path -when non-split SRB1 is configured on direct path |  |

### Issue B: High Priority Proposals for Scenario 1

RAN2 recently discussed the proposal 1.7A/B without any agreement as follows:

High Priority Proposals for Scenario 1 Proposal 1.7A: [HP] The network is allowed to configure SRB1 and SRB2 on same path or different paths. Proposal 1.7B: [HP] The bearer type (i.e. direct bearer, indirect bearer, or multi-path bearer) of SRB1 and SRB2 can be independently configured by the network. Discussion: Ericsson are not OK with allowing SRB1/SRB2 on different paths. Qualcomm also think they should be on the same path, and further that it should always be the direct path, which may be more reliable. MediaTek think they should be on the same path and wonder about the motivation for configuring them differently. LG indicate that the proposal reflects a split in the contributions. They think from a signalling perspective, different paths can be allowed, but the network can always choose to configure them on the same path. Nokia agree that there is no motivation for different paths, but they think it can be left to the network. They think RAN2 could decide not to optimise for different paths. Vivo see no need for a restriction on separating SRB1 and SRB2 if SRB1 is on the direct path. On P1.7B, they think the indirect bearer could be removed. InterDigital are OK with Nokia’s suggestion on P1.7A. On P1.7B, they are a bit sceptical about removing the indirect bearer, because we already agreed that we can have non-split indirect SRB1. Vivo think SRB1 should not be able to go on the indirect path; they do not see a motivation for this. Xiaomi think it is motivated because the remote UE may be moving out of direct coverage and have the indirect path be more reliable; they do not see a technical problem with using the indirect path. Huawei think non-split SRB1 on indirect path is not needed; there is a restriction in legacy operation that non-split SRB1 cannot be configured on SCG, and we already agreed that the Pcell is the Uu cell, so they do not see the coverage argument as correct. They would like to avoid the spec and test complexity of allowing it. OPPO think the indirect bearer should be omitted from P1.7B. ZTE agree with the original proposals; the UE may initially access through the indirect path, at which time only the indirect bearer can be configured, and they think the network should not be forced to reconfigure to the direct path if the indirect path is good enough. Ericsson think we should not do flexibility for its own sake. They see that we know the direct path is good and do not see why we should use the indirect path for signalling. They think we would only add the direct path in the case mentioned by ZTE if the UE is near cell centre. InterDigital think we should keep the existing agreements allowing non-split SRB on either path and having the Pcell on the direct path. Ericsson note that the flexibility is still there through using split SRB if necessary. InterDigital understand that this would lead to cases where the UE was required to transmit on the direct path even though indirect is more reliable. Samsung think the key point is whether we can configure non-split SRB1/SRB2 on indirect path. They see no reason to restrict SRB2 but maybe some reason to restrict SRB1, since the Pcell is on the direct path. The bearers have different priorities and they think it might be preferable to have higher reliability for SRB1.

As captured above, in the previous discussion some companies challenged the following RAN2 agreement made at the initial stage for scenario 1. Thus, it seems good to check whether companies are really willing to modify the following agreements:

- Agreements

  - For scenario 1, SRB1 and SRB2 can be configured on either the direct or the indirect path, or on both at least with duplication.  FFS if they can be configured on different paths from one another.

  - Upon detection of 3GPP-defined RLF failure in one path, remote UE (configured with MP) can report path failure via the alternative available path if SRB1 is configured on the alternative path or split SRB1 is configured.

Question B1: Should we support the case of non-split SRB1 on the indirect path based on the previous agreement for scenario 1? If yes, when non-split SRB1 can be configured on the indirect path? If no, why?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes | Indirect path may be more reliable than direct path, when remote UE is at cell edge. Furthermore, since the relay UE and remote UE may connect to the same cell, non-split SRB1 on indirect path doesn’t conflict with the Pcell on indirect path. |
| OPPO | No | We do not see a need to introduce a new scenario where SRB1 is limited to Scell only but not covering Pcell. If so, there could be strange case that RRC re-establishment triggered even when Pcell does not have RLF problem. |
| Apple | No |  |
| vivo | No | It has not clear motivation to separately configure Pcell on direct and SRB1 on indirect path, which will introduce additional complexity of RLF and RRC re-establishment. |
| CATT | Yes | Indirect path may be also in the PCell. |
| ASUSTeK | No | We think support of direct SRB1 and split SRB1 with duplication enabled are sufficient. |
| Huawei, HiSilicon | No | We do not see the motivation to have non-split SRB on indirect path. for the scenario mentioned by other companies that remote UE is accessing via a L2 Relay first and added a direct link later, this should be a PCell change (aka reconfiguration with sync) procedure, which involves some reconfiguration, and reconfiguring SRB1’s RLC bearer from SL RLC to Uu RLC is not a issue. |
| NEC | Yes | Same view as Xiaomi, gNB can always select a path with higher reliability for SRB1. |
| ZTE | Yes | When UE initially connects to the network via the indirect path, only indirect bearer can be configured for SRB1 at this time. Even if UE is later configured with direct path addition, the indirect bearer for SRB1 can be kept without change. |
| Qualcomm | No | Direct path is more reliable than indirect path because Uu coverage is much larger than PC5 coverage and indirect path is more easy to be failure since any hop failure with result in indirect path failure. Additionally, decouple SRB1 and PCell path is not supported by current spec. if agreed, then RAN2 needs to review all the existing procedures to check whether there are problems with it, which will spend much time on the useless scenario. |
| InterDigital | Yes | There is no clear motivation to revert the agreement as there is nothing broken with the current agreement (i.e., the relay could be connected to the PCell). More importantly, the gNB should be free to choose the most reliable path for SRB1 without always being forced to configure SRB1 with duplication. |
| Nokia | Yes | We see no technical problem or additional complexity in support of non-split SRB on the indirect path while having PCell on the direct path. PCell is not always the best in link quality: the path with better link quality can change dynamically, or the indirect path may provide better link quality if the UE is in cell edge. Assuming the single gNB, non-split SRB on the indirect path or split SRB with primary RLC on the indirect path only allows reliable transmission of RRC signal with no harm. |
| Fujitsu | Yes | Agree with Xiaomi. |
| Lenovo | Yes | when UE is located in the cell edge, indirect path is more reliable. |
| Spreadtrum | Yes |  |
| CMCC | No |  |
| Ericsson | No | CP should always be on the more robust path i.e., direct path in this case. The indirect path is over two hops and the stability of PC5-link is questionable. Uu-link has been optimized for CP signaling significantly. For a cell-edge scenario, firstly, we think a multipath will not be configured. Even if that was the case, we can always configure split-SRB configuration with/without duplication. |
| Samsung | No |  |

Question B2: Should we support the case of non-split SRB2 on the indirect path based on the previous agreement for scenario 1? If yes, when non-split SRB1 can be configured on the indirect path? If no, why?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes | Same as B1. |
| vivo | No |  |
| CATT | Yes | Same as B1. |
| Huawei, HiSilicon | No | No clear motivation either, and prefer to align with SRB1. |
| NEC | Yes | When the relay UE and remote UE served by the same cell. |
| ZTE | Yes |  |
| Qualcomm | No | No motivation, and this is not aligned with current spec. Currently both SRB2 and SRB1 are configured on the same path which is the path of PCell. If agreed, RAN2 needs to spend much time to review carefully whether all the existing procedures can work well, which is not necessary. |
| InterDigital | Yes | Same as B1 |
| Nokia | Yes | Same as B1. No reason to differentiate SRB1 and 2. |
| Fujitsu | Yes |  |
| Lenovo | Yes | Same as B1 |
| Spreadtrum | Yes |  |
| CMCC | No |  |
| Ericsson | No | SRB1/2 should be configured on the same path. |
| Samsung | Yes | SRB2 has lower priority than SRB1. If we consider direct path is different from indirect path from some angles, e.g., reliability, latency, etc., SRB2 on indirect path can be up to gNB decision. |

Rapporteur’s original intention with the proposal 1.7A/B was whether the network is allowed to configure SRB1 and SRB2 on same or different paths with same or different bearer types. Some companies think that we need restriction while other companies think that it can be up to network i.e. the network can anyway avoid different paths or different bearer types by proper configuration.

Question B3: Do you think that we should restrict configuration of SRB1 and SRB2 with different bearer types by 3GPP specification (e.g. by ASN.1, field description or NOTE in 38.331) for scenario 1?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | No | It can be up to NW implementation. We don’t see technical problem to support any combinations. |
| OPPO | No | In legacy multi-path like scenario, CA, DC, the legs to be used are all configured per-bearer, so do not see the need to restrict now for MP-relay. |
| vivo | No | It is up to NW implementation to configure the bearer type (i.e. direct bearer, split bearer) for SRB1 and SRB2. |
| CATT | No | It can be up to NW implementation. The configuration is per RB. |
| ASUSTeK | No | We think it can be up to network. |
| Huawei, HiSilicon | No | We agree with others the bearer type is configured per bearer. |
| NEC | No with comments | We do not restrict the bearer type, but restrict when to configure the indirect SRB1, see our comments for QB2 |
| ZTE | No |  |
| Qualcomm | No |  |
| InterDigital | No | Should be upto NW implementation |
| Nokia | No | It can be left up to gNB configuration. As commented during the meeting, the important thing is that RAN2 will not optimize further to support different types of SRB1/2. |
| Fujitsu | No | It is up to NW implementation. |
| Lenovo | No | up to NW implementation. |
| Spreadtrum | No |  |
| Ericsson | See comments | Not sure about the intention of the question |
| Samsung | No | Up to network |

Question B4: (If yes in B3) Which combination of different SRB1/2 types should be restricted or supported for scenario 1?

- Direct SRB1 + Indirect SRB2

- Direct SRB1 + Split SRB2

- Split SRB1 + Direct SRB2

- Split SRB1 + Indirect SRB2

- Indirect SRB1 + direct SRB2

- Indirect SRB1 + split SRB2

| Company | Restricted (i.e. not supported) combination number(s) | Supported combination number(s) | Comment |
| --- | --- | --- | --- |
| Xiaomi |  | All | It can be up to NW implementation. We don’t see technical problem to support any combinations. |
| OPPO | 5,6 | At least 2, 3 Open to 1,4 | Whether 1,4 is OK depends on whether indirect SRB2 is acceptable. |
| Apple | 5,6 | 2,3, | For 1,4 we have no strong view |
| vivo | 1,4,5,6 | 2,3 | Better keep it simple |
| CATT |  | All |  |
| ASUSTeK | 5, 6 | 1, 2, 3, 4 |  |
| Huawei, HiSilicon | 1,4,5,6 | 2,3 | We do not need to allow many configuration combos for no good reason. |
| NEC |  | All |  |
| ZTE |  | All | It is up to network implementation on the potential configuration. We see no blocking issue for the different combinations. |
| Qualcomm | 1,4,5,6 | 2,3 | No motivation to have so many combinations, and such flexible combinations bring much complexity to UE implementation. And we need to spend time to review whether existing procedure could work for all the configurations. |
| InterDigital |  | All | Placing restrictions only adds further specification effort |
| Nokia |  | All | It is up to gNB. |
| Fujitsu |  | All | We have no strong view on the restriction of the combinations. |
| Lenovo |  | All | Up to gNB implementation. |
| Spreadtrum |  | All | Up to gNB implementation. |
| CMCC | 1,4,5,6 | 2,3 |  |
| Ericsson | See comments | See comments | It is cumbersome to go through each of the combinations. It would also be very difficult to capture such restrictions. High-level principles should be discussed first before talking about combinations |
| Samsung | 5,6 | 1,2,3,4 |  |

### Issue C: High Priority Proposals for Scenario 2

RAN2 did not discuss the proposal 2.1B/C and 2.3 due to lack of time.

High Priority Proposals for Scenario 2 Proposal 2.1B: [HP] The remote UE reports relay UE’s ID to gNB for indirect path addition, when both UEs are in RRC_CONNECTED. FFS which UE ID is used as relay UE’s ID. FFS for relay UE’s serving cell information. Proposal 2.1C: [HP] RAN2 is requested to discuss whether to support more than one relationship between relay UE and remote UE. Proposal 2.3: [HP] RAN2 is requested to discuss whether to support indirect path change in Scenario 2

Question C1: Do you support proposal 2.1B (possibly with or without modification)?

Proposal 2.1B: [HP] The remote UE reports relay UE’s ID to gNB for indirect path addition, when both UEs are in RRC_CONNECTED. FFS which UE ID is used as relay UE’s ID. FFS for relay UE’s serving cell information.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | Yes |  |
| Apple | No | We think RAN2 shall first confirm that relay UE is already in CONNECTED state before gNB initiates indirect path additional procedure (as we assume the inter-UE relationship is only reported when both UEs are in CONNECTED state). Then, we think it is also possible to consider to let relay UE to report remote UE C-RNTI as a feasible alternative after relay UE enters RRC_CONNECTED. It is an equivalent solution as the one in P2.1B, so we think both are equally feasible and has the same complexity. |
| vivo | Yes |  |
| CATT | Yes |  |
| ASUSTeK | Yes | We think remote UE can trigger relay UE to enter RRC_CONNECTED based on relay and remote UE implementation, if remote UE would like to add indirect path. Thus, it is reasonable for remote UE to report relay UE’s ID after relay UE enters RRC_CONNECTED. |
| Huawei, HiSilicon | Yes | For Apple’s comments, we agree with 1) that for simplicity we can assume relay UE is already in connected state before UE ID reporting. Regarding 2), we agree that relay reporting is also feasible, but we slightly prefer remote UE reporting, because it is more like the measurement reporting, the legacy measurement logic and signalling can be reused. |
| NEC | No | We support to report the ID of RRC_CONNECTED Relay UE. But how to be aware of the RRC state of Relay UE by Remote UE should be left to UE implementation since there is an ideal UE-UE link. |
| Qualcomm | No | It is really bad and wasteful to request all the candidate Relay UE(s) entering CONNECTED state before MP relay is configured. The gNB may not configure MP to Remote UE in case that e.g. gNB is overload, Remote UE or Relay UE is not authorized, etc. When gNB is overload, the Remote UE may trigger the Relay UE entering CONNECTED state again and again in order to request MP relay operation. It is a huge power saving and signalling consumption for all the candidate Relay UEs to enter CONNECTED state every time the Remote UE reports the Relay UE ID to the gNB. I think RAN2 had similar discussion for U2N relay in Rel-17. About how to identify the Relay UE, the existing U2N relay UE ID IE can be reused, and the same procedure used for Scenario 1 can be reused for Scenario 2. We can clarify UE ID format and definition is out of 3GPP. This also complies with the RAN2 and RAN principle that solutions for scenario 1 and scenario 2 should be commonality. |
| InterDigital | Yes |  |
| Fujitsu | Yes |  |
| Lenovo | Yes | the report can be used to indicate the association between remote UE and relay UE in scenario#2. |
| Spreadtrum | Yes |  |
| CMCC | Yes |  |
| Ericsson | No strong opinion | The UEs in RRC_CONN can also individually report their relationship |
| Samsung | Partial yes with comments | We agree to let remote UE to report the ID of relay UE. However, the proposal raises two issues which are dependent each other: Issue 1: how to know the RRC status of Relay UE by remote UE Issue 2: which relay ID is used If C-RNTI for issue 2 is selected, it means that the relay UE ID can be reported only when the relay UE is in CONNECTED status; then we need another solution of relay UE ID when relay UE is in IDLE/INACTIVE status. If another ID, e.g., Relay UE L2 ID, for issue 2 is selected, the RRC status of relay UE is not that important. Note that, we are considering the indirect path addition, which means that the relay UE can be in any RRC status before adding indirect path. Thus, we suggest that at the proposal is not necessarily required to link the status of relay UE, and it can be revised as: The remote UE reports relay UE’s ID to gNB for indirect path addition, when both UEs are in RRC_CONNECTED. FFS which UE ID is used as relay UE’s ID. FFS for relay UE’s serving cell information |

Question C2: (If no in C1) What will be an alternative to proposal 2.1B?

| Company | Alternative proposal | Comment |
| --- | --- | --- |
| Apple | For gNB trigger indirect path addition, either RRC_CONNECTED remote UE or RRC_CONNECTED relay UE can report the inter-UE relationship (e.g. peer UE’s C-RNTI) to gNB. |  |
| NEC | How to be aware of the RRC state of Relay UE by Remote UE is up to UE implementation. | Additional proposal |
| ZTE | Yes |  |
| Qualcomm | Candidate or target Relay UE can be in IDLE or Inactive state. The existing U2N relay UE ID IE in MR and SUI message can be reused, and the same procedure used for Scenario 1 can be reused for Scenario 2. We can clarify UE ID format and definition is out of 3GPP. | Some benefits on this alternative: - Less spec change - Save Relay power consumption and signalling overhead - More candidate Relay UEs to be considered, increase the possibility of MP. - Comply with the RAN2 and RAN principle that solutions for scenario 1 and scenario 2 should be commonality. |
| Nokia | Yes | In R17 the selection of a Relay in IDLE/INACTIVE is possible, and the Relay moves into CONNECTED when relay connection is established. For MP, we can keep this principle. |
| Samsung | The remote UE reports relay UE’s ID to gNB for indirect path addition. FFS which UE ID is used as relay UE’s ID. FFS for relay UE’s serving cell information | As commented in Question C1 |

Question C3: Which type of UE ID can be included in the report to gNB (e.g. relay’s C-RNTI or s-TMSI)?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | C-RNTI | Since relay UE is in RRC_CONNECTED, C-RNTI is enough. |
| OPPO | C-RNTI | While we do not see the need of PCI since ideal connection to us means the relay/remote UE are collocated in practice, so not see the scenario where the two are of different cells. |
| Apple | C-RNTI |  |
| vivo | C-RNTI |  |
| CATT | C-RNTI |  |
| ASUSTeK | C-RNTI |  |
| Huawei, HiSilicon | C-RNTI |  |
| NEC | C-RNTI |  |
| ZTE | Both C-RNTI or S-TMSI are acceptable |  |
| Qualcomm | UE ID used in U2N relay | As in Question C2. |
| InterDigital | C-RNTI |  |
| Nokia | C-RNTI |  |
| Fujitsu | C-RNTI |  |
| Lenovo | See comments | If remote UE and relay UE are belonging to the different cell, C-RNTI may be not sufficient. |
| Spreadtrum | C-RNTI |  |
| CMCC | C-RNTI |  |
| Ericsson | C-RNTi |  |
| Samsung | Comments | If we select C-RNTI, which means that when adding indirect path, the relay UE should be in connected status. How about the case when the relay UE is in IDLE/INACTIVE status? In our understanding, the indirect path addition is triggered after the remote UE reports ID of relay UE. However, at this moment, relay UE can be in any status. Before concluding C-RNTI, we need resolve the issue: What is our assumption on the RRC status of the relay UE when reporting the relay UE ID by remote UE? And how to realize such assumption? |

Concerning proposal 2.1C, some companies think that one of multiple candidate relay UE can be selected for a remote UE in scenario 2 e.g. based on UE-to-UE link status, while other companies think that more than one candidate relay UE is not needed for a remote UE considering UE-to-UE link is ideal.

Question C4: Do you support more than one relationship between relay UE and remote UE. If yes, why we need more than one relationship even with ideal link between the UEs.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | No | We understand the relationship between remote UE and relay UE is fixed. |
| OPPO | No | We understood the ideal connection is typically wired connection, so not sure if it is a typical case that ‘more than one relationship between relay UE and remote UE’ |
| Apple | No |  |
| vivo | No | More than one relay UE or even multiple legs can be postponed into the later release. |
| CATT | No |  |
| Huawei, HiSilicon | Yes | It is possible that a remote UE can have more than one candidate relay UE connected with. The scope only restrict that one relay can provide relaying service, i.e. configured as indirect path. To support more than one association has minor spec effort, while restricting to one is not future-proof. |
| NEC | No | At least for this release. |
| ZTE | Yes | More than one relay UEs are available. However, gNB can configure at most one indirect path for remote UE at a given time. We have agreed that “If UE-UE link failure is detected on indirect path in Scenario 2, the remote UE can report UE-UE link failure to gNB over direct path”. In this case, it is natural for gNB configure other candidate relay UE for remote UE once failure happens. |
| Qualcomm | Yes | To clarify this question, only one Relay UE is selected for MP operation, but Remote UE can associate and connect with multiple candidate Relay UEs. It should not restrict the real deployment, e.g. Remote UE can associate with two Relay UEs via WiFi as today. |
| InterDigital | No | For scenario 2, the relationship is fixed. |
| Nokia | No |  |
| Fujitsu | No |  |
| Lenovo | No | The case of multiple associated relay UEs can be discussed in future release. |
| Spreadtrum | No |  |
| CMCC | Yes |  |
| Ericsson | No |  |
| Samsung | Yes | Since we agree that the UE-UE link is up to implementation. However, it does not mean the implementation is restricted to a fix relationship only. In addition, we already agree to support the indirect path failure, and failure reporting. Allowing another candidate relay UE, the failure recovery can be carried out autonomously. Otherwise, the indirect failure recovery due to UE-UE link failure should completely rely on the UE-UE link, which is not performed autonomously. |

Proposal 2.3 seems related to proposal 2.1C. If there are multiple candidate relay UEs for a remote UE, relay UE change could be supported for a better relay UE. But, if not, it is not clear whether to support relay UE change.

Question C5: Do you support indirect path change for scenario 2?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Xiaomi | No | Since only one relay UE is assumed for remote UE, indirect path change is necessary. |
| OPPO | No | Same reason as for C4 above. |
| Apple | No |  |
| vivo | No |  |
| CATT | No |  |
| Huawei, HiSilicon | Yes | Path change is basically an old path release + new path addition, both of release and addition would be supported, we do not see the point to rule out release+addition at the same time. |
| NEC | No |  |
| ZTE | Yes with comments | Even if we support indirect path change for scenario 2, as agreed in RAN2#120 meeting, RAN2 should not do additional work over scenario 1 to enable it. |
| Qualcomm | Yes | Same view as Huawei, from specification point of view, we don’t need such restriction. The use case is as commented in C4. |
| InterDigital | No |  |
| Nokia | No |  |
| Fujitsu | No |  |
| Lenovo | No |  |
| Spreadtrum | No |  |
| CMCC | Yes |  |
| Ericsson | No |  |
| Samsung | Yes | We think the procedures defined for scenario 1 can be reused for this case. |

# Conclusion and recommendation

In conclusion, Rapporteur recommends agreeing the following proposals: