## Slide 1: Way forward for DRX, eDRX and PTW value ranges for NB-IoT
Ericsson, Vodafone, ZTE, Docomo, Huawei, …
3GPP TSG-RAN WG2 Meeting #93bis R2-163053 Dubrovnik, Malta, 11 – 15 April 2016

## Slide 2: Background
NB-IoT has similar framework for paging as eMTC (DRX, eDRX and PTW), except:
  Maximum eDRX cycle is 3 hours
  Maximum number of L1 repetitions for paging is 2048
  UE specific DRX is not supported
RAN2 intended to specify a single DRX cycle value:
  For simplicity
  However difficult to agree on a single value
  Different NW deployments may support different coverage enhancement levels and require different DRX cycle values

## Slide 3: Proposal
The following DRX, eDRX and PTW value ranges are supported in NB-IoT:
  Issue 1 DRX:
    NB-IoT supports {1.28, 2.56, 5.12, 10.24} sec
  Issue 2 eDRX:
    NB-IoT supports {20.48, 40.96, 81.92, 163.84, 327.68, 655.36, 1310.72, 2621.44, 5242.88, 10485.76} sec.
  Issue 3 PTW:
    Working assumption: {0, 5, 7.5, 10, 12.5, 15, 17.5, 20, 22.5, 25, 27.5, 30, 32.5, 35, 37.5, 40} sec.
    NOTE: The WA can be re-visit according to the outcome of email discussion [93#xx][LTE/eDRX] eDRX paging solution