## Slide 1: Support non-3GPP access for wearables
​Institute for Information Industry
3GPP TSG-RAN WG2 #95 R2-165148
Gothenburg, Sweden, 22rd – 26th August 2016 Agenda: 8.4.1

## Slide 2: Introduction
In Busan meeting, the RAN Plenary approved the revised FS_feD2D_IoT_relay_wearable SID (Further Enhancements to LTE Device to Device, UE to Network Relays for IoT and Wearables) and agreed to study and evaluate a generic Layer 2 evolved UE-to-Network Relay architecture, including the possibility of a common solution supporting UE to network relaying over non-3GPP access (Bluetooth/WiFi).
In this paper, we want to discuss an additional non-3GPP access relaying scenarios.

## Slide 3: Discussion
We propose to enhance existing solutions to support remote UE to relay UE connectivity via non-3GPP access technology.
Existing solutions
  EPC-level ProSe Discovery in conjunction with WLAN direct discovery and communication
  Relaying via PC5 (need enhance to support non-3GPP access)
  Relaying via S2a or S2b (R2-163949)
  Wifi tethering (R2-163949)

## Slide 4: EPC-level ProSe Discovery in conjunction with WLAN direct communication
Source: TS 23.303
Right figure shows the high level view of the non-roaming architecture from TS 23.303. In this figure, UE A and UE B use a subscription of the same PLMN, where PC5 is the reference point between ProSe-enabled UEs used for control and user plane for ProSe Direct Discovery, ProSe Direct Communication and ProSe UE-to-Network Relay. In addition, when EPC support for
WLAN direct discovery and communication is requested as part of the EPC-level ProSe Discovery procedure, the additional parameters for support of WLAN direct discovery and communication are enclosed in brackets in the figures. Therefore, the remoted UE can establish a WLAN direct communication via relay UE if remote UEs can support E-UTRAN connection and have 3GPP subscription credentials.

## Slide 5: Relaying via PC5
Source: TS 23.303
In the figure, the ProSe UE-to-Network Relay entity provides the functionality to support connectivity to unicast services for Remote UEs that are not served by E-UTRAN.
The relay UE shall relay unicast between the remote UE and the network, and provide generic function that can relay any type of traffic that is relevant for public safety communication. Therefore, we could enhance ProSe UE-to-Network Relay to support non-3GPP access if remote UEs can support Wi-Fi direct or Bluetooth connection and have 3GPP subscription credentials.

## Slide 6: Wi-Fi tethering
Wi-Fi tethering is a technique where one relay UE provides IP access to the remote UE by announcing itself as a Wi-Fi access point. The other remote UEs may then connect to the relay UE using standard Wi-Fi procedures. Typically IPv4 and NAT are used in the relay UE which implies the remote UE is not visible to the core network or the RAN of the relay UE. Also from the network point of view, all traffic from the remote UE seems to originate from the relay UE. Therefore, we could enhance Wifi tethering by using IEEE 802.11u and Hotspot 2.0 to provide cellular-like experience if remote UEs can support WLAN connection and have 3GPP subscription credentials.
S7/Gx
Relay UE
eNodeB
MME
S-GW
WLAN UE
LTE-Uu
S1-C
HLR
PCRF
S11
IEEE 802.11
P-GW
S1-U
S5/S8
S6a
Gxc

## Slide 7: Potential Additional Relay Scenario (1/2)
UE (Vehicle)
UE (Passenger)
UE (Wearable)
Prose application
evolved PC5
Source: TS 23.303 & TR 23.785
evolved PC5
Source: TR 22.861
Original Path
Access via Passenger UE
Access via Vehicle UE
LTE-Uu

## Slide 8: Potential Additional Relay Scenario (2/2)
Figure shows the in-vehicle ProSe-enabled UE could detect proximity authorized passenger; then it automatically creates WLAN direct connection between passenger’s UE and vehicle’s UE, and routes the traffic of passenger’s UE via vehicle’s E-UTRAN. In addition, the in-vehicle ProSe-enabled UE could also detect proximity authorized passenger’s wearable; then it automatically creates WLAN direct connection between wearable and vehicle’s UE, and routes the traffic of wearable via vehicle’s E-UTRAN.
Proposal 1: To Study remote UE connect to network via in-vehicle ProSe-enable UE.

## Slide 9: Summary
As shown in above analysis there are four existing solutions for doing relaying. EPC-level ProSe Discovery in conjunction with WLAN direct communication effectively support establishing a WLAN direct communication between remoted UE and relay UE, but this can also be achieved by enhancing ProSe UE-to-Network Relay to support non-3GPP access.
Proposal 2: Enhance existed ProSe UE-to-Network Relay to support non-3GPP access.

## Slide 10: References
TS 23.402, “Architecture enhancements for non-3GPP accesses (Release 14) ”
TS 23.303, “Proximity-based services (ProSe) (Release 13)”
TR 23.785, “Study on architecture enhancements for LTE support of V2X services (Release 14)”
TR 22.861, “Feasibility Study on New Services and Markets Technology Enablers for Massive Internet of Things (Release 14)”
RP-161303, “Further Enhancements to LTE Device to Device, UE to Network Relays for IoT and Wearables”, RAN#72, Busan, Korea, June 13 - 16, 2016
R2-163949, “Relaying scenarios for wearables”, RAN2#94, Nanjing, P.R. China, 23rd – 27th May 2016

## Slide 12: Appendix: Relaying via S2a or S2b
Right figure shows the Non-Roaming Architecture within EPS using S5, S2a, S2b from TS 23.402. In this architecture a remote UE may access through a relay UE acted as a trusted or untrusted Wi-Fi access point.
The trusted access point may contact the 3GPP AAA server via STa to authenticate the UE. Then, the data path is routed towards the operator’s PDN GW via S2a.
The untrusted access point may contact the 3GPP AAA server via SWa to authenticate the UE. Secondly, the data path is realized via SWu as an encrypted IPsec tunnel terminating in the ePDG.
Source: TS 23.402