## Slide 1
3GPP TSG-RAN WG4 Meeting#70bis R4-141442
San Jose del Cabo, Mexico, 31 March - 4 April 2014
Agenda item: 7.31.1
Source: KDDI
Document for: Approval
Title: Way Forward on UE REFSENS for CA_1A-28A

## Slide 2: Background
CA_1A-28A is classified as Class A2.
3rd harmonic of Band 28 UL falls into Band 1 DL. Therefore, requirements for MSD (maximum sensitivity degradation) are needed.
This contribution summarizes proposals in RAN4#70-bis and try to make way forward to conclude this WI on time.

## Slide 3: Summary
Company Name | Channel Bandwidth |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz
Qualcomm, KDDI [R4-141189] | -90 | -89.5 | -89 | -88.5
NTT docomo *1 [R4-141811] | -96 | -95.5 | TBD | TBD
Ericsson *2 [R4-141987] | -88.5 | -88.2 | -87.9 | -87.7
Broadcom *3 [R4-142112] | -88 | -87.5 | -87.2 | -87
NOTE1: Values are obtained from difference between co-existence requirements to be applied. NOTE2: Assuming UE architecture without implementing harmonics filter. NOTE3: Proposed values in R4-142112 are preferable but values in R4-141189 could be also acceptable by proponent. |  |  |  | 

## Slide 4: UE Reference Architecture
In R4-141987, architecture without harmonic filter is proposed.
  Study with harmonic filter would be done in RAN4#71.
In R4-141811, it is proposed that harmonic filter is placed between duplexer and PA.
  This might be able to avoid Rx penalty (0.5 dB).
Observation: Agreement on UE Reference Architecture is necessary.

## Slide 5: Way Forward
Further study for specifying MSD is necessary. Related parties are encouraged to input contributions in RAN4#71.
Specifically, analogous study in R4-141987 would be done with harmonic filter and provided in RAN4#71.