## Slide 1: WF on CCIM UE Behavior during C-DRX OnDuration
LG Electronics
3GPP TSG-RAN WG4 Meeting #78
St. Julian’s, Malta, 15 – 19 February, 2016
Agenda Item: 6.4.1
R4-161214

## Slide 2: Background
RAN4 agreed that
  Baseline receiver for control channel is MRC receiver.
  Candidate receivers structure for control channel IM (CCIM) as follows:
    LMMSE-IRC + CRS-IC
    ELMMSE-IRC
    ELMMSE-IRC + CRS-IC
RAN4 will define performance requirement for CCIM receiver in Connected mode.
It is difficult to define performance requirement for CCIM receiver in C-DRX mode.
  Need to clarify CCIM UE behavior during OnDuration.

## Slide 3: In C-DRX Mode
Candidate CCIM receivers are required more computational complexity/power consumption comparing with baseline MRC receiver.
By using CCIM receiver during OnDuration, UE power consumption would be increased against original purpose of DRX which is UE power saving.
Proposal
  When UE which has CCIM capability switches over C-DRX mode for power saving,
    CCIM receiver could be allowed fallback to MRC receiver as its behavior during OnDuration.