## Slide 1: Way forward on UE RF requirements scalability for flexible channel BW consideration
Agenda Item: 10.1.1.2
Document for: Approval
Source: MediaTek Inc.
3GPP TSG-RAN WG4 #82 Meeting R4-1702091
Athens, Greece, 13th – 17th February, 2017

## Slide 2: Background (1)
Flexible channel bandwidth operation for NR has been proposed in RAN4 Spokane NR ad hoc meeting where a WF was drawn for further studies [1].
Many aspects in supporting flexible channel were discussed in this meeting [2-6].
One of the key aspects in supporting flexible channel bandwidth is how to define UE RF specifications over a wide range of carrier bandwidth in resolution of a single PRB.

## Slide 3: Background (2)
Though UE RF specifications scalability over channel bandwidth has been discussed in [6], a WF was suggested for further studies to address the following questions and concerns.
  Can UE RF specifications be parameterized over channel bandwidth? If not, how specifications would be written?
  Is defining a finite set of channel bandwidth for UE RF specifications sufficient for performance and functional test coverage?
    From RF performance perspective
    From RRM perspective

## Slide 4: Way Forward
To study if UE RF requirements can be parameterized over channel bandwidth, specifically, for those requirements not channel bandwidth independent nor linearly scalable with channel bandwidth, such as MPR and A-MPR.
To study if defining a finite set of channel bandwidth (including asymmetrical CH BWs for UL & DL) for UE RF specifications is sufficient for performance and functional test coverage?
  For example, if X MHz and Y MHz (two adjacent test points) were defined for test specifications, can passing X MHz and Y MHz requirements guarantee that any BW between X MHz and Y MHz would also fulfill the performance and functional requirements?
  Study the possibility that some UE RF specifications for an arbitrary channel bandwidth not in the finite set can be derived from those for channel bandwidth in the finite set in any necessary way of combination?
This way forward focuses on UE RF requirements only. The study results may later be considered to apply for BS RF requirements.

## Slide 5: References
[1] R4-1700301 Way Forward on flexible channel bandwidth consideration for NR, MediaTek Inc., TSG-RAN WG4 NR AH Meeting, Spokane, Washington, USA, Jan. 17th – 19th , 2017
[2] R4-1700774 Considerations on downlink common channels for flexible channel bandwidth, ZTE Microelectronics Tech. Co., 3GPP TSG-RAN WG4 #82 Meeting, Athens, Greece, Feb. 13th – 17th, 2017
[3] R4-1700785 Flexible channel bandwidth and UE maximum bandwidth, Nokia, Alcatel-Lucent Shanghai Bell, 3GPP TSG-RAN WG4 #82 Meeting, Athens, Greece, Feb. 13th – 17th, 2017
[4] R4-1700865 Consideration on flexible channel bandwidth for NR, ZTE Corporation, 3GPP TSG-RAN WG4 #82 Meeting, Athens, Greece, Feb. 13th – 17th, 2017
[5] R4-1701810 More on flexible channel bandwidth consideration in NR, MediaTek Inc., 3GPP TSG-RAN WG4 #82 Meeting, Athens, Greece, Feb. 13th – 17th, 2017
[6] R4-1710824 UE RF specifications scalability over channel bandwidth, MediaTek Inc., 3GPP TSG-RAN WG4 #82 Meeting, Athens, Greece, Feb. 13th – 17th, 2017