## Slide 1
3GPP TSG-RAN WG4 #82-bis R4-1702827 Spokane, US, 3 - 7 April, 2017
Agenda item: 7.18.1 - General [LTE_feMTC-Core]
Document for: Approval
Band 5 operation in Japan for FeMTC UE
KDDI Corporation

## Slide 2: Proposal
Proposal: For FeMTC Band 5 UE, requirements for Band 5 operation in Japan should also apply.

## Slide 3: How to introduce our proposal
    NOTE39 in Table 6.6.3.2-1 should be modified for FeMTC Band 5 UE.
E-UTRA Band | Protected Band | Frequency Range (MHz) |  |  | Level (dBm) | MBW (dBm) | NOTE
5 | E-UTRA Band 1, 2, 3, 4, 5, 7, 8, 10, 12, 13, 14, 17, 23, 24, 25, 28, 29, 30, 31, 34, 38, 40, 42, 43, 45, 65, 66 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 26 | 859 | - | 869 | -27 | 1 | 
 | E-UTRA Band 41 | FDL_low | - | FDL_high | -50 | 1 | 2
 | E-UTRA Band 18, 19 | FDL_low | - | FDL_high | -40 | 1 | 39
 | Frequency range | 1884.5 | - | 1915.7 | -41 | 0.3 | 8, 39
 | Frequency range | FDL_low | - | FDL_high | -50 | 1 | 39
NOTE39: Applicable only when the assigned E-UTRA carrier is confined within 824 MHz and 845 MHz for UE category M1, NB1, M2 and NB2. |  |  |  |  |  |  | 

## Slide 4: Technical Justification (1/2)
E-UTRA Band | Protected Band | Frequency Range (MHz) |  |  | Level (dBm) | MBW (dBm) | NOTE
5 | E-UTRA Band 18, 19 | FDL_low | - | FDL_high | -40 | 1 | 39
    The above requirement is only for Japan.  Limited frequency range of Band 5 UL (824 – 845 MHz) shall satisfy the requirement.
849
894
815
824
860
869
Band 5
Band 18
830
MHz
Band 19
845
860
890
Protected Band
Aggressor range

## Slide 5: Technical Justification (2/2)
E-UTRA Band | Protected Band | Frequency Range (MHz) |  |  | Level (dBm) | MBW (dBm) | NOTE
5 | E-UTRA Band 18, 19 | FDL_low | - | FDL_high | -40 | 1 | 39
    In the past, RAN4 studied co-existence between B19 UL and B18/B19 DL by assuming Band 5 duplexer.
    The conclusion was specified as NS_08. B19 UL assuming B5 duplexer can satisfy the above requirement up to NRB ≤ 44.
    Therefore, B5 cat.M2 UE can also meet the above requirement because allowed maximum NRB for FeMTC is 25RBs (less than 44).

## Slide 6: Summary
849
894
815
824
860
869
Band 5
Band 18
830
MHz
Band 19
845
860
890
Japanese requirement applies in this range
As indicated in previous slides, B5 Cat.M2 UE can protect B18/B19 DL below -40dBm/MHz up to NRB = 44
Aggressor range of B5 UL

## Slide 7: Conclusion
Proposal: For FeMTC Band 5 UE (cat.M2), requirements for Band 5 operation in Japan should also apply.
How to introduce this proposal is shown below as an example.
E-UTRA Band | Protected Band | Frequency Range (MHz) |  |  | Level (dBm) | MBW (dBm) | NOTE
5 | E-UTRA Band 1, 2, 3, 4, 5, 7, 8, 10, 12, 13, 14, 17, 23, 24, 25, 28, 29, 30, 31, 34, 38, 40, 42, 43, 45, 65, 66 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 26 | 859 | - | 869 | -27 | 1 | 
 | E-UTRA Band 41 | FDL_low | - | FDL_high | -50 | 1 | 2
 | E-UTRA Band 18, 19 | FDL_low | - | FDL_high | -40 | 1 | 38
 | Frequency range | 1884.5 | - | 1915.7 | -41 | 0.3 | 8, 38
 | Frequency range | FDL_low | - | FDL_high | -50 | 1 | 38
NOTE38: Applicable only when the assigned E-UTRA carrier is confined within 824 MHz and 845 MHz for UE category M1, NB1, M2 and NB2. |  |  |  |  |  |  |