## Slide 1: WF on UL enhancement
CMCC, Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #82bis Spokane, US, 3th - 7th April 2017
Agenda Item: 7.12.3
R4-1704200

## Slide 2: Background
In the RAN4#82 meeting, following open issues were identified:
UL 256QAM
  MCS: MCS26 or MCS 27
  UE TX EVM: 0 or 3.5%
PUSCH in UpPTS
  Test methodology
    Option 1: only special subframe is scheduled in the test
    Option 2: both special subframe and normal UL subframes are scheduled in the test

## Slide 3: Agreements
UL 256QAM
  MCS: MCS26
  UE TX EVM: 0
    FFS if additional margin or test tolerance is needed to account for residual EVM in the test.
PUSCH in UpPTS
  Test methodology
    only special subframe is scheduled in the test

## Slide 4: Updated simulation assumption for UL 256QAM
Parameters | Value
Maximum number of HARQ transmissions | 4
RV sequence | 0, 2, 3, 1, 0, 2, 3, 1
Uplink-downlink allocation for TDD | Configuration 1 (2:2)
Tx number | 1
Rx number | 2, 4, 8
CP type | Normal
Propagation conditions and antenna correlation | EPA 5Hz Low
PRB allocation | Full PRB
MCS | MCS26
System Bandwidth | 1.4MHz, 3MHz, 5MHz, 10MHz, 15MHz, 20MHz
UE TX EVM | 0
Channel estimation | Realistic
Performance metric | SNR at 70% Maximum throuput

## Slide 5: Updated simulation assumptions for PUSCH in UpPTS
Parameters | Values
TDD UL/DL configuration | 1
Special subframe configuration | 10
RV sequence | 0, 2, 3, 1, 0, 2, 3, 1
TTI bundling | Disabled
CP length | Normal
Number of data symbols | 5
DMRS | In symbol#3 in UpPTS
Number of TX antennas | 1
Number of RX antennas | 2, 4, 8
Antenna correlation | Low
System BW | 1.4MHz, 3MHz, 5MHz, 10MHz, 15MHz, 20MHz
PRB allocation | Full BW
MCS | MCS20 (16QAM) MCS 26(256QAM)
Propagation conditions | EPA5
Performance metric | SNR at 70% Maximum throuput
Table 2 Simulation assumptions for PUSCH in UpPTS

## Slide 6: Way Forward
UL 256QAM
  Companies are encouraged to provide practical results with impairments and implementation margins
PUSCH in UpPTS
  Companies are encouraged to provide ideal results for alignment and practical results with impairments and implementation margins