## Slide 1: WF on Demodulation Performance for V2X UE
3GPP TSG-RAN WG4 Meeting #82BIS Spokane, USA, 3 - 7 April 2017
Agenda Item: 7.16.5
R4-1704272
LG Electronics, Huawei, HiSilicon, CATT

## Slide 2: Background
In last RAN Plenary, V2X WI core part was completed.
Based on core specification, demodulation performance for V2X WI is started.
Work plan (R4-166984) to finish performance part on time (~ September, 2017)
  RAN4 # 82BIS
    Identify list of demodulation test cases and discuss simulation assumptions
  RAN4 # 83
    Collect simulation and impairment results of identified demodulation test cases
    Provide Draft CR TS36.101 for V2X demodulation Requirements
  RAN4 # 84
    Approve CRs on V2X demodulation test cases
    Complete demodulation performance requirement
Companies are encouraged to provide simulation results for identified test case for V2X UE

## Slide 3: PSBCH test
Background
  SLSS/PSBCH were introduced in RAN1 V2X WI phase, and SLSS/PSBCH transmission and reception is up to UE capability
Test purpose
  Verify PSBCH demodulation performance
Test propagation condition
  EVA180
Introduce new test case for PSBCH performance requirement

## Slide 4: PSSCH decoding processing test
Background
  Maximum number of bits per TTI
    The maximum number of sidelink transport block bits received within a TTI is set to 31704.
    The maximum number of bits of a single sidelink transport block is 31704.
  The total SL soft buffer size is 737280.
Test purpose
  Verify SL soft buffer management and the maximum number of bits per TTI supported by the UE
Introduce new test case for PSSCH decoding capability requirement

## Slide 5: PSCCH decoding processing test
Background
  For UE decoding capability
    UE is not expected to attempt to decode more than X PSCCHs in a subframe. UE is able to decode up to X PSCCH in a subframe.
    UE is expected to attempt to decode at least Y RBs per subframe counting both PSCCH and PSSCH decoding RBs.
    Two types of UE capability are defined
      One with (X=10, Y=100), the other with (X=20, Y=136)
Test purpose
  Verify PSCCH decoding capability both X=10 and X=20 according to UE capability
    Type 1 : X=10, Y=100
    Type 2 : X=20, Y=136
Test configuration for Type 2 UE
  do not consider PSSCH overlapping test configuration
  Option1: Only focus to verify X (PSCCH decoding processing capability)
  Option2: Verify Both X and Y
  For Type 2, baseline is Option1. Companies can bring additional test purposes.
Introduce new test cases for PSCCH decoding capabilities (X=10 and X=20) requirements

## Slide 6: eNB synchronization source based test
Background
  eNB synchronization source were introduced for V2X UE
Test purpose
  Verify UE demodulation for PSCCH/PSSCH performance base on eNB synchronization source
Definition for performance requirement
  Option 1: do not define test case.
  Option 2: define test case with [x] Ts TO and [y] Hz FO
    Option 2-1: Reuse GNSS based performance requirements (only introduce test case)
    Define 2-2: define new performance requirements
  FFS resource pool configuration by eNB
Need to investigate PSCCH/PSSCH performance based on eNB synchronization source

## Slide 7: WAN SDR test activated V2X communication
Background
  V2X UE can transmit and receive packets by Uu and PC5 simultaneously
Test purpose
  Check impact performance for WAN and V2X
Definition for performance requirement
  Option 1: do not define test case
    V2X UE has separate soft buffer size for V2X, and priority between WAN and V2X is signaled by PPPP
  Option 2: define test case
    Option 2-1: define new test configuration
    Option 2-2: reuse legacy WAN SDR test + V2X PSSCH decoding processing test
    (V2X UE will be tested by two test simultaneously, and pass each existing requirement)
    Need further analysis and test methodology