## Slide 1: WF on indoor positioning core requirement maintenance
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting #82bis R4-170xxxx
Spokane, US, April 3 - 7, 2017
Agenda Item: 7.23.1

## Slide 2: Proposal:
  RAN4 will specify the following requirements for indoor positioning:
  Shared PCI using PRS-ID
  Align terminology with RAN2 by introducing TP and PRS-only beacon concepts
  Sharing PCI using muting:
  Scaling the measurement time in order to keep the same number of PRS occasions per cell above side condition
  CRS+PRS
  Clarify the requirement when CRS plus PRS is used
  Additional PRS configuration
  Intra RSTD requirement:
  When T_PRS<MGRP, the PRS occasion will overlap with gap. Thus some of the PRS will not be available
    Scale the measurement period when T_PRS<MGRP if gap is configured
  Inter RSTD requirement:
  Since UE could only measure PRS every MGRP, when T_PRS<MGRP, the measurement period shall base on MGRP, rather than PRS occasion period
  When number of consecutive PRS subframes per PRS occasion is bigger than MGRP, UE can measure PRS multiple times during a PRS occasion.
    Scale the measurement period since UE can measure PRS multiple times during a PRS occasion