## Slide 1: Summary of discussions for Release Independent Spec 36.307
Ericsson, Nokia, MCC, LGE
3GPP TSG-RAN WG4 Meeting #82bis R4-1704316 Spokane, USA, 3rd-7th April, 2017
Agenda Item: 4.2.6
Document Type: Discussion

## Slide 2: 36.307 scope
The specification of 36.307 has been extended to not only CA bands for CA class but also general features e.g. 4Rx to be release independent.

## Slide 3: Background
The following features with requirements defined in RAN4 in 36.101 are considered to be release independent that are specified or supposed to be specified in the release independent spec 36.307.
  CA in general, different power class UEs for different bands, Cat NB1 UEs, Cat 0 UEs, Cat M1 UEs, V2V, V2X, 4Rx, HST, LAA
But the current spec of 36.307 doesn’t have a consistent procedure when making these features release independent

## Slide 4: Example of definition
Normally, a feature is introduced only in the latest open release Rel-N of 36.101/36.133 and future releases are based on the previous one so that future releases inherit the requirements of this feature. Introducing a feature "in a release independent way from Rel-M onwards" (M<N) means it was decided that this feature would be also beneficial in previous, already frozen releases starting with Rel-M until Rel-(N-1). In order to avoid touching core specifications of these frozen releases, the corresponding requirements are captured in TS 36.307.

## Slide 5: Existing issue
Duplication of features in both 36.101 and 36.307 in the same release so such replica should be removed from 36.307
  LAA
  V2X
  Some CA class

## Slide 6: Suggestions of categories of features
Additional E-UTRA operating bands
  Single carrier band
Additional E-UTRA CA configurations
  CA config for different CA class
Additional operating bands for specific features
  Additional band and/or CA bands??
  Cat NB1, UE Cat 0, Cat 1
General band dependent RF requirements
  4Rx RF new REFSENS
General band agnostic baseband requirements
  4Rx baseband requirements, HST

## Slide 7: Goals to be achieved for 36.307
Clear definition of each feature/category of features
Clear procedure of how to make each category of features to be release independent
  Annex of 36.307 to include the table of requirements of each feature to from the same release of 36.101
  Mapping table of which release the feature will be release independent from and link to the Annex table
No redundant duplica requirements in the same release of 36.101 and 36.307.
Clear info provided which release which feature was introduced with clear WI code to keep tracking
Spec text consistent among all releases of the same spec

## Slide 8: Features to be release independent
Examples of features to be release independent info table except CA
Feature | Release independent from | Feature category
4Rx RF | 10 | 4
4Rx baseband | 10 | 5
HST | 13 | 5
Operating bands for UE category 0 | 12 | 3
Operating bands for UE category M1 | 13 | 3
Operating bands for UE catebory NB1 | 13 | 3
Operating bands for LAA | 13 | 3
Operating bands for V2X | 14 | 3
Operating bands for V2V | 14 | 3