## Slide 1: WF on Maximum Channel Bandwidth
Qualcomm Incorporated
3GPP TSG-RAN WG4#82 Bis
Spokane, USA, April 3rd-4th, 2017
R4-1704397
Agenda : 10.3.1
Document for: Approval

## Slide 2: Support of New Channel Bandwidths
Addition of new maximum channel bandwidths in a backwards compatible way should be allowed in a future release
  The gNB may configure a new CHBW that is not supported by legacy UEs
  Handling of a the gNB configured CHBW with CA by the UE that does not support the configured CHBW needs to be supported in the specifications for forward compatibility
    RAN1 already agreed this [R1-1706615]
  gNBs will have to handle UEs that support the gNB configured CHBW with CA such that legacy UEs can still use entire aggregated bandwidth UMBW
CHBW 400MHz
CHBW 400MHz
UMBW 800MHz
400MHz
400MHz
UMBW 800MHz
400MHz
400MHz
CHBW 800MHz
Rel.15
Future Release
Addition of
800MHz CHBW
gNB
UE

## Slide 3: Agreements
Addition of new maximum channel bandwidths is allowed in future releases
  NR design should ensure forward compatibility, send LS to RAN1/2 to inform about this agreement
UE is allowed to operate within a maximum gNB configured CHBW that it does not support using CA combinations
  For example, with 400MHz UE can support 2x200MHz or 4x100MHz even if the gNB has configured 400MHz channel bandwidth
    UE can process the “CCs” independently from a baseband point of view
    Each CC bandwidth is from the set of channel bandwidths defined for that band
    Which combinations are allowed is FFS
  Assumption is that there is no guardband between CCs
    To be checked and confirmed by RAN4
The set of channel All defined channel bandwidths should be supportable by at least one type of UE and will be defined in the UE and BS specs
The set of channel bandwidths will be band and SCS specific
The set of RF bandwidths supportable by BS can be larger than the set of channel bandwidths

## Slide 4: Maximum channel bandwidth (CHBW) in Rel. 15
For bands below 6GHz
  100MHz maximum CHBW
For bands above 24GHz
  400MHz maximum CHBW
Whether different maximum channel bandwidths are defined for different SCS is FFS
Not all UEs need to support the maximum channel bandwidth but there must be at least one type of UE that can support it.