## Slide 1: Africa Band Key points about 3300-3400MHz band
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting 84Bis
Dubrovnik , Croatia, 09th – 13th October, 2017
R4-1711410
Agenda Item: 8.12.1
Document for: Approval

## Slide 2: Background
At the 3GPP TSG RAN Meeting #76 in West Palm Beach, USA June 5 - 8, 2017, a new WI about the study of the TDD in the C-band (3300-3400 MHz) has been approved.
To evaluate the need to take into account directly in the standard the current regulation, in this contribution, several regulatory information are provided.
In the followed slides, several key points, e.g. Power, sensitivity … are proposed for approval

## Slide 3: Need to take into account in the standard the regulation?
ATU response to the 3GPP LS (R4-1709188)
The Doc R4-1710124, ATU response to 3GPP RAN4:
In conclusion, ATU is of the view that it is not necessary to introduce further requirements in the 3GPP specification of the new band to protect incumbent radar services.
Also, the contribution R4-1708452 (Huawei, Hisilicon) as study the need (or not) to take into account some specific regulations in the 3GPP standard.
The conclusion is that the 3GPP standard does not need to take into account any specific regulation to protect incumbent users.

## Slide 4: Proposals for approval 1/3
Proposal 1: Numbering band => B52
Proposal 2: E-UTRA channel numbers =>
  59140 to 60139
  Frequency start: 3300MHz
Proposal 3: Not take into account any specific technical continuation to protect incumbent users (co-channel & adjacent channel) in the 3GPP standard,
  UE => No A-MPR
  BS => No additional filter
E-UTRA Operating Band | Downlink |  |  | Uplink |  | 
 | FDL_low [MHz] | NOffs-DL | Range of NDL | FUL_low [MHz] | NOffs-UL | Range of NUL
52 | 3300 | 59140 | 59140–60139 | 3300 | 59140 | 59140–60139
Table X-2: EARFCN allocated for E-UTRA Band 52
E‑UTRA Operating Band | Uplink (UL) operating band BS receive UE transmit |  |  | Downlink (DL) operating band BS transmit UE receive |  |  | Duplex Mode
 | FUL_low – FUL_high |  |  | FDL_low – FDL_high |  |  | 
52 | 3300 MHz | – | 3400 MHz | 3300 MHz | – | 3400 MHz | TDD
Table X-1 E-UTRA frequency bands

## Slide 5: Proposals for approval 2/3
Proposal 4: UE reference sensitivity power level
  Same as B42
  The reference sensitivity is specified in Table 8.6-1 for Band 52 for general case:
  For specific case, UE(s) equipped with 4 antenna ports, the following additional requirements described in the table 8.6-2 is applied:
Proposal 5: BS & UE power emission
  Same as B42
Channel bandwidth |  |  |  |  |  |  | 
E-UTRA Band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex Mode
52 |  |  | -99 | -96 | -94.2 | -93 | TDD
Reference sensitivity QPSK PREFSENS
Channel bandwidth |  |  |  |  |  |  | 
E-UTRA Band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex Mode
52 |  |  | -101.2 | -98.2 | -96.4 | -95.2 | TDD
Reference sensitivity QPSK PREFSENS

## Slide 6: Proposals for approval 3/3
Proposal 6: Spurious emissions and UE coexistence
  Same as B42
Proposal 7: CA Between :
  B52 & B42
  B52 & B43
  B52 & B42 & B43
Proposal 8: Provide all relevant draft CRs for the next 3GPP RAN4 meeting