## Slide 1: WF on UE RF remaining issues in range 1 and 2
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 #84bis Meeting
Dubrovnik, Croatia, 9th - 13th October 2017
R4-1711574

## Slide 2: Background
UE RF remaining issues in range 1 and 2 are being in below papers.
  R4-1711075: Range 1
    Issue 1: A-MPR values
    Issue 2: Power control
    Issue 3: UE-to-UE protection level at mmWave bands
    Issue 4: Maximum input level
    Issue 5: Rx intermodulation
    Issue 6: Rx spurious emissions
    Issue 7: Receiver image
  R4-1711076: Range 2
    Issue 1: Frequency error
    Issue 2: TX General spurious emissions
    Issue 3: UE-to-UE protection level at mmWave bands
    Issue 4: Tx intermodulation, Narrow-band blocking, Rx intermodulation
    Issue 5: Beam correspondence
    Issue 6: Rx spurious emissions
    Issue 7: Receiver image

## Slide 3: WF on range 1 [1/2]
Issue 1: A-MPR values
  For LTE refarming bands, A-MPR needs to studied band-by-band
Issue 2: Power control
  Absolute, Relative, Aggregated power controls are needed. How to specify them will be decided in the next meeting
Issue 3: UE-to-UE protection level at mmWave bands
  Huawei (R4-1701334) observed -25, -22, and -18 dBm/MHz based on deterministic UE-UE analysis for 28, 40 and 60 GHz respectively
  Confirm if these values are appropriate from system point of view in the next meeting. If not, an alternative value shall be determined in RAN4#85
  Sending an LS of the testability aspect could be considered to RAN5
Issue 4: Maximum input level
  Adopt below table for NR single-carrier. FFS if -20 dBm should be maintained for NR intra-band contiguous CA
Rx Parameter | Units | Channel bandwidth |  |  |  |  |  |  |  |  | 
 |  | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 100 MHz
Power in Transmission Bandwidth Configuration | dBm | -252 |  |  |  | -242 | -222 | -212 | -202 |  | 
 |  | -273 |  |  |  | -263 | -243 | -233 | -223 |  | 
NOTE 1: The transmitter shall be set to 4dB below PCMAX_L at the minimum uplink configuration specified in Table xx with PCMAX_L as defined in subclause xx NOTE 2: Reference measurement channel is FFS for 64QAM NOTE 3: Reference measurement channel is FFS for 256QAM |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: WF on range 1 [2/2]
Issue 5: Rx intermodulation
  Adopt below at least for LTE refarming bands, n77 and n78.
  FFS for n79 (wider interference could be considered)
Issue 6: Rx spurious emissions
  Follow the LTE requirement (already agreed in the chairman minute)
Issue 7: Receiver image (in-channel)
  No need to specify this at least for NR single-carrier. FFS CA cases.
Rx parameter | Units | Channel bandwidth |  |  |  |  |  |  |  |  | 
 |  | 5 | 10 | 15 | 20 | 25 | 40 | 50 | 60 | 80 | 100
 |  | MHz | MHz | MHz | MHz | MHz | MHz | MHz | MHz | MHz | MHz
Pw in Transmission Bandwidth Configuration | dBm | REFSENS + channel bandwidth specific value below |  |  |  |  |  |  |  |  | 
 |  | 6 | 6 | 7 | 9 | [10] | [12] | [13] | [13.8] | [15] | [16]
PInterferer 1 | dBm | -46 |  |  |  |  |  |  |  |  | 
(CW) |  |  |  |  |  |  |  |  |  |  | 
PInterferer 2 | dBm | -46 |  |  |  |  |  |  |  |  | 
(Modulated) |  |  |  |  |  |  |  |  |  |  | 
BWInterferer 2 | MHz | 5 |  |  |  |  |  |  |  |  | 
FInterferer 1 | MHz | –BW/2-[7.5] |  |  |  |  |  |  |  |  | 
(Offset) |  | / |  |  |  |  |  |  |  |  | 
 |  | + BW/2+[7.5] |  |  |  |  |  |  |  |  | 
FInterferer 2 | MHz | 2*FInterferer 1 |  |  |  |  |  |  |  |  | 
(Offset) |  |  |  |  |  |  |  |  |  |  | 
NOTE 1: The transmitter shall be set to 4dB below PCMAX_L,c or PCMAX_L as defined in TBD. |  |  |  |  |  |  |  |  |  |  | 
NOTE 2: Reference measurement channel is TBD. |  |  |  |  |  |  |  |  |  |  | 
NOTE 3: The modulated interferer consists of the Reference measurement channel specified in TBD. |  |  |  |  |  |  |  |  |  |  | 
NOTE 4: The interfering modulated signal is TBD; |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: WF on range 2 [1/2]
Issue 1: Frequency error
  Confirm if +/-0.1 ppm is appropriate or not from system and implementation feasibility point of view for the next meeting. If not, an alternative value shall be determined in RAN4#85.
Issue 2: TX General spurious emissions
  Clarify the lower edge of -13 dBm/MHz and emission requirements below the edge from system and regulatory point of view in the next meeting
Frequency Range | Maximum Level | Measurement bandwidth | NOTE
[9 kHz  f < 150 kHz] | [-36 dBm] | [1 kHz] | 
[150 kHz  f < 30 MHz] | [-36 dBm] | [10 kHz] | 
[30 MHz  f < FFS] | [-36 dBm] | [100 kHz] | 
FFS  f < 2nd harmonic of the upper frequency edge of the UL operating band in GHz | -13 dBm | 1 MHz | 

## Slide 6: WF on range 2 [2/2]
Issue 3: UE-to-UE protection level at mmWave bands
  Huawei (R4-1701334) observed -25, -22, and -18 dBm/MHz based on the deterministic UE-UE co-existence analysis for 28, 40 and 60 GHz respectively
  Confirm if these values are appropriate from system point of view in the next meeting. If not, an alternative value shall be determined in RAN4#85
  The UE feasibility should also be studied to agree the final requirement
Issue 4: Tx intermodulation, Narrow-band blocking, Rx intermodulation
  Not to be introduced in range 2 (already agreed in the chairman minute)
Issue 5: Beam correspondence
  To be discussed in other papers related to EIRP/EIS
Issue 6: Rx spurious emissions
  Clarify if below spurious level for  26 GHz can be applicable and required emission level for > 26 GHz from system and regulatory point of view
  How to treat LO, image leakage shall also be clarified in RAN4#85
Issue 7: Receiver image (in-channel)
  No need to specify this at least for NR single-carrier. FFS CA cases.
Frequency Range | Measurement bandwidth | Maximum Level | NOTE
[30MHz  f < 1GHz] | [100 kHz] | [-57 dBm] | 
[1GHz  f  26 GHz] | [1 MHz] | [-47 dBm] | 
26 GHz  f < 2nd harmonic of the upper frequency edge of the DL operating band in GHz | FFS | FFS |