## Slide 1: WF on sTTI UE remaining open issues
Ericsson, Qualcomm, Huawei
3GPP TSG-RAN WG4 RAN4#84b
Dubrovnik, Croatia, 9th-13th October, 2017
R4-1711595
Document for: Approval

## Slide 2: Background
In last RAN4#84, transient period location was agreed for 2os and an associated WF was agreed to [1].
This WF would capture further agreements on remaining UE open issues for sTTI based on the contributions listed in the Reference slide and offline discussions.

## Slide 3: Agreement: Transient period (1)

## Slide 4: Agreement: Transient period (2)
Case | If condition | Then
1, 1a, 2 | If the symbols across the transient are [R, R] | Then share the transient period symmetrically
 | Else if the symbol on the right of the transient is ‘R’ | Then irrespective of the symbol on the left, place the entire transient period in the right ‘R’
 | Else if the symbol left of the transient is ‘R’ | Then irrespective of the symbol on the right, place the entire transient period in left ‘R’
 | Else | Share transient period symmetrically between the two symbols/TTIs
3 | For all possible data patterns | Place the entire transient period in right/next TTI

## Slide 5: Agreement: Transient period (3)
Case | If condition | Qualcomm
4 | If the last symbol of current TTI is SRS and if the first symbol on the right sTTI is ‘R’ | Place the entire transient period in ‘R’
 | Else if the last symbol of current TTI is SRS and if the first symbol on the right sTTI is ‘D’ | Share the transient period symmetrically between the two symbols/TTIs
 | Else | Place the entire transient period in current TTI
5 | For all data patterns | Treat this case similar to that of legacy 1msec+1msec TTI

## Slide 6: Pcmax and CA - intraband
All links shall only support same sTTI length
They shall have same TAG.

## Slide 7: Pcmax and CA - interband
Pcmax evaluation will be made every Teval_CA, considering Tref_CA period.

## Slide 8: MPR / A-MPR for single carrier
MPR and A-MPR shall be evaluated according to following table
TTI/sTTI pattern |  | MPR/A-MPR evaluation window
7os | MPR and A-MPR is evaluated per sTTI or frequency hopping duration | Min(“Frequency-Hopping-Duration”, 7os)
3os | MPR and A-MPR is evaluated per sTTI or frequency hopping duration | Min(“Frequency-Hopping-Duration”, 3os)
2os | MPR and A-MPR is evaluated per sTTI or frequency hopping duration | Min(“Frequency-Hopping-Duration”, 2os)

## Slide 9: MPR / A-MPR for single carrier
MPR and A-MPR evaluation for CA shall be aligned with Pcmax evaluation for CA.

## Slide 10: References
R4-1708903, WF for dynamic transient period and Teval window for power control, Qualcomm, Ericsson, Huawei
R4-1710220, UE ON/OFF time mask between consecutive 2OS sTTIs, Huawei
R4-1710221, UE ON/OFF time mask between TTI and 2OS sTTI, Huawei
R4-1710222, UE ON/OFF time mask between consecutive 7OS sTTI, Huawei
R4-1710224, Discussion on Pcmax definition for intra-band UL CA, Huawei
R4-1710225, Discussion on Pcmax definition for inter-band UL CA, Huawei
R4-1710622, Transient period and its location for sTTI, Qualcomm
R4-1710624, PCmax computation and evaluation for inter-band CA with sTTI, Qualcomm
R4-1710625, PCmax TREF and Teval window for sTTI, Qualcomm
R4-1710626, Reply LS on implication of sTTI operation on UL ON/OFF time mask, Qualcomm
R4-1710866, MPR/A-MPR for single carrier and CA, Ericsson
R4-1710867, UE transient period, Ericsson