## Slide 1
WF on NR spectrum utilization
ZTE, []
3GPP TSG-RAN WG4 #84bis Meeting
Dubrovnik, Croatia, 9 - 13 October, 2017
Agenda: 9.3.3
Document for: Approval
R4-1711736

## Slide 2: Background: Latest agreement for below 6GHz (R4-1709075)
SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | N.A | N.A | N.A
30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
60 | N.A | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
Above RB values are agreed based on the assumption of symmetric guard band.
The RB values in the table are only meant to indicate the minimum guard band achievable for a given SCS and channel BW . The actual maximum RB allocation can be equal to or 1 RB less than the values shown in the table.
Note1: Above RB values are agreed based on the assumptions of below requirements for sub 6GHz:
BS requirements: output power limit (R4-1706960), ALCR/ACS requirements (R4-1706971),EVM requirements (R4-1706969)
,SEM requirements (R4-1706973);
UE requirements: Power Class (PC3 and PC2), ALCR/ACS requirements (R4-1706525),EVM requirements (R4-1706612),SEM requirements; (R4-1706692)
Companies can further check above RB values based on further agreements for above requirements and agreements for channel raster.
Above RB values are agreed based on the assumption of no edge PRB EVM requirements in Rel-15.
Note2: Above RB values are derived based on RAN4 perspective, which can be further check by other working groups i.e. sub-carrier and RB alignment, and RB allocation restriction for DFT-OFDM waveform

## Slide 3: Background: Latest agreement for mmWave (R4-1709075)
Note 1: Above RB values are agreed based on the assumption of symmetric guard band. If asymmetric guard-band agreed, potential 1 RB reduced may be considered.
The RB values in the table are only meant to indicate the minimum guard band achievable for a given SCS and channel BW. The actual maximum RB allocation can be equal to or 1 RB less than the values shown in the table.
Note1: Above RB values are agreed based on the assumptions of below requirements for mm Wave:
BS requirements: output power limit (R4-1706960), ALCR/ACS requirements (R4-1706954),SEM requirements (R4-1706964);
UE requirements: Power Class definition (R4-1706945), ALCR/ACS requirements (R4-1706063), SEM requirements (R4-1706073);
Companies can further check and bring analysis for above RB values based on further agreements for above requirements and agreements for channel raster, BS EVM and UE EVM requirements.
Above RB values are agreed based on the assumption of no edge PRB EVM requirements in Rel-15.
Note2: Above RB values are derived based on RAN4 perspective, which can be further check by other working groups i.e. sub-carrier and RB alignment, and RB allocation restriction for DFT-OFDM waveform
SCS [kHz] | 50MHz | 100MHz | 200MHz | 400 MHz
 | NRB | NRB | NRB | NRB
60 | 66 | 132 | 264 | N.A
120 | 32 | 66 | 132 | 264

## Slide 4: Open issues
Companies have different understanding on RAN1 nested RB grid alignment agreements
  Issue 1: Which SCS in a channel BW will be the reference SCS for subcarrier and RB alignment to finalize the RB values?
    Option 1: Minimum SCS in a channel BW (fixed value agnostic to actual set of SCS used by NW)
    Option 2: Reference SCS is based on NW scheduling.
      FFS on whether or not UE needs to get information on the reference SCS. If UE needs, FFS on details how UE gets information on the reference SCS.
    Other options not precluded
  Issue 2: RB grid alignment among different SCSs
    Option 1: Start from left channel edge
      Option 1A: Align PRB #0 across different SCSs.
      Option 1B: Do not put constraints on aligning PRB #0 across different SCSs.
    Option 2: Start from channel center and do not put constraints on aligning PRB #0 across different SCSs
    Other options not precluded
  Issue 3: Assuming that some way of arranging PRBs are decided, in which specification will this PRB arrangement be captured, and how it will be captured?
    Assumption: A shift of ½ reference SCS in a channel BW is acceptable for the reference SCS and PRB reduction will not be applied.

## Slide 5: Way forward (1)
Companies are encouraged to bring contributions to the next RAN4 meeting with the following analysis
  The channel BW in this WF means both BS channel BW and UE channel BW.
  RB grid structures with RB allocations for different SCS/CBW
    Analysis could cover cases when reference SCS has N and N-1 PRBs, where N is number of PRBs in R4-1709075
  Estimates of the left/right guard bands for each SCS/CBW using the procedure in the next slide
  The analysis should take into account the following factors affecting guard band asymmetry
    Channel raster
    DC subcarrier
    Subcarrier alignment across different numerologies
    PRB alignment across different numerologies
  Proposals on threshold for guard band reduction (kHz) when PRB reduction should be applied.
  Proposals on open issue 3.
  FFS on whether the RB grid alignment impact on spectrum utilization is the same at the UE and the BS.

## Slide 6: Way forward (2)
Procedure for guard band calculation:
  For reference SCS
    Put all RBs of the reference SCS in the middle of the channel BW.
    According to RAN4 agreements such as channel raster, channel raster mapping to subcarrier, etc., shift the center of all RBs to the required location.
    Calculate the guard band of each SCS and channel BW combination of the reference SCS.
  For non-reference SCSs
    Put all RBs of non-reference SCS in the middle of the channel BW.
    Shift the RBs of non-reference SCS to left/right to ensure that
      Subcarrier 0 is aligned with the subcarrier 0 of the reference SCS
      RB grid alignment among different SCSs is maintained and one RB of a higher order SCS always consists of two RBs of one order lower SCS
      The difference between right/left guard bands is minimized
    Calculate the right and left guard band of each SCS and channel BW combination of the non-reference SCS.