## Slide 1: WF on simulation assumption for NR BS EVM requirement
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting #84bis R4-1711777
Dubrovnik, HR, 9 - 13 October, 2017

## Slide 2: Background (FR1)
The WF [1] approved in RAN4 NR #2 meeting has agreed
Due to DMRS pattern design for DL from RAN1 which may have impact to EVM requirement, WF [2] was approved to evaluate the impact.
Further agreement is needed for EVM requirement evaluation for FR1.

## Slide 3: Background (FR2)
Discussion for how to evaluate the NR EVM for FR2 have been provided in contributions [3][4].
Assumptions in [5] has been approved to perform system simulation for UE EVM evaluation for FR2, and the reference simulation methodology is shown in [6].

## Slide 4: WF for assumptions for FR1
Evaluate BS Tx EVM impacts on DL link performance by considering the following aspects
  Both conducted and OTA EVM requirements should be considered
  DMRS patterns with different density according to the latest RAN1 outcome.
  EVM levels shall be considered together with DMRS density patterns derived from RAN1 outcome.
    The intention is to use EVM levels defined in [1]
  1 and/or 2 layers shall be considered

## Slide 5: WF for assumptions for FR2
Both system and link simulation should be considered
  Investigate approperiate DM-RS patterns and PT-RS patterns needed
  Considering the following modulation scheme for evaluation
    64QAM, 256QAM, 16QAM , QPSK is priority order
    EVM levels shall be compared to EVM = 0%
For system simulation, to evaluate BS Tx EVM by considering the following aspects.
  The simulation assumptions shall include urban macro scenario and indoor hotspot scenario in 38.803
    The assumptions agreed for UE [5] can be used as a reference for urban macro scenario
    How to capture the RF impairments is FFS.

## Slide 6
Reference
  [1] R4-1706969, WF on NR BS EVM, Nokia
  [2] R4-1710022, Way on simulation assumption for EVM, Nokia, Nokia Shanghai Bell
  [3] R4-1711271, Consideration on BS Tx EVM, Huawei, HiSilicon
  [4] R4-1710804, Discussion on EVM requirement for FR2 NR BS, ZTE
  [5] R4-1709666, Simulation assumptions on UE Tx EVM for mmWave, Huawei, HiSilicon
  [6] R4-1710493, Evaluation on UE Tx EVM for mmWave, Huawei, HiSilicon
  [7] R4-1711162, Simulation Results of DM-RS patterns on EVM for FR1, Ericsson