## Slide 1: WF on Clarification of UE Measurement Mode
MediaTek
R4-1803118
Document for: Approval
3GPP TSG-RAN WG4 meeting #86
Athens, Greece, February 26th – March 2nd, 2018
Agenda item: 7.9.3.1

## Slide 2: Background: Decision during Monday evening adhoc
In RAN4 AH1801 meeting, WF R4-1801087 was approved to further study the remaining issues in the following scenarios for UE capable to per-FR-gap:
  Scenario 1: In NSA, for UE capable to per-FR gap without FR2 serving cells but with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap pattern ID within #0 to #11.
    Effective MGRP 20 ms to be adopted for UE to meet the corresponding toward FR2 measurement objects
  Scenario 2: For UE capable to per-FR gap with both FR1 and FR2 serving cells and with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap.
    FFS the UE behavior

## Slide 3: Background: RAN2 agreements in #101 meeting
RAN2 Agreements
  The network configuration from the MN to the UE indicates if the measurement gap from MN applies to LTE/FR1/FR2 serving cell(s) (i.e. per UE gap) or applies to LTE/FR1 serving cell(s) (i.e. per FR gap to LTE/FR1 and no per FR gap for FR2 serving cells).

## Slide 4: Updated proposal for Scenario 1 (Serving cells in LTE/FR1. Measurement objects in both LTE/FR1 and FR2)
If MN indicates UE that the measurement gap from MN applies to LTE/FR1/FR2 serving cell(s),
  FFS the measurement requirements
If MN indicates UE that the measurement gap from MN applies to only LTE/FR1 serving cell(s),
  UE fulfils the per-FR requirements for FR1/LTE measurement objects based on the configured measurement gap pattern.
  UE fulfils the per-FR requirements for FR2 measurement objects based on effective MGRP 20

## Slide 5: Updated proposal for Scenario 2 (Serving cells in both LTE/FR1 and FR2. Measurement objects in both LTE/FR1 and FR2)
In case only MN configures gap and MN indicates UE that the measurement gap from MN applies to LTE/FR1/FR2 serving cell(s),
  From scheduling opportunity and gap applicability perspective, it’s per-UE gap
  FFS the measurement requirement

## Slide 6: Updated proposal for Scenario 2 (Serving cells in both LTE/FR1 and FR2. Measurement objects in both LTE/FR1 and FR2)
In case only MN configures gap and MN indicates UE that the measurement gap from MN applies to LTE/FR1 serving cell(s),
  From scheduling opportunity and gap applicability perspective, it’s per-FR gap for FR1
  From measurement requirement perspective,
    UE fulfils the per-FR requirements for FR1/LTE measurement objects based on the same configured measurement gap pattern.
    UE cannot perform measurement toward measurement objects in FR2
In case only SN configures gap,
  From scheduling opportunity and gap applicability perspective, it’s per-FR gap for FR2
  From measurement requirement perspective,
    UE cannot perform measurement toward measurement objects in FR1
    UE fulfils the per-FR requirements for FR2 measurement objects based on the configured measurement gap pattern.

## Slide 7: Updated proposal for Scenario 2 (Serving cells in both LTE/FR1 and FR2. Measurement objects in both LTE/FR1 and FR2)
In case MN configures gap and MN indicates UE that the measurement gap from MN applies to LTE/FR1/FR2 serving cell(s) and SN configures gap,
  This is invalid case, and UE behavior is unpredictable
In case MN configures gap and MN indicates UE that the measurement gap from MN applies to LTE/FR1 serving cell(s) and SN configures gap,
  From scheduling opportunity and gap applicability perspective, the gap configured by MN is per-FR gap for FR1/LTE, and the gap configured by SN is per-FR gap for FR2
  From measurement requirement perspective,
    UE fulfils the per-FR requirements for FR1/LTE measurement objects based on the measurement gap pattern configured by MN, and
    UE fulfils the per-FR requirements for FR2 measurement objects based on the measurement gap pattern configured by SN.