## Slide 1: WF on WF on RRC Re-establishment and Connection Release with Redirection
Ericsson, Samsung
3GPP TSG-RAN WG4 Meeting # 86
Athens, Greece, Feb. 26-March 02, 2018
R4-1803137

## Slide 2: Agreements on RRC Connection Release with Redirection Requirements in TS 38.133
Proposal 1: The requirements for RRC connection release with Redirection shall be specified for the following scenarios:
  redirection to NR carrier provided this procedure is specified by RAN2,
  redirection to E-UTRA FDD carrier,
  redirection to E-UTRA TDD carrier.
Proposal 2: if this procedure is specified by RAN2 then the requirements for RRC connection release with Redirection to NR carrier shall be specified for the NR target cell’s side conditions comparable to those for performing inter-frequency non-blind handover.
Proposal 3: The requirements for RRC connection release with Redirection to E-UTRA FDD or TDD carrier shall be specified for E-UTRA FDD or TDD target cell’s side condition corresponding to SCH Ês/Iot  -3 dB.
Proposal 4: RAN4 is to investigate cell search delays based on above proposals
Note: The requirements for RRC redirection shall be specified provided corresponding procedure is specified in RAN2 specifications.

## Slide 3: Agreements on RRC Connection Re-establishment Requirements in TS 38.133
Proposal 1: The requirements for RRC connection re-establishment shall be specified for the NR target cell’s side conditions comparable to those for performing NR intra-frequency measurements.
Proposal 2: The time to identify (Tsearch) a target NR cell in the requirements for RRC connection re-establishment consists of time to acquire physical cell ID (PCI) of the target cell i.e. PSS/SSS acquisition time.
Proposal 3: The requirements for RRC connection re-establishment shall be specified for the cases when target NR cell is: known and unknown.
Proposal 4: RAN4 is to investigate cell search delays based on above proposals
Note: The requirements for RRC re-establishment shall be specified provided corresponding procedure is specified in RAN2 specifications.