## Slide 1: Way forward on Propagation Model for Demodulation
Intel, CATR, Spirent, Rohde & Schwarz, Keysight Technoogies
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26 Feb - 02 Mar 2018
R4-1803560

## Slide 2: Background
In RAN4-AH-1801 baseband only test methodology was agreed up on for demodulation performance testing in FR2.
  Proposal 1. Adopt “pure baseband” testing methodology for demodulation performance testing in FR2.
    Assumes max rank 2 with cross polarized transmission
    Rank 2 spatial MIMO would not be included
    As a starting point an isotropic UE antenna pattern is assumed
  Proposal 2. Methodology for RRM testing in FR2 is further discussed during the SI.

## Slide 3: Way Forward
Proposal#1: Define demodulation requirements with TDL channel models
    The detailed TDL definition is FFS
    Channel models defined for FR2 in 38.901 could be a starting point
    How the models can be emulated in the tests is FFS
    Generation of TDLs from CDLs is not precluded
Proposal#2: Further study the modifications necessary to channel models to capture effect of beamforming and antenna pattern
Proposal#3: Further study the modifications necessary to simplify existing TDL channel models
Proposal#4: Define UE performance test cases with TDL-D and TDL-E channel models; these models can be further simplified based on the outcome of studies captured in P2 and P3