## Slide 1: Way forward on Beam management requirements in NR
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 7.10.4.4
R4-1807283

## Slide 2: Way forward on link reconfiguration for BM
RAN4 will introduce the requirements for link reconfiguration, including:
  Beam failure detection
  Candidate beam detection
The requirements on both CSI-RS based beam failure detection and SSB based beam failure detection will be introduced, and the following aspects will be specified:
  BLER value for the threshold Qout_LR , which can be defined as 10%.
  Maximum number of beam failure detection RS resources
  Hypothetic PDCCH parameters for beam failure indication
  L1 evaluation period for beam failure instance evaluation
  L1 indication interval of two successive beam failure instance, which can be defined as the maximum values between the shortest periodicity of BFD-RS resources and 2ms
The requirements on both CSI-RS based candidate beam detection and SSB based candidate beam detection will be introduced, and the following aspects will be specified:
  The evaluation period of L1-RSRP, which will be defined in core requirements.
  The absolute measurement accuracy of L1-RSRP, which will be defined in core requirements.

## Slide 3: Way forward on L1-RSRP reporting for BM
RAN4 will introduce the measurements requirements on L1-RSRP reporting , including CSI-RS based and SSB based.
The following aspects will be specified
  L1-RSRP measurement period
    Single shot measurement is assumed.
  L1-RSRP measurement accuracy
    Both absolute and relative accuracy are included.
RAN4 shall specify the L1-RSRP reporting mapping for beam management.
  FFS whether the same RSRP measurement reporting mapping can be used for SS-RSRP, CSI-RSRP, L1-RSRP.
RAN4 shall specify the differential L1-RSRP reporting mapping for beam management