## Slide 1: WF for RRM requirements for euCA
3GPP TSG-RAN WG4 #87 R4-1807545
Busan, Korea (Republic of), May 21st - May 25th , 2018
Agenda item: 6.26
Nokia, Nokia Shanghai Bell

## Slide 2: Background
During the meeting RAN4 had discussions based on the summary document R4-1807936 Summary of open issues and proposals for euCA.
3 topics were discussed based on the company input:
  Idle mode measurements for fast CA setup.
  Direct SCell activation.
  Dormant SCell state.
Following slides includes agreements and open issues for further discussion.

## Slide 3: Idle mode measurements for fast CA setup
Agreement:
  RAN4 will define UE reporting requirements for euCA based on the following conditions:
    The UE measurement requirements for a carrier configured to be measured for the purpose of early measurement reporting, depends on if the carrier is an overlapping or non-overlapping carrier.
      An overlapping carrier is a carrier configured for early measurement reporting and inter-frequency mobility measurements.
      A non-overlapping carrier is a carrier for early measurement reporting and not configured for inter-frequency mobility measurements.
  Basic assumptions:
    A detected cell in connected mode prior to connection release is assumed to remain in detected state when UE has entered Idle mode, provided that the following conditions are met:
      The UE is provided with a list of cells and/or carrier frequencies for early measurement reporting by
        Dedicated RRC signaling
        FFS SIB5
      The detected cell is among the list of cells and/or on the carrier frequencies provided for early measurement reporting
      The UE is provided with T331 by dedicated RRC signaling, or optionally regardless of the presence of T331 up to UE implementation
      A detected cell remains detectable until UE reconnects to the network and sends the early measurement reporting
    Conditions for a detected cell applies for serving cells and known cells in connected mode.
    Idle mode measurement requirements apply for carriers configured for mobility.

## Slide 4: Idle mode measurements for fast CA setup
Agreement:
  UE measurement requirements for non-overlapping carrier:
    If serving cell quality is higher than thresholds (Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ)
      UE is not required to perform periodic measurements on detected cells
      Prior to early reporting UE perform a single measurement
    If serving cell quality is lower than thresholds (Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ)
      Same as above for (Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ)
  UE measurement requirements for overlapping carrier:
    If serving cell quality is higher than thresholds (Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ)
      UE is not required to perform periodic measurements on detected cells
      Prior to early reporting UE perform a single measurement
    If serving cell quality is lower than thresholds (Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ)
      Existing UE idle mode measurement requirements apply.

## Slide 5: Idle mode measurements for fast CA setup
Aspects for further discussions:
  Minimum number of cells and inter-frequency layers to measure:
    UE can be configured with up to 3 carriers.
    As agreed in RAN4#86bis, UE measurement capability is not affected by euCA.
    Number of cells follows existing idle mode measurement requirements.
  Detected cell condition for early measurement reporting
    Whether to include or not the presence of the previous valid measurement report during connected mode
  Measurement time limitation for SIB5 based configuration:
    No limit
    RAN4 defined limit (x seconds, T331 or other)
  Measurement accuracy:
    Will be discussed during the performance part.
  Detected cells in connected:
    T331 and SIB5

## Slide 6: Direct Scell activation
Agreements:
  Reference point n after RRC reconfiguration message is received
    Reference point ‘n’ is the end of the last TTI containing the RRC configuration when UE is configured with direct activated SCell..
  Activation delay for unknown cell is 10ms longer than that of known cell
    Direct Scell activation delay for unknown cell is 10ms longer than that of known cell.

## Slide 7: Direct Scell activation
Agreement
  It is more challenging for a UE to meet a given SCell activation delay timeline when directly activating more number of SCells.
  Not all UEs will be able to directly activate the same number of SCells within a given SCell activation delay timeline
  RAN4 will define a maximum number of SCells, X>=1, that can be directly activated by one RRC message.
    For a UE capable of supporting maximum of Y SCells, only up to min(X, Y) number of SCells can be directly activated by one RRC message

## Slide 8: Direct Scell activation
Issues for further discussion:
  Activation delay for known cell
    Proposal 1 and proposal 2 are open (R4-1807936).
    Companies are encouraged to analyse further for next meeting:
      RAN2 procedures.
  Interrupts requirements at direct SCell Activation
  Direct SCell configuration during HO.
  maximum number of SCCs that can be directly activated at once (RAN2 impact)

## Slide 9: Dormant SCell
Agreements:
  Scell activation delay and interruption requirement for a dormant Scell is defined under the side condition that MBSFN subframe(s) are not configured.
  Deactivated to Dormant state transition:
    Upon receiving a MAC-CE command in subframe n shall be able to change the SCell from deactivated state to the dormant SCell state no later than in subframe n+24 and n+34 when the SCell is known and unknown respectively.
  CQI Reporting and ‘A dormant Scell follows PCell DRX for CQI/RRM measurement report triggering’
    UE shall report CQI according to the SCell CQI reporting requirements
    The CQI reporting in dormant SCell state following the PCell DRX cycle shall follow the existing rules as defined for CQI reporting in DRX
    CQI accuracy of the dormant Scell is not affected from the fact that the measurement/reporting of the CQI follows the Pcell DRX

## Slide 10: Dormant SCell
Agreement
Config | Interruption Length | Interruption Window | Scell activation delay
FDD | 2ms (intra-band), 1ms (inter-band) | [n+5, n+7] | n+[8] (Already Agreed)
TDD | 5ms (intra-band), 1ms (inter-band) | [n+5, n+10] | n+[11]
Note 1: Requirement in the table is conditioned that MBSFN subframe(s) are not configured in any of the active serving cell(s) and the SCell being activated. |  |  | 
Table 1. Scell Activation Delay/Interruption Window for a Dormant Scell (when a MAC CE with Scell activation command is received at subframe n)

## Slide 11: Dormant SCell
Open items for further discussion:
  UE interruptions for Dormant Scell