## Slide 1: WF on NR V2X RRM requirement scope
LG Electronics, CATT
3GPP TSG-RAN WG4 #92 Meeting
Ljubljana, Slovenia, 26th– 30th Aug., 2019
R4-1909994

## Slide 2
RAN4 discussed following topics for NR V2X RRM
  UE Tx timing
    Synchronization reference source
      GNSS, gNB, eNB, SynRefUE
      Multiple gNB & eNB
      Timing misalignment between GNSS & gNB
  Synchronization
    Selection/Reselection
    Simulation assumption for SL SS
    Initiation/Cease of SL SS transmission
  Measurement
    S-RSRP measurement
    Autonomous Resource Reselection measurement
    Congestion Control measurement
  Interruption
    Interruption to SL due to Uu
    Interruption to Uu due to SL
  SL BWP switching
  Unicast, groupcast related
    SL RLM
    HARQ
Background

## Slide 3
RAN4 agreed the followings
  Synchronization related
    Use band n47 (5.9GHz) as the frequency carrier to define the RRM requirements for NR V2X
      The simulation for other frequency bands will depend on the conclusion of RF session
    For the evaluation of detection time, the maximum relative velocity is assumed to be 260km/h
    For evaluation, 15kHz/30kHz/60kHz will be considered.
      No need to define the requirements for all the SCS-es
  Measurement related
    Derive the S-RSRP accuracy requirements for NR V2X based on one symbol SSSS
Background

## Slide 4
Selection/Reselection to SyncRef UE
  Study detection time of SyncRef UE with followings
    Related simulation assumptions for alignment
      Frequency carrier : 5.9GHz(n47)
      Maximum relative velocity = 260km/h
      SL SCS = 15kHz/30kHz/60kHz
      Frequency offset = 0ppm, 0.1ppm
      Propagation condition = AWGN, TDLC30-1400
        Other Channel is not precluded(down selection will be done in next meeting)
    Companies are welcome to provide simulation assumptions and initial simulation results in next meeting.
  Study dropping rate of SL for selection/reselection
Synchronization(1/2)

## Slide 5
Selection/Reselection to gNB or eNB in EN-DC or NE-DC
  Study potential RRM impact for following sub-bullets from RAN4 perspective
    how to choose gNB or eNB as synchronization reference source when they’re in the same priority, and
    how to choose serving cell as synchronization reference source when multiple active serving cells under the same RAT(NR or LTE) are configured as candidate synchronization reference sources
    how to facilitate the communication between UEs that synchronized to asynchronized synchronization reference sources.
  Depending on RAN4 conclusions, RAN4 will inform other WGs if spec. impact to other WGs is identified
Initiation/cease of SLSS transmission
  When NR serving cell is used as synchronization reference source, evaluation time is [X] times of NR intra-frequency measurement time.
    Study RRM impact due to timing misalignment between GNSS & gNB/eNB
Synchronization(2/2)

## Slide 6
Autonomous Resource Reselection measurement
  Study based on RAN1 decision
Congestion Control measurement
  Study based on RAN1 decision
Measurement

## Slide 7
Interruption to SL due to NR Uu BWP switching
  For case of NR V2X in ITS and concurrently supporting NR Uu
    Define interruption requirements based on what operation is prioritized
  For case of NR V2X in licensed band
    Study interruption requirement based on what operation is prioritized, if the scenario is agreed in RF session
Interruption to Uu due to SL BWP configuration/reconfiguration
  The SCS/BWP change on NR SL on ITS band is not a practical case in R16, and RAN4 will not define any requirement for this impractical SCS/BWP change on NR SL on ITS band in R16.
    RAN4 send LS to inform RAN1
Interruption

## Slide 8
    Study interruption when Uu BWP is different from SL BWP for NR V2X in shared licensed band if the scenario is agreed in RF session
        When NR Uu BWP switching, and NR V2X SL BWP configuration/reconfiguration (if supported) are performed simultaneously
  Study related RRM impact and UE behaviour
Not preclude other possible interruption scenario in next meeting, such as
  SL UE communication initiation and termination.
  SL-Uu inter-band or intra-band cases based on RAN1 and RAN4 RF group agreement
Interruption

## Slide 9
        SL RLM
  Study SL V2X RLM requirements in NR V2X for unicast based on RAN1/2 agreements on RLM metrics.
        HARQ
  Study potential RRM impact based RAN1 decision
Unicast, groupcast