## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson
3GPP TSG-RAN4 Meeting #92
Ljubljana, Slovenia, August 26 - 30, 2019
R4-1910017
Document for: Approval

## Slide 2: Agreements
Type of requirements
  PMI only
Frequency range
  FR1
Number of Tx ports
  Option 1: 16, 32
  Option 2: 16
Codebook type
  Type I single panel codebook
PMI tests:
  Option 1: Cover wideband PMI and subband in different tests, not duplicate all the tests
  Option 2: Only Wideband
Test metric:
  As baseline, Relative throughput ratio between following PMI and random PMI at SNR point corresponding to 90% TP with follow PMI

## Slide 3: Test configuration
CHBW/SCS:
  10MHz/15kHz for FDD
  40MHz/30kHz for TDD
Antenna correlation:
  XP high (as baseline)
Propagation condition:
  TDLA30-5 (as baseline)
Codebook construction:
  16 Tx ports: (N1, N2) = (8, 1) or (4, 2)
  32 Tx ports (if PMI reporting requirement for 32 Tx ports will be defined): (N1, N2) = (4, 4) or (8, 2) or (16, 1)
Number Rx antennas:
  2Rx, 4Rx
Rank:
  Option 1: up to rank 4 for 4Rx, and up to rank 2 for 2Rx
  Option 2: up to rank 2
MCS:
  Up to 64QAM
Interested companies are encouraged to provide simulation results in RAN4#92bis