## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 - 30 August, 2019
Huawei, HiSilicon
Way forward on LTE-NR coexistence for TDD
R4-1910018

## Slide 2: Test Configurations (1/2)
Number of tests
  Option 1: 2 tests
    Test 1: Mapping Type A, Start symbol 3, Duration 9
    Test 2: Mapping Type A, Start symbol 3, Duration 11
  Option 2: 1 test
    Mapping Type A, Start symbol 3, Duration 11
SCS for NR carrier: 15 kHz; FFS 30kHz
Channel bandwidth: 10MHz
TDD UL/DL configuration
  LTE: LTE UL-DL configuration 2, Special subframe configuration 7
  NR with 15kHz SCS
    Option 1: DDDSU with S=10:2:2
    Option 2: DSU+DD
SSB configuration:
  Periodicity 20 ms, allocated in first slot within 20 ms
PDSCH scheduling
  Skipped slots with NR SSB and LTE PBCH/PSS/SSS

## Slide 3: Test Configurations (2/2)
Number of HARQ process: 8
Antenna configuration
  4x2 and 4x4 ULA Low
MCS
  MCS 4 (QPSK, CR 0.30)
Rank
  Rank 1
DMRS configuration
  Type 1, Single symbol, 1 additional DMRS
TRS configuration for NR TDD configuration Option 1
  2 slots, offset 10 ms, periodicity 20 ms
CRS rate matching configuration
  4 antenna ports, v-shift 0
Channel model:
  TDLA30-10

## Slide 4: Test Configuration Summary
Parameter |  | Unit | Value
Duplex mode |  |  | TDD
CHB/SCS |  |  | CBW:10MHz SCS: 15kHz; FFS 30kHz
Channel Model |  |  | TDLA30-10
TDD configuration |  |  | LTE: LTE UL-DL configuration 2, Special subframe configuration 7 NR with 15kHz SCS Option 1: DDDSU with S=10:2:2 Option 2: DSU+DD
SSB configuration |  |  | Periodicity 20 ms, allocated in first slot within 20 ms
TRS configuration for NR TDD configuration Option 1 |  |  | 2 slots, offset 10 ms, periodicity 20 ms
MCS |  |  | MCS 4 (QPSK, CR 0.30)
Antenna configuration and Rank |  |  | 4x2 and 4x4 ULA Low Rank 1
PDSCH configuration | Mapping type |  | Type A
 | Starting symbol (S) |  | 3
 | Length (L) |  | Option 1: 9 and 11; Option 2: 11
 | PDSCH aggregation factor |  | 1
 | PRB bundling size |  | 2
 | PDSCH scheduling |  | Skipped slots with NR SSB and LTE PBCH/PSS/SSS
PDSCH DMRS configuration | DMRS Type |  | Type 1
 | Number of additional DMRS |  | 1
 | Position of the first DM-RS for downlink |  | 3
 | Maximum number of OFDM symbols for DL front loaded DMRS |  | 1
CRS for rate matching (Note 1) | LTE carrier centre subcarrier location |  | Same as NR carrier centre subcarrier location
 | LTE carrier BW | MHz | 10
 | Number of antenna ports |  | 4
 | v-shift |  | 0
Number of HARQ Processes |  |  | 8
Note 1: No MBSFN is configured on LTE carrier |  |  |