## Slide 1: WF on Intra-band non-contiguous ULCA general requirements
Qualcomm, Nokia, Intel, Apple, Huawei, […]
­­­3GPP TSG-RAN WG4 Meeting #92 R4-1910282
Ljubljana, Slovenia, 20th to 26th Aug. 2019

## Slide 2: SEM
The SEM mask is the composite SEM mask of the individual sub-blocks, and
Where two or more masks overlap, the most relaxed limit is used.
Composite spectrum emission mask applies to frequencies up to  ΔfOOB starting from the edges of the sub-blocks
If for some frequency an individual sub-block spectrum emission mask overlaps with the bandwidth of another sub-block, the emission mask does not apply for that frequency.
IQ image(s) and Carrier leakage exception(s) that fall within the cumulative aggregated BW
Whether other exceptions lies within cumulative aggregated BW shall be defined based on the above SEM mask can be further study in the next meeting

## Slide 3: General Spurious Emissions
Apply to each sub-block
The spurious emission limits apply for the frequency ranges that are more than FOOB (MHz) from the edge of the aggregated sub-block bandwidth.
No spurious emission limit applies in the gap where the frequency between the lowest edge of the upper sub-block and the highest edge of the lower sub-block is smaller than ∆FOOB_L + ∆FOOB_H.
IQ image(s) and Carrier leakage exception(s) inside the cumulative aggregated BW are not precluded.

## Slide 4: ACLR
Adjacent Channel Leakage Power Ratio is the ratio of the sum of the filtered mean powers centred on each of the assigned sub-block frequency to the filtered mean power centred on an adjacent sub-block frequency at nominal channel spacing equal to the aggregated bandwidth of the sub-block.
In case the sub-block gap bandwidth Wgap is smaller than either sub-block bandwidth, no NC-CA ACLR requirement is set for the corresponding sub-block for the gap.
Measurement BW is the aggregated sub-block bandwidth minus the sum of the guard bands on both sides of the sub-block.

## Slide 5: IBE, EVM
EVM, IBE requirements for simultaneous intra-band contiguous CA are defined with all CCs active and configured with PRB allocation only applied on the PCC and no PRB allocation applied on other CCs per subclause 6.5.2A [4].
  Whether all CCs can be assumed to be active is FFS for non-simultaneous UL NC CA
PCC with PRB allocation, SCC and other CCs without PRB allocation
Figure 1: EVM, IBE Evaluation for FR2 NC CA

## Slide 6: OBW
OBW is specified per sub-block
OBW is defined as the bandwidth containing 99% of the total integrated power of the transmitted spectrum on the sub-block per subclause 6.6.1A [4].

## Slide 7: MPR
MPR could be a function of allocation ratio, where the spacing of the gap is taken into account by using the cumulative aggregated bandwidth rather than the aggregated bandwidth.
Cumulative aggregated BW includes all active and non active CCs.
Option 1
Other options, but not limited to the ones in [3], are not precluded.

## Slide 8: Reference
R4-1909581 Intra-band non-contiguous ULCA general requirements and MPR consideration for FR2, Qualcomm
R4-1909134 On intra-band UL non-contiguous CA requirement for FR2, Huawei
TR36.833-4 (V12.0.0)
TS36.101 g20