## Slide 1: WF on Emission Requirements for NR-U
Nokia
R4-1910585
3GPP TSG-RAN WG4 #92
August 26th – 30th, 2019
Ljubljana, Slovenia

## Slide 2: Baseline Emission Mask for NR-U
  Based on discussions related to R4-1908717, R4-1908371, R4-1908251, and R4-1909260 together with Chairman guidance there is consensus for the following :
  -> Regional requirements will be addressed by using NS approach
  -> Companies will further discuss the generic requirements as baseline mask
  - Option 1: NR requirements
  - Option 2: Modified ETSI mask
  -> NS specific requirements will be also discussed based on regional regulatory requirements after baseline requirements (mask) is agreed.
  The two points left for discussion are addressed in the following slides.

## Slide 3: Baseline Emission Mask for NR-U (Alternative 1)
  Baseline Emission Mask based on the NR Spectrum Emission Mask (SEM) as given in section 6.5.2.2 of 38.101-1

## Slide 4: Baseline Emission Mask for NR-U (Alternative 2/3)
  Baseline Emission Mask based on:
    Alt. 2 - ETSI EN 301 893 (v2.1.1) mask (Failed LBT sub-bands see slide 7)
    Alt. 3 - IEEE 802.11ac (No requirements for failed LBT sub-bands)
 | a [MHz] | b [MHz] | c [MHz] | d [MHz]
ETSI EN 301 893 (v2.1.1) | 0.5 x N | 0.55 x N | N | 1.5 x N
IEEE 802.11ac | (0.5 x N) - 1 | (0.5 x N) + 1 | N | 1.5 x N

## Slide 5: Baseline Emission Mask for NR-U (Alternative 4)
  Baseline Emission Mask based on:
    Alt. 4 – IEEE 802.11ax

## Slide 6: Baseline Emission Mask for NR-U (Alternative 5)
  Baseline Emission Mask based on:
    Alt. 5 – Modified ETSI mask (with -28 dB floor across failed LBT sub-bands)

## Slide 7: Baseline Emission Mask for NR-U (Alternative 6/7)
  Baseline Emission Mask based on:
    Alt. 6 – Modified ETSI mask with -25 dB floor across failed LBT sub-bands
    Alt. 7 – Modified IEEE 802.11ac/ax with -25 dB floor across failed LBT sub-bands
    For alt. 6 the OOB slope definition dependent on the number of LBT sub-bands from ETSI are reused is reused. In case of a failed LBT sub-bands the 20MHz slope is used.
    For alt. 7 the OOB slope definition dependent only on the total number of LBT sub-bands from IEEE 802.11ac/ax is reused.

## Slide 8: Baseline Emission Mask for NR-U (Alternative 8/9)
  Baseline Emission Mask based on:
    Alt. 8 – Modified ETSI/ IEEE 802.11ac/ax mask with -25 dB floor across failed LBT sub-bands
    Alt. 9 – Modified ETSI/ IEEE 802.11ac/ax mask with -28 dB floor across failed LBT sub-bands
    For alt. 8 and 9, the 1 MHz offset to carrier edge from IEEE 802.11ac/ax is removed and the mask starts at the carrier edge as for the ETSI mask.
    For alt. 8 and 9, the OOB slope definition dependent only on the total number of LBT sub-bands from IEEE 802.11ac/ax is reused. Only in the case of a failed LBT sub-band closest to the edge of the carrier the floor across failed LBT sub-bands is reused until interception with the OOB mask.

## Slide 9: ACLR for PC5 and PC3
  Based on discussions related to R4-1909205, R4-1908717 and R4-1908844 together with Chairman guidance there is consensus for the following :
  -> Companies will further discuss the ACLR requirements for PC3 and PC5.
  -> The range for PC5 ACLR should be [25.5dBc] to [30dBc]
  -> The range for PC3 ACLR should be [x] to [y]