## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, USA, 18th – 22th November 2019
Huawei, HiSilicon
Way forward on RRM requirements of R16 enhancement for NB-IoT
R4-1914889

## Slide 2: Preconfigured UL resource
The requirements for measurement for PUR TA validation is derived based on the need from UE mobility perspective.
The requirements for measurement for PUR TA validation is defined independent of requirements for other measurement.
The requirements for measurement for PUR TA validation defines the time period before PUR transmission within which UE should have a RSRP measurement that fulfils the accuracy requirements.
UE should have an RSRP measurement with the 320ms before the PUR transmission.

## Slide 3: Multi carrier operation non-anchor RRM
RAN4 should make decision on filtering the results from different carriers from the below two options
  Option 1: The US is allowed to translate the non-anchor NRSRP sample results by the corresponding offset.
  Option 2: UE should only filter the samples from the same carrier.
Any filtered results, either from anchor or non-anchor carrier, can trigger neighbor cell measurement and/or relaxed monitoring abortion.
A threshold should be used so that if the two samples of measured RSRP are spaced by a period longer than the threshold the results do not count.