## Slide 1: WF on MR-DC Early measurement reporting
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #93 R4-1915842
Reno, USA, 18-22 Nov 2019

## Slide 2: NR EMR
NR measurements for EMR while serving cell is in NR

## Slide 3: Background
RAN4 has earlier agreed that the UE measurement capability will not change due to EMR
RAN4 has earlier agreed that requirements for EMR will be the same in Inactive mode and Idle mode
RAN4 agreed to adopt support of overlapping and non-overlapping carrier concept.

## Slide 4: Definition of overlapping carrier
Option 1 (LTE definition):
  An overlapping carrier is defined as a carrier configured by higher layer for early measurement reporting and inter-frequency mobility measurements
  A non-overlapping carrier is defined as a carrier configured by higher layer for early measurement reporting while not configured for inter-frequency mobility measurements
Option 2:
  An overlapping carrier is a carrier which the UE is actively measuring for mobility and EMR.
  An non-overlapping carrier is a carrier which the UE is actively measuring for EMR only.
Tentative Agreement: Option 2.

## Slide 5: Working assumption on EMR Carriers
RAN4 EMR requirements for NR carriers while camped on NR only apply if EMR carriers are in CA combination supported by UE
RAN4 EMR requirements for NR carriers while camped on LTE only apply if UE supports EN-DC and NR EMR carriers are in the ENDC band combination supported by UE

## Slide 6: WF on Idle measurements for EMR
Number of carriers to measure for EMR considering the use of overlapping and non-overlapping carriers:
  Option 1: Re-use the LTE euCA requirements for number of carriers to be reported for early measurements (Qualcomm)
    Limit the number of overlapping and number of non-overlapping carriers (i.e. LTE EMR approach)
  Option 2: Specify the total number of carriers (MediaTek)
    Limit the number of overlapping + non-overlapping carriers (i.e. total number of carriers for EMR)
  Option 3: No limit on carriers that can be configured for EMR (as long as it does not exceed UE measurement capability) (Nokia, Huawei)
  Option 4: Limit the number of non-overlapping carriers only (New, option 3 + limit on number of non-overlapping carriers)
FFS: UE behavior when the above limits are exceeded

## Slide 7: WF on Idle measurements for EMR
Measurements for EMR and mobility:
  Possible options:
    S-measure threshold is assumed not applicable to carriers for EMR.
      Overlapping EMR carriers are measured continuously.
      Non-EMR carriers are measured according to s-Measure threshold.
    Hence, beyond s-Measure threshold UE measures both EMR and non-EMR carriers.
    To reduce overall measurement latency:
      EMR carriers are measured when Serving cell RxLev is good
      EMR carriers are not required to be measured or can be down selected when Serving cell RxLev is not good
      Non-EMR carriers obey s-Measure threshold
  RAN4 to discuss whether to apply threshold on serving cell condition for EMR:
    Example:
      EMR carriers will measured when Rxlev>threshold
      EMR carriers are not required to be measured or can be down selected when Rxlev<threshold

## Slide 8: WF on Idle measurements for EMR
Early measurement and cell change, discuss following aspects :
  Possible Agreement: Follow RAN2 agreements which are (for information)
    Dedicated:
      UE performs measurements for EMR using the RRCRelease configured MOs independently from PCell changes while T331 is running.
    SIB Configured:
      UE performs EMR measurements according to serving cell SIB configuration while T331 is running.
    FFS whether the above also applies when the carrier changes from overlapping to non-overlapping or from non-overlapping to overlapping after the cell change
  Discuss if any additional rules are necessary from RAN4 side

## Slide 9: WF on Idle measurements for EMR
Early measurement and cell change, discuss following aspects:
  At cell change, what is the UE behaviour related to reporting of EMR:
    Option 1: leave it to UE implementation
    Option 2: RAN4 defines specific rules
  RAN4 to discuss introduction of the concept of unknown cells considering early measurement reporting
    Option 1: Introduce known/unknown cells for EMR
    Option 2: Do not introduce known/unknown cells for EMR
  Impact on early measurements after T331 stops and before reporting EMR
    FFS if RAN4 specifies applicable requirements for the early measurements performed and used for EMR after the expiry of the T331 timer (at least for overlapping carriers)
    FFS if the UE shall be capable of reporting the results of the early measurements at least up to T0 after the expiry of T331

## Slide 10: WF on Idle measurements for EMR
On detected cell and cell detection:
  The existing requirements under ca-IdleModeMeasurements as baseline,
  FFS whether to defines requirements for the detected cell status for the idle mode CA measurement when UE transitions from RRC Connected mode to Idle mode and after UE has entered Idle mode in 36.133 section 4.9.2.1
Possible options:
  Option 1: Apply the same principles for NR inter-frequency cells.
  Option 2: Do not apply the same principles for NR inter-frequency cells.

## Slide 11: LTE NR Inter-RAT EMR
NR inter-RAT measurement for EMR while camped in LTE

## Slide 12: LTE NR Inter-RAT EMR
Different UE capabilities:
  Option 1: UE supporting ca-IdleModeMeasurements also support measurement of NR inter-RAT for early reporting.
  Option2: UE not supporting ca-IdleModeMeasurements support measurement of NR inter-RAT for early reporting.
  Other options are not precluded
  For all options: it is assumed that the UE under discussion is a UE capable of EN-DC, while a UE capable of existing ca-IdleModeMeasurements might not support EN-DC.
Possible options: proceed the work in RAN4 defining requirements for all cases.

## Slide 13: LTE NR Inter-RAT EMR
Number of carriers:
  Possible options:
    For a UE supporting EMR of NR inter-RAT carriers in addition to ca-IdleModeMeasurements existing number of LTE carriers as defined under ca-IdleModeMeasurements are kept unchanged
      For a UE supporting EMR of NR inter-RAT carriers in addition to ca-IdleModeMeasurements shall support NR inter-RAT measurements on a number of NR carriers in addition to existing inter-frequency carriers as defined under ca-IdleModeMeasurements.
    For a UE supporting EMR of NR inter-RAT carriers in addition to ca-IdleModeMeasurements the UE support a number of EMR carriers which may be LTE or NR (total number of euCA EMR carriers remain unchanged)
    For a UE supporting EMR of NR inter-RAT carriers but not supporting ca-IdleModeMeasurements shall support measurements on a number of NR carriers.
    Other options are not precluded
  Number of NR inter-RAT carriers:
    FFS

## Slide 14: LTE NR Inter-RAT EMR
Detected cell state:
  The existing requirements under ca-IdleModeMeasurements as baseline,
  FFS whether to define requirements for the detected cell status for the idle mode CA measurement when UE transitions from RRC Connected mode to Idle mode and after UE has entered Idle mode in 36.133 section 4.9.2.1
Possible options:
  Option 1: Apply the same principles for NR inter-RAT cells.
  Option 2: Do not apply the same principles for NR inter-RAT cells.