## Slide 1: Way forward on BWP switching on multiple CCs
Intel Corporation
3GPP TSG-RAN WG4 #93 Meeting R4-1915933
Reno, Nevada, USA, 18th - 22th Nov, 2019

## Slide 2: Background
In RAN4#92bis (R4-1912837) 2 cases for BWP switching on multiple CCs were agreed
Case 1: Simultaneous triggering of BWP switching on multiple CCs
Time
BWP switching on CC1
Trigger BWP switching
Time
Trigger BWP switching
BWP switching on CC2
Figure 1: An example of triggering BP switching on multiple CCs at the same time.
Time
BWP switching on CC1
Trigger BWP switching on CC1
Time
Trigger BWP switching on CC2
BWP switching on CC2
Figure 2: An example of BWP switching on multiple CCs with partially overlapping time.
Case 2: Non-simultaneous triggering of BWP switching on multiple CCs

## Slide 3: Definition of Simultaneous triggering
Definition of Simultaneous triggering of BWP switching on multiple CCs
For DCI based switching:
  The timing difference among the first symbol of slot carrying DCI for all CCs is received within the MRTD for inter-band CA
For Timer based switching
  The timing difference among the beginning of the slot where timer based BWP switching starts for all CCs is within MRTD inter-band CA
For RRC based switching
  RRC based BWP switching on multiple CCs for NR-CA is triggered by 1 RRC command
    FFS for NR-DC operation

## Slide 4: Requirements for simultaneous triggering
Requirements are defined for BWP switching on all CCs triggered by the same method (DCI, Timer or RRC)
  RRC based BWP switching on multiple CCs for NR-CA is triggered by 1 RRC command
    FFS for NR-DC operation
For BWP switching delay requirements companies are encouraged to bring analysis on BWP switching delay components that can be done in parallel and sequentially
  Option 1: BWP switching on multiple CCs would be N times delay of single CC
    Where 1 < N < Number of CCs
      FFS if BWP switching delay requirements are scaled for subset of CCs or for all CCs.
  Option 2: BWP switching delay 1 CC + ; Where D is the incremental processing delay on additional CCs; N is number of CCs; K is number of CCs that can be processed simultaneously
  Other options are not precluded
Interruption requirements are FFS

## Slide 5: Requirements for partial overlap triggering
For BWP switching on multiple CCs with partial overlap:
  Requirements are defined for BWP switching on all CCs triggered by the same method (Timer or RRC)
  DCI based switching is not considered for CA; FFS for NR-DC
  RRC based switching shall be considered for NR-DC only
  Timer based switching shall be considered for CA and NR-DC
FFS on BWP switching delay with partial overlap triggering
FFS on interruption requirements for BWP switching with partial overlap triggering

## Slide 6: Non-simultaneous BWP related descriptions in TS 38.213 (for information)
12 Bandwidth part operation
  A UE does not expect to detect a DCI format 1_1 indicating an active DL BWP change or a DCI format 0_1 indicating an active UL BWP change for a scheduled cell within FR1 (or FR2) in a slot other than the first slot of a set of slots for the DL SCS of the scheduling cell that overlaps with a time duration where the UE is not required to receive or transmit for an active BWP change in a different cell from the scheduled cell within FR1 (or FR2).
  When a UE's BWP inactivity timer for a cell within FR1 (or FR2) expires within a time duration where the UE is not required to receive or transmit for an active UL/DL BWP change in the cell or in a different cell within FR1 (or FR2), the UE delays the active UL/DL BWP change triggered by the BWP inactivity timer expiration until a subframe for FR1 or half a subframe for FR2 that is immediately after the UE completes the active UL/DL BWP change in the cell or in the different cell within FR1 (or FR2).