## Slide 1: WF on RRM measurement relaxation for Power Saving
CATT
3GPP TSG-RAN WG4 Meeting #93 R4-1915946
Reno, USA, 18 - 22 Nov 2019

## Slide 2: WF on RRM measurement relaxation
For information: Scenarios
  #1: Low mobility scenario
  #2: Not in cell-edge scenario
  #3: Low-mobility + Not in cell-edge scenario
RRM measurement relaxation methods for UE power saving in RRC_idle/inactive state
  Option 1: Allow RRM measurements with longer intervals
  Option 2: UE is not required to meet the intra-frequency and inter-frequency neighbor cell measurement requirements

## Slide 3: WF on RRM measurement relaxation
Applicability of RRM relaxation methods when the relaxation criteria are fulfilled
Selection of option 1 or option 2 will depend on the details of the criteria as developed by RAN2.
Encourage companies to bring the analysis on how to relax measurement interval if option 1 is proposed in next meeting
Encourage companies to bring the analysis for option 2 if option 2 is proposed in next meeting
 | Applicable RRM relaxation methods
Scenarios #1 | FFS: Option 1 and/or 2
Scenarios #2 | FFS: Option 1 and/or 2
Scenarios #3 | Option 2

## Slide 4: WF on RRM measurement relaxation
  RRM measurement relaxation by reducing the number of frequency layer to be measured is FFS
  The impact on early measurement reporting due to power saving mode:
    Option 1: UE is not allowed to relax or enter any relaxed measurement modes (e.g. based on scenarios defined in slide 2) if UE is configured with early measurement reporting (EMR) and T331 timer is running.
    Other options is not precluded
  RAN4 to study the RRM impact, e.g. timeline of DCI based BWP switch, due to cross-slot scheduling power saving technique if there is any impact to the DCI processing delay based on RAN1 agreements.