## Slide 1: WF on Tx Full power transmission test cases
vivo, Intel, OPPO, Samsung
3GPP TSG-RAN WG4#93 Meeting R4-1916007
Reno, USA, 18th – 22nd Nov, 2019

## Slide 2: Background(1)
Testing scenarios and configurations in original contributions:
  Note: [4] was not included due to the generality of final proposal.
 | 1 port, rank1 | 2 ports, rank1
Mode 1 |  | Vivo, Samsung: TPMI 2 Qualcomm: TPMI 0,1,2 Intel: Yes for TPMI2 if rank2 not supported; No if rank2 supported and verified..
Mode 2 | Samsung, Qualcomm | (full power TPMIs) Vivo, Samsung, Qualcomm, Intel
 |  | (Non full power TPMIs) Qualcomm
None “The other mode” |  | Vivo (TPMI: FFS)

## Slide 3: Background(2)
Agreement from Chairman’s minutes:
  In REl-16 eMIMO, only full power transmission will be tested
    This means the power scaling scheme which would cause non-full Tx power needs not be verified.
Some other issues and proposals other than verification point:
  How to meet other Tx requirements when testing full power transmission
  Only add maximum output power requirements. I.e. no other test cases such as emission tests. [4]
  Enable test equipment to perform measurements on multiple antenna.[3]
  Power class applicability, i.e. whether UL full power transmission could be extended to other power classes other than PC3.[3]
  …

## Slide 4: Way Forward (1)
Test configurations introduced based on supported mode
  Current assumption is UE can only support one mode. This could also be updated based on RAN1 progress
 | 1 port, rank1 | 2 ports, rank1
Mode 1 | - | TPMI2 (Note 1)
Mode 2 | FFS [(Note 4)] | Full power TPMI(s) UE reported (Note 2)
None “The other mode” | - | TPMI: [One random selected] (Note 3)
Note 1: No need to be tested if Rel-15 UL-MIMO rank2 is supported and verified. Note 2: Random selection of one TPMI is considered to limit the test case number. Note 3: All the full power TPMI(s), typically one should be tested. [Note 4: This only applies to Mode 2 thus cannot be used for other modes. In addition, if Rel-15 introduced similar case, this tentative point would be totally unnecessary.] |  | 

## Slide 5: Way Forward (2)
At least introduce MOP requirements for Full Tx Power feature in Rel-16 eMIMO.
Study whether other cases, such as emission requirements should be verified or not.

## Slide 6: Reference
[1] R4-1913319, Discussion on Uplink full power transmission, Samsung, RAN4#93
[2] R4-1914227, Further analysis of RF requirements for eMIMO UL Full Power, vivo, RAN4#93
[3] R4-1913801, TX full power capability, Qualcomm Incorporated, RAN4#93
[4] R4-1915355, Consideration on eMIMO full power, Huawei, RAN4#93
[5] R4-1913472, On Full tx power measurement, Intel , RAN4#93
[6] Chairman’s notes, RAN4#93