## Slide 1: WF on IAB DC/CA Requirements
AT&T, Ericsson, Qualcomm, Nokia
3GPP TSG-RAN WG4 Meeting #93 Reno, USA, Nov 18th – 22nd, 2019
R4-1916149

## Slide 2: Scenario 1: DC for IAB nodes
As noted in the 38.300 running CR for IAB [2], different architecture options are supported for IAB, where the IAB-MT can connect to the network in a NSA (i.e. EN-DC) or SA mode:
  The IAB-node can access the network using either SA-mode or EN-DC. In EN-DC, the IAB-node also connects via E-UTRA to a MeNB, and the IAB-donor terminates X2-C as SgNB.
In addition, redundant backhaul routes are supported in Rel-16 based on the existing NR DC framework:
  4.x.4.3 Topological redundancy
  The IAB-node may have redundant routes with the IAB-donor CU.
  For IAB-nodes operating in SA-mode, NR DC is used to enable route redundancy in the BH by allowing the IAB- MT to have concurrent BH RLC channels with two parent nodes. The parent nodes have to be connected to the same IAB-donor CU-CP, which controls the establishment and release of redundant routes via these two parent nodes. The parent nodes together with the IAB-donor CU obtain the roles of the IAB-MT’s MN and SN. The NR DC framework (e.g. MCG/SCG-related procedures) is used to configure the dual radio links with the parent nodes (TS 37.340 [zz]).
  Observation 1: IAB-nodes which utilize EN-DC and NR DC should be supported from a RAN4 specification perspective

## Slide 3: Scenario 2: CA for IAB nodes
Due to the larger processing capabilities and dedicated power supplies, it is expected that IAB nodes will be capable of both intra-band combinations and inter-band combinations for the IAB-MTs to fully realize the backhaul link capacity, independently of what is supported for the access UEs which may be limited to a single component carrier due to processing or power saving considerations.
  Observation 2: Intra-frequency/inter-frequency CA for IAB nodes should be supported from a RAN4 specification perspective

## Slide 4: Way Forward
One straightforward approach is to take the existing specifications for regular UEs as the starting point. Specifically adopting sections 5.2A, 5.3A, 5.4A, and 5.5A of 38.101-2 (in case of FR2 standalone operation) as the starting point for equivalent sections in the corresponding RAN4 specification for IAB nodes.
Of course RAN4 can further discuss and decide whether only a subset of the existing CA configurations (e.g. based on Tables 5.2A.1-1 5.3A.4-1) and should be supported for IAB-MTs and can be based on specific requests from operators based on prioritized deployment scenarios.
Proposal: RAN4 investigate how the specify the intra-band CA support for IAB MTs in IAB TS with below options:
1. Refer to 38.101-2
2. Self-contained in IAB TS spec
Details of supported intra-band CA combinations can be further discussed based on operator requests.
FFS: Introduction of other scenarios (e.g. EN-DC, inter-band CA)

## Slide 5: Appendix – 38.101-2 5.2A
NR CA Band | NR Band (Table 5.2-1)
CA_n257B | n257
CA_n257C | n257
CA_n257D | n257
CA_n257E | n257
CA_n257F | n257
CA_n257G | n257
CA_n257H | n257
CA_n257I | n257
CA_n257J | n257
CA_n257K | n257
CA_n257L | n257
CA_n257M | n257
CA_n260B | n260
CA_n260C | n260
CA_n260D | n260
CA_n260E | n260
CA_n260F | n260
CA_n260G | n260
CA_n260H | n260
CA_n260I | n260
CA_n260J | n260
CA_n260K | n260
CA_n260L | n260
CA_n260M | n260
CA_n260O | n260
CA_n260P | n260
CA_n260Q | n260
CA_n261B | n261
CA_n261C | n261
CA_n261D | n261
CA_n261E | n261
CA_n261F | n261
CA_n261G | n261
CA_n261H | n261
CA_n261I | n261
CA_n261J | n261
CA_n261K | n261
CA_n261L | n261
CA_n261M | n261
CA_n261O | n261
CA_n261P | n261
CA_n261Q | n261
Table 5.2A.1-1: Intra-band contiguous CA operating bands in FR2

## Slide 6: Appendix – 38.101-2 5.3A
NR CA bandwidth class | Aggregated channel bandwidth | Number of contiguous CC | Fallback group
A | BWChannel ≤ 400 MHz | 1 | 1,2,3,4
B | 400 MHz < BWChannel_CA ≤ 800 MHz | 2 | 1
C | 800 MHz < BWChannel_CA ≤ 1200 MHz | 3 | 
D | 200 MHz < BWChannel_CA ≤ 400 MHz | 2 | 2
E | 400 MHz < BWChannel_CA ≤ 600 MHz | 3 | 
F | 600 MHz < BWChannel_CA ≤ 800 MHz | 4 | 
G | 100 MHz < BWChannel_CA ≤ 200 MHz | 2 | 3
H | 200 MHz < BWChannel_CA ≤ 300 MHz | 3 | 
I | 300 MHz < BWChannel_CA ≤ 400 MHz | 4 | 
J | 400 MHz < BWChannel_CA ≤ 500 MHz | 5 | 
K | 500 MHz < BWChannel_CA ≤ 600 MHz | 6 | 
L | 600 MHz < BWChannel_CA ≤ 700 MHz | 7 | 
M | 700 MHz < BWChannel_CA ≤ 800 MHz | 8 | 
O | 100 MHz ≤ BWChannel_CA ≤ 200 MHz | 2 | 4
P | 150 MHz ≤ BWChannel_CA ≤ 300 MHz | 3 | 
Q | 200 MHz ≤ BWChannel_CA ≤ 400 MHz | 4 | 
NOTE 1: Maximum supported component carrier bandwidths for fallback groups 1, 2, 3 and 4 are 400 MHz, 200 MHz, 100 MHz and 100 MHz respectively. NOTE 2: It is mandatory for a UE to be able to fallback to lower order CA bandwidth class configuration within a fallback group. It is not mandatory for a UE to be able to fallback to lower order CA bandwidth class configuration that belong to a different fallback group. |  |  | 
Table 5.3A.4-1: CA bandwidth classes