## Slide 1: Way Forward on PC1.5 MPR
T-Mobile USA
3GPP TSG-RAN WG4 #98bis-e
April 12th ‒ 20th, 2021
Electronic Meeting
R4-210xxxx

## Slide 2: Current PC1.5 MPR situation
MPR was defined in the PC1.5 for n41 WI
Several companies provided measurement data. Some of the data showed PC2 MPR to be sufficient for PC1.5.
After the MPR negotiations, relatively generous MPR was agreed in order to complete ethe work in the Release 16 timeframe.
The agreed to PC1.5 MPR is 3 dB higher than the PC2 MPR for outer and edge allocations, and 1.5 dB higher for inner allocations.
If a UE takes the maximum allowed MPR there is only 1.5 dB of benefit for PC1.5 compared to PC2 for inner allocations, and no benefit for outer and edge allocations. (The goal of PC1.5 was not to get 1.5 dB of benefit for inner allocations.  )

## Slide 3: MPR improvement from the operator’s perspective
Coverage is determined by the uplink, so reduced MPR = more UL power = better coverage
For FWA, there are not the same constraints on the form factor, so better antenna isolation and PCB isolation is possible and practical.
Even though MPR is a maximum and UEs can always use less, vendors often just use the RAN4 defined MPR

## Slide 4: PC 1.5 MPR for Smartphones
Re-analyze measurement data from the n41 PC1.5 WID to see if improvements could be made without new measurements
Companies welcome to bring in new measurements

## Slide 5: MPR for FWA
FWA MPR can use different assumptions than smartphone MPR
Measurement campaign for FWA
Assumptions:
  20 dB antenna isolation
  PCB isolation effect neglected
  Post-PA front-end loss assumed to be 4 dB per Tx Chain