## Slide 1: WF on RF exposure mitigation approaches for PC 1.5
Samsung
R4-21xxxxx
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, Apr 12th – 20th 2021
Agenda: 7.37

## Slide 2
In [1], it is agreed to reuse existing mechanism for PC1.5 to meet the regional SAR limit for n77 and n78 handheld device
  Currently, the default duty cycle limit is 25% for PC1.5 if nothing is reported
  Otherwise, it is half the reported value since the same IE is used for PC2 reporting as well
In RAN4#98-e, it is proposed that MPE should be used as the evaluation criterion for FWA devices rather than SAR
  A FWA device is significantly different from a handheld UE that is held next to the user’s head
  It is agreed to carry out the study on the quantitative impact to see if a different mechanism can be applied to FWA from handheld UEs based on existing devices or compliance reports
Background

## Slide 3
For smartphone SAR, following issues were discussed in RAN4#98-bis-e
  Whether the same method identified for Band n41 can also be used for Band n77, n78, and n79
  If FWA uses a different method, how should this be indicated to the network?
  If a different method is used between smartphone and FWA, does the network need to know whether the device is smartphone or FWA?
Based on the discussion, it has been agreed that
  Same method as identified for Band n41 is also used for Band n77, n78, and n79
  Whether separate signaling is needed for FWA is FFS, depending on the outcome of FWA MPE discussion
Way Forward: Smartphone SAR

## Slide 4
In RAN4#98-bis-e, following approaches were proposed for FWA MPE handling. Both are still on the table without consensus
    Proposal 1: Duty cycle reporting is not used. Instead, focus on G_tx assumption
      If actual G_tx is larger than assumed G_tx, then P-MPR is applied
    Proposal 2: Duty cycle approach is used with possible longer evaluation period
Companies are encouraged to provide a detailed (or merged) method given the existing and proposed options below
    P-MPR: Baseline method. UE centric solution with other optional solutions
    Duty cycle: Optional method. e.g., same with smartphone (25%), or other limit (e.g. 50%)
    Antenna gain (G_tx): Optional method. e.g., G_tx assumption with/without duty cycle
    Other options are not precluded
RAN4 will further discuss how to define the optional solutions and its signaling for FWA devices in RAN4#99-e
Way Forward: FWA MPE

## Slide 5
[1] | RP-202912 | New WID on high-power devices operation use cases over Band n77 and n78 | 
[2] | R4-2104975 | MPR for PC 1.5 NR UE on n77/n78 or n79 | LGE
[3] | R4-2105035 | MPE handling for high power FWA devices | Samsung
[4] | R4-2107264 | On the RF exposure limit for FWA PC1.5 | Huawei
References