## Slide 1: WF on introduction of lower 6GHz NR unlicensed operation for Europe
RAN4
Nokia, …

## Slide 2: General - Band plan
Unlicensed operation in the range 5945-6425 MHz can be introduced by (Agreed in R4-2103229):
  Option 1: Re-using already defined band n96
    FFS if additional notes and/or clarifications are needed. Regional specific requirements to be included in relevant specifications.
  Option 2: Defining a new band n[xx]
    On top of specific requirements provided by ECC, the new band shall reuse requirements already defined for n96, where possible.

## Slide 3: General - Note for n96
Currently the note in 38.101-1 reads: NOTE 14: This band is applicable in the USA only subject to FCC Report and Order [FCC 20-51]
  Option 1: Modify the note according to R4-2106273:
    This band is applicable in the USA subject to FCC Report and Order FCC 20-51 and in Europe subject to CEPT ECC Decision (20)01 for the 5945 to 6425 MHz frequency range.
  Option 2: Modify the note to generic text:
    This band is only applicable subject to regional and/or country specific restrictions.
  Option 3: Other proposal:
    ...

## Slide 4: General - LPI and VLP deployment
Inclusion of VLP deployment to 3GPP specification:
  Option 1: VLP deployment is subject to further checking of regulations
  Option 2: VLP deployment can be included in specification given the available regulations

## Slide 5: UE RF - NS definition
NS shall be defined corresponding to LPI deployments and if introduced also VLP deployments (Agreed in R4-2103229).
Reusing existing PC5 with additional NS limitations to TX power is sufficient to limit MOP for VLP.

## Slide 6: UE RF - A-MPR values
A-MPR for PC5 LPI:
A-MPR for VPL is FFS
Pre-coding | Modulation | RB Allocation | 
 |  | Full2 (dB) | Partial3 (dB)
DFT-s-ODFM | Pi/2 BPSK4 | ≤ [1.5] | ≤ [2.5]
 | QPSK | ≤ [2.0] | ≤ [4.0]
 | 16 QAM | ≤ [2.5] | ≤ [4.0]
 | 64 QAM | ≤ [3.5] | ≤ [4.5]
 | 256 QAM | ≤ [5.0] | ≤ [5.5]
CP-OFDM | QPSK | ≤ [3.5] | ≤ [5.0]
 | 16 QAM | ≤ [4.0] | ≤ [5.0]
 | 64 QAM | ≤ [5.5] | ≤ [5.5]
 | 256 QAM | ≤ [7.0] | ≤ [7.0]
NOTE 1: The A-MPR shall apply to all SCS in all active 20 MHz sub-bands contiguously allocated in the channel. The MPR applies to interlaced allocations with uplink resource allocation type 2 as specified in TS 38.214 [10]. NOTE 2: Full RB allocation A-MPR applies when all RB’s in a 20 MHz channel or all RB’s in all sub-bands for wideband operation are fully allocated and sub-bands are transmitted according to configuration A in Table 6.2F.2-2. NOTE 3: Partial RB allocation A-MPR applies when one or more RB’s in one or more sub-bands are not allocated or when the transmitted sub-bands for wideband operation are transmitted according to configuration B in Table 6.2F.2-2. NOTE 4: Applicable to Pi/2-BPSK modulation when IE powerBoostPi2BPSK is set to 0. NOTE 5: The A-MPR applies instead of MPR for 20 MHz channel centered at the nearest NR-ARFCN corresponding to 5955 MHz, 40 MHz channel at the nearest NR-ARFCN corresponding to 5965 MHz, 60 MHz channel at the nearest NR-ARFCN corresponding to 5975 MHz, and 80 MHz channel at the nearest NR-ARFCN corresponding to 5985 MHz. For all other channels, A-MPR is zero and MPR as specified in Table 6.2F.2-1 applies. |  |  | 

## Slide 7: BS RF -
There is no further need for clarifications for BS maximum output power, as compared to those given for n96 in 38.104.
There is no further need for additional REFSENS, as compared to those given for n96 in 38.104.
FFS if ΔfOBUE/ ΔfOOBB should follow n46 or n96