## Slide 1: WF on RF architecture options handling for PC2 intra-band UL NC CA
Huawei, HiSilicon, []
R4-210XXXX
3GPP TSG-RAN WG4 #98bis-e
April 12 – 20, 2021
Electronic meeting

## Slide 2: Background: MPR evaluation assumption for different architectures
RF architectures under discussion and MPR assumptions for intra-band UL NC CA are summarized as below:
PC2 non-contiguous UL CA architecture options and MPR assumption |  | 
Arch | description | MPR evaluation assumption
#1 | 2x26dBm PA + 2LO with 100MHz BW | PA calibration for 20MHz QPSK DFT-s-OFDM 100RB0 waveform based on 4dB post PA losses and 1dB MPR: 26dBm/antenna: 29dBm at 31dB ACLR 23dBm/antenna: 26dBm at 30dB ACLR Equal PSD and Equal back-off power split For 2PA architecture, 10dB antenna isolation is assumed For 2PA architecture, Emission requirements are checked by summing the power of the two transmit paths Waveform: both CP-OFDM and DFT-s-OFDM can be evaluated CBW configuration: 20MHz channel 15kHz SCS and 40MHz channel 15kHz SCS with a gap of 20MHz (100MHz class and in gap ACLR) 40MHz channel 15kHz SCS and 40MHz channel 15kHz SCS with a gap of 120MHz (200MHz class) 100MHz channel 30kHz SCS and 100MHz channel 30kHz SCS with a gap of 400MHz (600MHz class for n77(2A)) RB allocation: Worst case back-off IMD3 at -13dBm/MHz and -30dBm/MHz for 1RB+1RB at 15kHz and 30kHz SCS for MPR with 31dBc ACLR The RB locations adopt for MPR evaluation in [2][8] can be referenced.
#2 | 1x26dBm PA + 1LO with 200MHz BW | 
#3 | 2x23dBm PA + 1LO with 200MHz BW | 
#4 | 1x23dBm+1x26dBm + 2LO with 100MHz BW | 

## Slide 3: PC2 intra-band UL NC CA architecture options handling
Agreements reached in Webinar session:
Companies to provide more MPR values to decide on the net power gain of PC2 in comparison with PC3
If some architecture is beneficial in supporting UL MIMO, the same or different set of requirements can be considered
To further check if in-gap exceptions (for both PC3 and PC2) required by some architectures are allowed by regulations

## Slide 4
PC2 intra-band UL NC CA architecture options handling
Issue 1: PA swap time for 1x23dBm+1x26dBm + 2LO with 100MHz BW
  Proposals
    Option 1: define new swap time specifically for this architecture
    Option 2: swap time is 0us
    Option 3: 0us or 35us or 140us
Issue 2: For 1x26dBm PA + 1LO with 200MHz BW and 2x23dBm PA + 1LO with 200MHz BW, how to handle in-gap requirement when LO or image fall inside?
  Proposals
    Option 1: Reuse in-gap exception under some conditions(e.g. Sync) as defined for PC3
    Option 2: use MPR to meet in-gap emission requirement
    Option 3: other
Agreement:
  Based on architecture #4, companies are encouraged to provide analysis on PA swap time UE can reach, and the impact of the swap time is evaluated on the remaining benefit versus PC3 for the different proposed swap time for PC2 intra-band UL NC CA.
  Based on architecture #2 and #3, RAN4 to further check on in-gap requirements.

## Slide 5: RF requirements other than MPR
Following agreements are reached:
For PC2 intra-band UL non-contiguous CA with 2PA architecture, the emission requirement is defined as the sum from both UE transmit antenna connectors.
Capability of MaxUplinkDutyCycle: Reuse the capability for single carrier case.

## Slide 6
Reference
[1] R4-2104437, “Potential issues on UL Intra band NC CA with 1PA/1LO assumption”, Nokia, RAN4 #98bis-e
[2] R4-2104819, “Discussion on Transmitter Architecture for PC2 UL NC CA”, Skyworks, RAN4 #98bis-e
[3] R4-2106366, “On PC2 intra-band non-contiguous NR CA”, ZTE, RAN4 #98bis-e
[4] R4-2106542, “Discussion on HP UE for TDD intra-band UL CA”, Xiaomi, RAN4 #98bis-e
[5] R4-2107261, “HPUE intra-band non-contiguous CA architecture”, Huawei, HiSilicon, RAN4 #98bis-e
[6] R4-2107282, “Discussion on possible reference architecture for nc ul ca”, Qualcomm, RAN4 #98bis-e
[7] R4-2105088, “Power capability and back-off for NC (and contigous) intra-band CA”, Ericsson, RAN4 #98bis-e
[8] R4-2010301, “[FR1ULCA] UE TX measurements and requirements for non-contiguous ULCA MPR and A-MPR”, Skyworks, RAN4 #96-e