## Slide 1: Way forward on MPR and AMPR PC2 for intra-band UL contiguous CA
Skyworks Solutions Inc., …
R4-210xxxx
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic meeting, 12 – 20 Apr. 2021

## Slide 2: Background: April 15 GTW agreements
For BW class B contiguous allocation MPR
Inner allocation: Take the average value
Outer allocation: Take the average value (TBD for edge allocation)
For BW class C contiguous allocation MPR
  Inner allocation: Take PC3 values ([7] for 256QAM)
  Outer allocation: Take PC3 values ([7] for 256QAM)

## Slide 3: WF: PC2 BW class B contiguous allocation MPR
Modulation |  | MPR for bandwidth class B(dB) | 
 |  | inner | outer1
DFT-s-OFDM | Pi/2 BPSK | 2.0 | 4.01
 | QPSK | 2.0 | 4.01
 | 16QAM | 2.5 | 4.01
 | 64QAM | 3.0 | 4.51
 | 256QAM | 5.5 | 6.0
CP-OFDM | QPSK | 2.5 | 5.01
 | 16QAM | 3.0 | 5.01
 | 64QAM | 3.5 | 5.01
 | 256QAM | 6.5 | 6.5
Note 1: When 1 RB or 2 RB are allocated at the lower edge of lowest CC or upper edge of upper CC, MPR for outer is 5.5dB |  |  | 
Management of Edge allocation failing because of WOLA and lower guard band for class B CA:
Since it is a very corner case when there is only allocation in one CC this can be handled with the following note:
Note 1: When 1RB or 2RB are allocated at the lower edge of lowest CC or upper edge of upper CC, MPR for outer is 5.5dB
WF: Table on the left is adopted for the specification

## Slide 4: WF: PC2 BW class C contiguous allocation MPR
Modulation |  | MPR for bandwidth class C (dB) | 
 |  | inner | outer
DFT-s-OFDM | Pi/2 BPSK | 2.5 | 7
 | QPSK | 2.5 | 7
 | 16QAM | 2.5 | 7
 | 64QAM | 5 | 7
 | 256QAM | [7] | 7.5
CP-OFDM | QPSK | 3.5 | 8
 | 16QAM | 3.5 | 8
 | 64QAM | 5 | 8
 | 256QAM | [7] | 8
Management of 256 QAM MPR:
Since there is only open question only for inner 256QAM this is only limited by EVM
Since EVM for CA is evaluated with only one CC allocated at the time, the 1CC MPR is enough to guarantee EVM (4.5dB for DFT-s-OFDM and 6.5dB). Note that Image leakage of 28dB would not allow to meet 256QAM EVM in most case.
WF: Table on the left is adopted for the specification without square brackets

## Slide 5: WF: PC2 BW class B non-contiguous allocation MPR
For inner, Qualcomm WC input is linked to the merge of inner and outer1
  This is not acceptable because it makes PC2 inner 3dB lower than PC3 which cannot be justified as it makes PC2 best power capability no better than PC3
  Without Qualcomm input there is good alignment and average can be taken
  To accommodate the issue, Note 1 is added allowing 4dB MPR for total allocations BW <1MHz
For Outer 1and outer 2 since most inputs are within 0.5dB of the average in most cases, the average is proposed
WF: values in the WF column for inner, outer 1 and outer 2 is adopted for the specification
BW class B |  | Inner |  |  |  |  |  |  |  | Outer1 |  |  |  |  |  |  |  | Outer 2 |  |  |  |  |  |  | 
Modulation |  | PC3 | SKW | QC | HW | LGE | Avg | WC | WF | PC3 | SKW | QC | HW | LGE | Avg | WC | WF | PC3 | SKW | QC | HW | LGE | Avg | WC | WF
DFT | QPSK | 2 | 3 | 5.5 | 3 | 3 | 3 | 5.5 | 3 -> 4 31 | 5.5 | 6.5 | 5.5 | 7 | 6.5 | 6.5 | 7 | 6.5 | 11.5 | 13 | 11.5 | 13 | 13 | 13 | 13 | 13
 | 16QAM | 2.5 | 3 | 5.5 | 3 | 3 | 3 | 5.5 | 3 -> 4 31 | 5.5 | 6.5 | 5.5 | 7 | 6.5 | 6.5 | 7 | 6.5 |  |  |  |  |  |  |  | 
 | 64QAM | 4.5 | 4.5 | 6 | 4.5 | 4.5 | 4.5 | 6 | 5 | 6 | 6.5 | 6 | 7 | 6.5 | 6.5 | 7 | 6.5 |  |  |  |  |  |  |  | 
 | 256QAM | 6 | 6 | 6.5 | 6 | 6 | 6 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 7 | 6.5 | 7 | 7 | 7 |  |  |  |  |  |  |  | 
CP | QPSK | 2.5 | 3 | 6.5 | 4 | 3 | 3.5 | 6.5 | 3.5 ->4 3.51 | 6.5 | 7 | 6.5 | 7.5 | 7 | 7 | 7.5 | 7 | 12 | 14 | 12 | 14 | 14 | 13.5 | 14 | 13.5 14.0
 | 16QAM | 3 | 3 | 7 | 4 | 3 | 3.5 | 7 | 3.5 ->4 3.51 | 7 | 7 | 7 | 7.5 | 7 | 7 | 7.5 | 7 |  |  |  |  |  |  |  | 
 | 64QAM | 5 | 5 | 7 | 5 | 5 | 5 | 7 | 5 | 7 | 7 | 7 | 7.5 | 7 | 7 | 7.5 | 7 |  |  |  |  |  |  |  | 
 | 256QAM | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |  |  |  |  |  |  |  | 

## Slide 6: WF: PC2 BW class C non-contiguous allocation MPR
For inner, Qualcomm WC input is linked to the merge of inner and outer1
  This is not acceptable because it makes PC2 inner 3dB lower than PC3 which cannot be justified as it makes PC2 best power capability no better than PC3
  Without Qualcomm input there is good alignment and average can be taken
  To accommodate the issue, Note 1 is added allowing 4dB MPR for total allocations BW <1MHz
For Outer 1and outer 2 since all inputs are within 1dB of the average in most cases, the average is proposed
WF: values in the WF column for inner, outer 1 and outer 2 is adopted for the specification
BW class C |  | Inner |  |  |  |  |  |  |  | Outer1 |  |  |  |  |  |  |  | Outer 2 |  |  |  |  |  |  | 
Modulation |  | PC3 | SKW | QC | HW | LGE | Avg | WC | WF | PC3 | SKW | QC | HW | LGE | Avg | WC | WF | PC3 | SKW | QC | HW | LGE | Avg | WC | WF
DFT | QPSK | 2.5 | 3 | 5.5 | 3.5 | 3 | 3 | 5.5 | 3 -> 4 31 | 6 | 6.5 | 8.5 | 8 | 6.5 | 7.5 | 8.5 | 7.5 | 13 | 13 | 13 | 15 | 13 | 13.5 | 15 | 13.5
 | 16QAM | 3 | 3 | 5.5 | 3.5 | 3 | 3 | 5.5 | 3 -> 4 31 | 6 | 6.5 |  | 8 | 6.5 | 7.5 | 8.5 | 7.5 |  |  |  |  |  |  |  | 
 | 64QAM | 5 | 5 | 5.5 | 5 | 5 | 5 | 5.5 | 5 | 6 | 6.5 |  | 8 | 6.5 | 7.5 | 8.5 | 7.5 |  |  |  |  |  |  |  | 
 | 256QAM | 6.5 | 6 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 |  | 8 | 6.5 | 7.5 | 8.5 | 7.5 |  |  |  |  |  |  |  | 
CP | QPSK | 3.5 | 3.5 | 5.5 | 3.5 | 3.5 | 3.5 | 5.5 | 3.5 ->4 3.51 | 7 | 7 | 8.5 | 8.5 | 7 | 8 | 8.5 | 8 | 14 | 14 | 14 | 15 | 14 | 14.5 | 14 | 14.5
 | 16QAM | 3.5 | 3.5 | 5.5 | 3.5 | 3.5 | 3.5 | 5.5 | 3.5 ->4 3.51 | 7 | 7 |  |  | 7 | 8 | 8.5 | 8 |  |  |  |  |  |  |  | 
 | 64QAM | 5 | 5 | 5.5 | 5 | 5 | 5 | 5.5 | 5 | 7 | 7 |  |  | 7 | 8 | 8.5 | 8 |  |  |  |  |  |  |  | 
 | 256QAM | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |  |  | 7.5 | 8 | 8.5 | 8 |  |  |  |  |  |  |  | 

## Slide 7: Open issue: MPR when only one CC is allocated
This issue is present for both PC3 and PC2 cases:
With current MPR definition for CA, CA MPR applies even when only one CC as allocation and is significantly higher than the single CC MPR
In general this should not be needed as ACLR and SEM are relaxed (wider) and EVM anyhow applies only for allocation in one CC
However additional MPR is needed for edge allocations at least in class B because the guard band is smaller than for the single CC case and SEM at channel edge is an issue.
WF: companies are encouraged to provide input on the topic in next meeting to enable similar performance to single CC in CA mode when only one CC is allocated with proper management of the edge allocations when CA guard-band is smaller than single CC case

## Slide 8: References:
[1] R4-2104655 FR1 PC2 Contiguous UL CA Simulation Results, Nokia Corporation, R4#98bis-e
[2] R4-2104994 MPR initial simulation results for NR intra-band contiguous CA according to candidate RF architectures, LG Electronics France, R4#98bis-e
[3] R4-2105088 Power capability and back-off for NC (and contiguous) intra-band CA, Ericsson, R4#98bis-e
[4] R4-2106304 PC2 Class C UL CA UE Architecture and MPR/A-MPR evaluation, Skyworks Solutions Inc. , R4#98bis-e
[5] R4-2107260 on HPUE intra-band contiguous CA MPR, HiSilicon Technologies Co. Ltd, R4#98bis-e
[6] R4-2107370 HPUE MPR with 1PA architecture, Qualcomm Incorporated, R4#98bis-e