## Slide 1: WF on intra-band UL contiguous CA for UL MIMO
vivo
3GPP TSG-RAN WG4 Meeting # #98-bis-e
Electronic Meeting, Apr. 12 -20, 2021
R4-210xxxx

## Slide 2: Configurations for CA+UL MIMO requirements
Proposals:
  RF requirements with following configuration is defined:
    2 layer configuration with codebook TPMI index 0.
    1 layer 2 port configuration with full power transmission: mode 0/1/2
    (Transparent) Tx diversity
      Agreements:
  2 layer configuration with codebook TPMI index 0 need to be defined.
  FFS for 1 layer 2 port UL MIMO configuration
  FFS for Transparent TxD configuration

## Slide 3: RF requirement definition type
Proposals (as in R4-2104956):
      Agreements:
  Companies encourage to further check the RF requirements for CA+UL MIMO
Tx characteristics | UL-MIMO + Intra-band UL C CA
UE maximum output power | Per-UE (Sum of all Tx and CC)
UE maximum output power reduction | [FFS, Per-UE but requirements need study]
UE addition maximum output power reduction | Per-UE
Configured transmitted power | Per-UE
Minimum output power | Per-carrier, sum of 2Tx
Transmit OFF power | Per-carrier per connector
Transmit ON/OFF time mask | Per-carrier per connector
Power control | Per-carrier, sum of 2Tx
Frequency error | Per-carrier per connector
Transmit modulation quality (EVM, Carrier leakage, IBE and EVM spectrum flatness) | [FFS]
Occupied bandwidth | Per-UE
Out of band emission | Per-UE
Spurious emission | Per-UE
Transmit intermodulation | Per connector, 2carreirs active

## Slide 4: Baseline RF architecture
Proposals
  Two PAs architecture with each PA supporting the aggregated CBW
      Agreements:
  Yes

## Slide 5: MPR
Proposals
  For PC3 intra-band UL contiguous CA in MIMO, reuse the MPR defined for PC3 contiguous CA
  For PC2 intra-band UL contiguous CA in MIMO, Evaluate value of delta MPR needed from the start of PC3 MPR requirement.
      Agreements :
  For PC3 intra-band UL contiguous CA in MIMO, use the MPR defined for PC3 contiguous CA as a starting point, check whether there is delta MPR.
  FFS PC2 intra-band UL contiguous CA in MIMO.

## Slide 6: Signaling
Proposals
  New capability for Supported aggregated CBW within UL CA+UL MIMO (R4-2106562)
      Agreements :
  FFS