## Slide 1: WF on [137] NR_ext_to_71GHz_Part1
Intel (Moderator)
3GPP TSG-RAN WG4 Meeting # #98-bis-e
Electronic Meeting, Apr. 12 -20, 2021
R4-210xxxx

## Slide 2: Issue 2-1-2: Licensed band definition
Background: Currently no regulatory for licensed operation in 60 GHz
Proposals
  Option 1: 66 – 71 GHz (CATT, ZTE, Ericsson, CMCC, Huawei)
  Option 2: Postpone the decision until regulatory becomes clear (Charter, Qualcomm, vivo, MTK, LGE, Nokia, Apple, AT&T)
WF (GTW on Apr. 14):
  Agree to define a band [66-71] GHz, based on which the system parameters discussion can proceed with an aim to harmonize for both licensed and unlicensed bands
  The work except system parameters on this band will start when regulations become clear

## Slide 3: Issue 2-1-3: Unlicensed band definition
Proposals
  Option 1: 57 – 71 GHz (vivo, Apple, Ericsson, Nokia, Charter, Qualcomm, CMCC, MTK, Xiaomi, LGE)
  Option 2: 57 – 66 GHz (vivo)
  Option 3: 57.24 – 70.2 GHz (CATT)
      WF (GTW on Apr. 14): :
  Option 1

## Slide 4: Issue 2-1-5: Baseline regulatory requirement
Proposals
  Option 1: ETSI EN 303 753 harmonized standard as baseline (Nokia, Xiaomi, LGE)
  Option 2: ETSI EN 303 753 is one of considerations and cannot be baseline (Qualcomm, Ericsson)
      WF (GTW on Apr. 14): :
  RAN4 to consider EU harmonized standards as starting point, not precluding other available regulatory requirements

## Slide 5: Issue 3-1-1: Minimum Channel BW
Background: Some of Minimum CBW are still open and RAN4 SI outcome does not align with RAN1 LS.
Proposals
      WF (GTW on Apr. 14): :
  120kHz: Option 1, 480kHz: Option 2, 960kHz: Option 1,
  The above agreement is subject to further review of licensed spectrum block sizes.
 | RAN4 SI Outcome (TR 38.808) | RAN1 LS (R1-2102128)
Subcarrier spacing [kHz] | Minimum bandwidths [MHz] | Minimum bandwidths [MHz]
120 | 50, 400 (Note) | Option 1: 100 (QC, CATT, MTK, Xiaomi, LGE, Ericsson, Apple, OPPO, ZTE) Option 2: 200 (CMCC, Huawei) Option 3: 400 (vivo, Intel, Nokia)
480 | 200 | Option 1: 200 (QC, CATT, CMCC, LGE, Huawei, Apple, OPPO, ZTE) Option 2: 400 (QC, vivo, Ericsson, Intel, Nokia)
960 | 400, 2160 (Note) | Option 1: 400 (Charter, QC, CATT, CMCC, vivo, Xiaomi, LGE, Huawei, Apple, Samsung, OPPO, Nokia, ZTE) Option 2: 800 Option 3: 2000 (Intel) or 2160 (Ericsson)
Note: for the cases where multiple values are listed as candidates, there is no direct linking among min and max values in this table. |  | 

## Slide 6: Issue 3-1-2: Maximum Channel BW
Background: Maximum CBW with 960 kHz SCS is still open and RAN4 SI outcome does not align with RAN1 LS.
Proposals
      WF (GTW on Apr. 14): :
  To further consider the following options:
    2000MHz for both licensed and unlicensed operations
    2160MHz as the max. bandwidth, also 2000MHz will be specified as a channel bandwidth, both licensed and unlicensed operations
    2160MHz for unlicensed operation and 2000MHz for licensed operation
    Make a decision for unlicensed operation and FFS for licensed operation
 | RAN4 SI Outcome (TR 38.808) | RAN1 LS (R1-2102128)
Subcarrier spacing [kHz] | Maximum bandwidths [MHz] | Maximum bandwidths [MHz]
120 | 400 | 400
480 | 1600 | 1600
960 | 1600, 2000, 2160, 3200 (Note) | Option 1: 2000 (Qualcomm, CATT, vivo, ZTE, Huawei, Intel, Samsung) Option 2: 2160 (Charter, Xiaomi, LGE, Ericsson, Sony, [Qualcomm])
Note: for the cases where multiple values are listed as candidates, there is no direct linking among min and max values in this table. |  | 

## Slide 7: Issue 3-1-4: Spectrum Utilization
Background: RAN1 LS asked SU on the max CBWs for each SCS.
Proposals
  Option 1: Target the same SU in FR2 (<= 95% SU) and table in R4-2104821 (Apple, vivo)
  Option 2: Consider ~ 85% SU (Ericsson)
  Option 3: Need more study (MTK, LGE, Qualcomm, Huawei)
WF (GTW on Apr. 15):
  Option 3