## Slide 1: WF on [137] NR_ext_to_71GHz_Part1
Intel (Moderator)
3GPP TSG-RAN WG4 Meeting # #98-bis-e
Electronic Meeting, Apr. 12 -20, 2021
R4-210xxxx

## Slide 2: Issue 2-1-2: Licensed band definition
Background: Currently no regulatory for licensed operation in 60 GHz
Proposals
  Option 1: 66 – 71 GHz (CATT, ZTE, Ericsson, CMCC, Huawei)
  Option 2: Postpone the decision until regulatory becomes clear (Charter, Qualcomm, vivo, MTK, LGE, Nokia, Apple, AT&T)
WF (GTW on Apr. 14):
  Agree to define a band [66-71] GHz, based on which the system parameters discussion can proceed with an aim to harmonize for both licensed and unlicensed bands
  The work except system parameters on this band will start when regulations become clear

## Slide 3: Issue 2-1-3: Unlicensed band definition
Proposals
  Option 1: 57 – 71 GHz (vivo, Apple, Ericsson, Nokia, Charter, Qualcomm, CMCC, MTK, Xiaomi, LGE)
  Option 2: 57 – 66 GHz (vivo)
  Option 3: 57.24 – 70.2 GHz (CATT)
      WF (GTW on Apr. 14): :
  Option 1

## Slide 4: Issue 2-1-5: Baseline regulatory requirement
Proposals
  Option 1: ETSI EN 303 753 harmonized standard as baseline (Nokia, Xiaomi, LGE)
  Option 2: ETSI EN 303 753 is one of considerations and cannot be baseline (Qualcomm, Ericsson)
      WF (GTW on Apr. 14): :
  RAN4 to consider EU harmonized standards as starting point, not precluding other available regulatory requirements

## Slide 5: Issue 3-1-1: Minimum Channel BW
Background: Some of Minimum CBW are still open and RAN4 SI outcome does not align with RAN1 LS.
Proposals
      WF (GTW on Apr. 14): :
  120kHz: Option 1, 480kHz: Option 2, 960kHz: Option 1,
  The above agreement is subject to further review of licensed spectrum block sizes.
 | RAN4 SI Outcome (TR 38.808) | RAN1 LS (R1-2102128)
Subcarrier spacing [kHz] | Minimum bandwidths [MHz] | Minimum bandwidths [MHz]
120 | 50, 400 (Note) | Option 1: 100 (QC, CATT, MTK, Xiaomi, LGE, Ericsson, Apple, OPPO, ZTE) Option 2: 200 (CMCC, Huawei) Option 3: 400 (vivo, Intel, Nokia)
480 | 200 | Option 1: 200 (QC, CATT, CMCC, LGE, Huawei, Apple, OPPO, ZTE) Option 2: 400 (QC, vivo, Ericsson, Intel, Nokia)
960 | 400, 2160 (Note) | Option 1: 400 (Charter, QC, CATT, CMCC, vivo, Xiaomi, LGE, Huawei, Apple, Samsung, OPPO, Nokia, ZTE) Option 2: 800 Option 3: 2000 (Intel) or 2160 (Ericsson)
Note: for the cases where multiple values are listed as candidates, there is no direct linking among min and max values in this table. |  | 

## Slide 6: Issue 3-1-2: Maximum Channel BW
Background: Maximum CBW with 960 kHz SCS is still open and RAN4 SI outcome does not align with RAN1 LS.
Proposals
      WF (GTW on Apr. 14): :
  To further consider the following options:
    2000MHz for both licensed and unlicensed operations
    2160MHz as the max. bandwidth, also 2000MHz will be specified as a channel bandwidth, both licensed and unlicensed operations
    2160MHz for unlicensed operation and 2000MHz for licensed operation
    Make a decision for unlicensed operation and FFS for licensed operation
 | RAN4 SI Outcome (TR 38.808) | RAN1 LS (R1-2102128)
Subcarrier spacing [kHz] | Maximum bandwidths [MHz] | Maximum bandwidths [MHz]
120 | 400 | 400
480 | 1600 | 1600
960 | 1600, 2000, 2160, 3200 (Note) | Option 1: 2000 (Qualcomm, CATT, vivo, ZTE, Huawei, Intel, Samsung) Option 2: 2160 (Charter, Xiaomi, LGE, Ericsson, Sony, [Qualcomm])
Note: for the cases where multiple values are listed as candidates, there is no direct linking among min and max values in this table. |  | 

## Slide 7: Issue 3-1-4: Spectrum Utilization
Background: RAN1 LS asked SU on the max CBWs for each SCS.
Proposals
  Option 1: Target the same SU in FR2 (<= 95% SU) and table in R4-2104821 (Apple, vivo)
  Option 2: Consider ~ 85% SU (Ericsson)
  Option 3: Need more study (MTK, LGE, Qualcomm, Huawei)
WF (GTW on Apr. 15):
  Option 3

## Slide 8: Issue 1-2-1: Unfinished UE Testability
Background:
  Majority view is supporting option 1 (Unfinished UE testability aspects shall not impact setting UE core requirements and completing the NR > 52.6 GHz WI)
Recommended WF:
  Agree on the option 1

## Slide 9: Issue 1-2-2: Testability
Background:
  There are approximately half and half to support the option 1 (include UE OTA in Rel-17 WI) and option 2 (plenary discussion). While this has been discussed in the plenary, the moderator understands this is RAN4 responsibility.
  During 2nd round discussion, a single company is clearly opposing against for the option 1 as this is plenary issue.
Recommended WF:
  RAN4 continues the discussion in the next meeting.

## Slide 10: Issue 3-1-2: Maximum Channel BW in 2nd rd
Background: Further input during 2nd round discussion based on the GTW on Apr. 14
  To further consider the following options:
    2000MHz for both licensed and unlicensed operations (vivo, CATT, Huawei)
    2160MHz as the max. bandwidth, also 2000MHz will be specified as a channel bandwidth, both licensed and unlicensed operations (Xiaomi, Charter, Sony)
    2160MHz for unlicensed operation and 2000MHz for licensed operation (vivo, Apple)
    Make a decision for unlicensed operation and FFS for licensed operation
Recommended WF
  RAN4 continues to discuss in the next meeting with the options above

## Slide 11: Issue 3-1-3: Carrier Aggregation Support
Background: Whether CA is enabled for 60 GHz and there were the following inputs during 2nd round discussion
  Input 1: No CA to support CBW ≤ 2000 MHz. CA is enabled for CBW > 2000 MHz (vivo)
  Input 2: CA is enabled for CBW < 2000 MHz to support 2000 MHz or larger. Sufficient number of smaller CBW shall be supported (Qualcomm)
  Input 3: Prioritize combination first (Apple)
  Input 4: CA shall be supported (CATT, Sony)
    Input 4-1: up to 4 CCs and max aggregated BW is 8.84 GHz (Charter)
    Input 4-2: CA case could be small CBW for larger aggregated CBW such as 5 x 400 MHz to support 2000 MHz. n x 2000 MHz can be discussed.
  Input 5: Need more analysis and discussion (Huawei)
Recommended WF
  RAN4 continues to discuss in the next meeting and interested companies are encouraged to bring a contribution.

## Slide 12: Issue 3-2-1: Harmonize licensed and unlicensed channelization
Background:
  The following WF suggested by the Chair in GTW on Apr. 15 but no conclusion.
    RAN4 agrees to seek a unified raster design for both licensed and unlicensed bands.
  During 2nd round discussion, views are diverged.
Recommended WF
  RAN4 come back this issue in the next meeting.

## Slide 13: Issue 3-2-2: Channelization for licensed band
Background:
  The following options were discussed in GTW on Apr. 15. 2nd round input are indicated for each option:
    Option 1: Do not use the NR-U approach, i.e. considering IEEE channels with fixed channelization
    Option 2: Do not consider IEEE channels, use floating raster like in NR system (Xiaomi, Apple)
    Option 3: Do not consider IEEE channels, use a fixed raster (Ericsson)
    Other comments:
      A fixed faster, harmonized where possible for the agreed unlicensed band (MTK, Charter)
      Come back next meeting (vivo)
      Two options can be discussed to see pros and cons in the next meeting (CATT)
  During 2nd round discussion, views are diverged.
      Recommended WF:
  Continue discussion in the next meeting

## Slide 14: Issue 3-2-3: Channelization for unlicensed band
Background:
  The following proposals were discussed
    Option 1: Align with IEEE 802.11ad/ay channels, i.e., fixed channelization like in NR-U (Charter, Qualcomm, Sony)
    Option 1A: Support sub-channelization for 2.16 GHz channels to facilitate smooth coexistence for narrowband operation (Nokia, CATT, Xiaomi, LGE)
    Option 2: Do not consider IEEE channels, i.e., floating raster like in NR system
    Option 3: More time to study (MTK, Huawei)
      Recommended WF:
  Continue discussion in the next meeting