## Slide 1: WF on UE RF requirements for R17 NB-IoT 16QAM
Nokia
3GPP TSG-RAN WG4 Meeting # 98-bis-e
Electronic Meeting, 12 – 20 April 2021
Agenda Item: 10.9
R4-210xxxx

## Slide 2: Background
Contributions on UE RF requirements for R17 NB-IoT 16QAM in RAN4#98-bis-e have a variety of proposals:
[1] R4-2104651 MPR for NB-IoT 16-QAM Nokia Corporation
[2] R4-2107246 UE RF impact analysis on R17 NB_IoT Ericsson
[3] R4-2107258 MPR Simulation Assumptions for 16QAM NB-IoT Uplink Huawei, HiSilicon
The Way Forward from the discussion of the contributions are summarized in the following slides.

## Slide 3: Way forward on EVM limit
Provisional Agreement:
  Same as E-UTRA, i.e., 12.5%.
To be confirmed in RAN4#99-e to allow more study.

## Slide 4: Way forward on In-band Emission limit
Provisional Agreement:
  Include the EVM limit in the IBE mask the same way as E-UTRA and NR.
To be confirmed in RAN4#99-e to allow more study.

## Slide 5: Way forward on MPR simulation assumptions
Agreements:
  I/Q image: 25 dB, Carrier leakage: 25 dBc, CIM3: 60 dB
  PA calibration point: MPR=0 for single-tone (worst case among 3.75 kHz pi/2 BPSK and pi/4 QPSK, 15 kHz pi/2 BPSK and pi/4 QPSK)
  Whether to include EVM limit: Yes.
    Can be reviewed in RAN4#99-e if find necessary by study.
  Whether to include IBE mask: Yes.
    Can be reviewed in RAN4#99-e if find necessary by study.
  Whether to include 12-tone: Yes. Simulate allocations of 3, 6, and 12 tones.
  Power classes to be considered: 3, 5
    Power class 6 is optional for simulation results in RAN4#99-e.