## Slide 1: WF on NR-U RRM Core Requirements all agreements in RAN4#98-e in email thread: [98-bis-e][201] NR_unlic_RRM_1
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #98bis-e R4-2105700
Electronic Meeting, 12th – 20th April, 2021
Agenda Items: 5.1.2

## Slide 2
Agreements from the 1st GTW session
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: General: Terminology updates due to CSSF (1/2)
Proposal 1 (ZTE Corporation): The following wording can be used in the spec: “When the UE is jointly configured with SMTC and CSSF, the assumed periodicity of SMTC occasions corresponds to the value of CSSF multiplies the original periodicity”.
Proposal 2 (Huawei, HiSilicon): L* is the number of SSB/SMTC occasions not available at the UE during the corresponding period, where the occasions are those that are actively used by the UE during the period considering the factors, e.g. DRX, MGRP, CSSF.
Proposal 3 (MediaTek, Qualcomm):
  For intra-frequency measurements without measurement gaps (deactivated SCell), intra-frequency measurements with measurement gaps, and inter-frequency measurements, to add the following notes in the requirement:
        When configured with DRX, the UE is not required to determine the availability of SMTC occasions more frequent than once per DRX cycle x CSSF.
        When configured with measurement gaps, the UE is not required to determine the availability of SMTC occasions more frequent than once during MGRP x CSSF.
        When configured with measurement cycles, the UE is not required to determine the availability of SMTC occasions more frequent than once per measurement cycle x CSSF.
  For Intra-frequency measurements without measurement gaps, to add the following notes in the requirement:
        The UE is not required to determine the availability of SMTC occasions more frequent than once during SMTC period x Kp x CSSF.
        When configured with DRX, the UE is not required to determine the availability of SMTC occasions more frequent than once per DRX cycle x Kp x CSSF.

## Slide 4: General: Terminology updates due to CSSF (2/2)
Proposal 4 (Apple):
    For intra-frequency measurements without measurement gaps (deactivated SCell), intra-frequency measurements with measurement gaps, and inter-frequency measurements, to add the following notes in the requirement:
          When configured with DRX, the UE is not required to determine the availability of SMTC occasions more frequent than once per DRX cycle x CSSF x 1.5 for DRX≤320ms or once per DRX cycle x CSSF for DRX >320ms.
          When configured with measurement gaps, the UE is not required to determine the availability of SMTC occasions more frequent than once during MGRP x CSSF.
          When configured with measurement cycles, the UE is not required to determine the availability of SMTC occasions more frequent than once per measurement cycle x CSSF.
    For Intra-frequency measurements without measurement gaps, to add the following notes in the requirement:
          The UE is not required to determine the availability of SMTC occasions more frequent than once during SMTC period x Kp x CSSF.
          When configured with DRX, the UE is not required to determine the availability of SMTC occasions more frequent than once per DRX cycle x Kp x CSSF x 1.5 for DRX≤320ms or once per DRX cycle x Kp x CSSF for DRX >320ms.
    For RLM: The UE is not required to determine the availability of SSB occasions more frequent than once per L1 indication interval.
    For CBD: The UE is not required to determine the availability of SSB occasions more frequent than once per P*DRX cycle length when configured with DRX.
Proposal 5 (Ericsson) - For measurement requirements with CSSF: The UE is not required to determine the availability of SMTC occasions more frequent than what is required by CSSF.

## Slide 5: SI reading with LBT in RRC release with redirection, RRC re-establishment, and paging interruption
Specify the SI reading delay in the test cases.

## Slide 6: SCell Activation: Interruptions
General
  Consider following scenarios for interruption requirements:
    Case 1: For intra-band CA, where victims Cells are all within the same band with the SCell being activated.
    Case 2: For inter-band CA, two cases to be considered:
    Case 2a: Inter-band victim Cells only without intra-band victim Cells.
    Case 2b: Inter-band victim Cells and intra-band victim Cells.
Intra-band CA
  Proposals 1 (Huawei, HiSilicon, Apple, MTK): For intra-band CA, up to 1+L interruption windows are allowed during SCell activation. The length of up to L interruption windows shall be extended considering the RF tuning.
  Proposal 2 (Qualcomm Incorporated): There is no need to specify additional RF re-tuning time or extend the interruption time because of DL LBT failure during intra-band SCell activation. No further clarification needed in the spec-text
Inter-band CA where victims on inter-band CCs and intra-band CCs interruptions and target SCell is unknown
  Proposal 1: (Ericsson, ZTE Corporation, Apple, MTK, Huawei): Scenario with victims on inter-band CCs and intra-band CCs: more than one interruption can be allowed.
  Proposal 2 (Qualcomm Incorporated): A single interruption applies to any victim cell outside the band with the SCell being activated, irrespective of whether any already active SCell (intra-band w.r.t. the aggressor) is present or not. No further clarification is needed in the spec text.
Inter-band CA where victims on inter-band CCs only (no intra-band victim serving cells) target SCell is unknown
  Capture in 38.133, the following RAN4 agreement from [R4-2103025]:
    For unknown target SCell:
      Scenario with victims on inter-band CCs only (no intra-band victim serving cells): single interruption
Inter-band CA regardless of whether the victim cell is on an intra-band or inter-band CC and target SCell is known
  Single interruption applies, regardless of whether the victim cell is on an intra-band or inter-band CC when measureCycle ≤ 160 ms . For the case when known SCell with measureCycle > 160 ms, continue the discussion in 2nd round.

## Slide 7: SCell Activation: sCellDeactivationTimer is NOT configured
Applicability of SCell activation requirements when sCellDeactivationTimer is NOT configured
  SCell activation delay requirements are applicable in
    Scenario A (CA with NR PCell and NR SCell) with any LBT type
    Scenario B and C (E-UTRAN-NR-U DC/SA NR-U) with LBT type 2C.
    In all scenarios, if the UE does not experience any UL LBT failures during SCell activation/deactivation.
  For all other scenarios the SCell activation requirements for NR-U do not apply, when the SCell activation delay exceeds the pre-defined time period T = 1280 ms.
    Note 1: UE behavior for this case is left undefined
    Note 2: Pre-defined time period T = 1280ms corresponds to the longest possible value of sCellDeactivationTimer

## Slide 8: Measuring CSI-RS during SCell activation
When none of the RRC parameters CO-DurationPerCell-r16, SlotFormatIndicator, and CSI-RS-ValidationWith-DCI-r16 is configured to a UE and all of the CSI reporting resources for being-activated SCell are available, the existing delay requirement of SCell activation with CCA could apply after removing the L4 related extension definitions in CSI reporting delay.

## Slide 9: Timing: Definition of the reference cell which is not available, with respect to DRX
Proposal 1 (Ericsson, Qualcomm Incorporated, Huawei, HiSilicon): SSB in a reference cell subject to DL CCA does not have to be outside the gaps in order to meet UE timing requirements SSB does not have to be within ON duration in a reference cell subject to DL CCA in order to meet UE timing requirements
  No clarification related to gap DRX is needed on the current definition of unavailability of a reference cell on a carrier frequency subject to CCA in section 7.1.1.
Proposal 2: (Qualcomm, Apple, MTK):
  In the requirements of clause 7.1.2, the term reference cell on a carrier frequency subject to CCA is not available at the UE refers to when at least one SSB is configured by gNB, but the first two successive candidate SSB positions for the same SSB index within the discovery burst transmission window are not available for at least one SSB, at the UE due to DL CCA failures at gNB during the last X ms; otherwise the reference cell on the carrier frequency subject to CCA is considered as available at the UE.
      X is FFS, X>160ms.

## Slide 10: Timing: Definition of the reference cell which is not available, with respect to MGs
Proposal 1 (Ericsson, Qualcomm): SSB in a reference cell subject to DL CCA does not have to be outside the gaps in order to meet UE timing requirements
  No clarification related to gap is needed on the current definition of unavailability of a reference cell on a carrier frequency subject to CCA in section 7.1.1.
Proposal 2 (Huawei, ZTE, MTK): The availability of reference cell shall base on the SSB within the DL active BWP which is not overlapping with measurement gaps.
Proposal 3: (Qualcomm, Apple, MTK):
  In the requirements of clause 7.1.2, the term reference cell on a carrier frequency subject to CCA is not available at the UE refers to when at least one SSB is configured by gNB, but the first two successive candidate SSB positions for the same SSB index within the discovery burst transmission window are not available for at least one SSB, at the UE due to DL CCA failures at gNB during the last X ms; otherwise the reference cell on the carrier frequency subject to CCA is considered as available at the UE.
      X is FFS, X>160ms.

## Slide 11: Timing test cases
The UE timing related requirements are verified in non-DRX and without measurement gaps.