## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs, UL spatial info switch
Intel Corporation
3GPP TSG-RAN WG4 Meeting #98bis-e R4-210####
Electronic Meeting, 12-20, April, 2021

## Slide 2: BWP switching on multiple CCs in core part(1)
Issue 1-1-1: Whether requirement for RRC based BWP switch on single CC for SCell for Rel-16 is applicable
  Option 1 : RRC based BWP switch delay requirement for single CC in section 8.6.3 is applicable to only SpCell.
  Option 2 : Yes.
  Option 2a : Yes, but further clarification about SCell is preferred, i.e. RRC-based BWP switch on single CC is appliable for SCell with parameter change except for the modification of firstActiveDownlinkBWP-Id and firstActiveUplinkBWP-Id.

## Slide 3: BWP switching on multiple CCs in core part(2)
Issue 1-1-2: Whether requirement for RRC based BWP switch on multiple CCs for Rel-16 is applicable
  Option 1: Yes.
  Option 1a: Yes, with clarification provided in single CC section on applicability of RRC based BWP switch for Scell.
  Option 2: Yes, but further clarification about SCells is needed. Clarify that RRC-based BWP switch on multiple CCs are appliable for SCells with the parameter change except the modification of parameters firstActiveDownlinkBWP-Id and firstActiveUplinkBWP-Id
  Option 3: No. Simultaneous RRC based BWP switch delay requirement for multiple CCs is removed. Non-simultaneous RRC based BWP switch delay requirement for multiple CCs is applicable to only PCell and PSCell in NR-DC.
  Option 4: No. Define delay requirements for changing any BWP parameter other than the firstActiveDownlinkBWP-Id or firstActiveUplinkBWP-Id via RRC on SCell. The delay requirement is defined by reusing the delay defined in section 8.6.3, TS 38.133.

## Slide 4: UL Spatial Relation Info Switch in core part(1)
Issue 2-1-1: Delay requirements for MAC–CE based UL spatial relation switch
  Option 1 : Refer to section 8.14 for additional delay due to PL-RS switch in UL spatial relation switch for known PL-RS. Specify that the no requirement is imposed during transient period (before PL-RS switch complete).
  Option 2 : Refer to section 8.14 for additional delay due to PL-RS switch in UL spatial relation switch.
  Option 3:
    If Only pucch-PathlossReferenceRS is changed in PUCCH-SpatialRelationInfo, refer to section 8.14.
    If both pucch-SpatialRelation for transmission and pucch-PathlossReferenceRS are changed in PUCCH-SpatialRelationInfo, longer delay is expected.
  Option 4: When both pucch-SpatialRelation for transmission and pucch-PathlossReferenceRS are changed in PUCCH-SpatialRelationInfo, if both DL-RS and PL-RS are known, the additional delay is as specified in 8.14, otherwise longer delay is expected. No requirement is imposed during the transient period (before both DL-RS and PL-RS relations switch complete).

## Slide 5: BWP switching on multiple CCs in performance part(1)
Issue 3-1-1: RAN4 to define test cases for simultaneous RRC based BWP switch on multiple CCs
FFS:
  Option 1 :
    TC1: EN-DC with NR FR1 cell (E-UTRAN PCell + NR FR1 PSCell + NR FR1 SCell)
    TC2: EN-DC with NR FR2 cell (E-UTRAN PCell + NR FR2 PSCell + NR FR2 SCell)
    TC3: SA with NR FR1 cell (NR FR1 PCell + NR FR1 SCell + NR FR1 SCell)
    TC4: SA with NR FR2 cell (NR FR2 PCell + NR FR2 SCell + NR FR2 SCell)