## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs, UL spatial info switch
Intel Corporation
3GPP TSG-RAN WG4 Meeting #98bis-e R4-210####
Electronic Meeting, 12-20, April, 2021

## Slide 2: BWP switching on multiple CCs in core part(1)
Issue 1-1-1: Whether requirement for RRC based BWP switch on single CC for SCell for Rel-16 for Rel-16 is applicable
  Yes, but further clarification about SCell is preferred, i.e. RRC-based BWP switch on single CC is appliable for SCell with parameter change except for the modification of firstActiveDownlinkBWP-Id and firstActiveUplinkBWP-Id.

## Slide 3: BWP switching on multiple CCs in core part(2)
Issue 1-1-2: Whether requirement for RRC based BWP switch on multiple CCs for Rel-16 is applicable
  Yes, but further clarification about SCells is needed. Clarify that RRC-based BWP switch on multiple CCs are appliable for SCells with the parameter change except the modification of parameters firstActiveDownlinkBWP-Id and firstActiveUplinkBWP-Id

## Slide 4: UL Spatial Relation Info Switch in core part(1)
Issue 2-1-1: Delay requirements for MAC–CE based UL spatial relation switch
Option 5: With PUCCH Spatial relation info switch when both associated DL-RS and pucch-PathlossReferenceRS change simultaneously with same MAC CE command
    If both associated DL-RS and PL-RS are known and performed sequentially, the switching delay is specified in section 8.14.3
    If either associated DL-RS or PL-RS are unknown, longer switching delay is expected.
    No requirements are defined until both the spatial relation switch and PL-RS switch are complete.
  Option 6: If UL spatial relation switch for PUCCH (PUCCH-SpatialRelationInfo) is changed as described in 8.12.3, and the pucch-PathlossReferenceRS in PUCCH-SpatialRelationInfo is also changed, an additional DL Pathloss reference signal switching delay may be allowed. The detailed delay and conditions are FFS, but RAN4 need to consider:
    Known DL pathloss RS
    Unknown DL pathloss RS

## Slide 5: BWP switching on multiple CCs in performance part(1)
Issue 3-1-1: RAN4 to define test cases for simultaneous RRC based BWP switch on multiple CCs
  TC1: EN-DC with NR FR1 cell (E-UTRAN PCell + NR FR1 PSCell + NR FR1 SCell)
  TC2: EN-DC with NR FR2 cell (E-UTRAN PCell + NR FR2 PSCell + NR FR2 SCell)
  TC3: SA with NR FR1 cell (NR FR1 PCell + NR FR1 SCell + NR FR1 SCell)
  TC4: SA with NR FR2 cell (NR FR2 PCell + NR FR2 SCell + NR FR2 SCell)