## Slide 1: WF on performance requirements of CSI-RS based L3 measurement
CATT,OPPO,…
3GPP TSG-RAN WG4 Meeting #98bis-e R4-21XXXX Electronic Meeting, 12th – 20th April, 2021
Agreement in 1st round
Agreement in GTW (Apr. 16th)
Agreement in 2nd round

## Slide 2: Sub-topic 2-1 CSI-RSRP measurement accuracy requirements
Issue 2-1: Timing offset for specifying CSI-RSRP measurement accuracy requirements
  Specify CSI-RSRP accuracy requirement with the absolute timing offset between the reference measurement timing and the target CSI-RS in one layer no larger than CP

## Slide 3: Sub-topic 2-2 CSI-RSRQ measurement accuracy requirements
Issue 2-2: Timing offset for specifying CSI-RSRQ measurement accuracy requirements
  Specify CSI-RSRQ accuracy requirement with the absolute timing offset between the reference measurement timing and the target CSI-RS in one layer no larger than CP

## Slide 4: Sub-topic 2-3 CSI-SINR accuracy requirements
Issue 2-3: Timing offset and upper limit of side condition for specifying CSI-SINR measurement accuracy requirements
  Specify CSI-SINR accuracy requirement based on the following conditions on timing offset between the reference measurement timing and the target CSI-RS (T) and Es/Iot side condition(s)
    Side condition #1:
      |TΔ|≤ CP/2 and Es/Iot ≤ 15 dB
    Side condition #2
      |TΔ|≤ CP and Es/Iot ≤ [6] dB
      No dedicated test cases will be introduced for side condition #2

## Slide 5: Sub-topic 1-1: Time offset configuration(in email thread #213)
Time offset configuration between cells in the test cases
  Time offset for CSI-RSRP and CSI-RSRQ accuracy requirement: CP
  Time offset for CSI-SINR accuracy requirement: CP/2
The unit of time offset
  Use absolute time for all tests , e.g., s
    CP for 15KHz: 4.7 us
    CP for 30KHz: 2.35 us
    CP for 120KHz: 0.58 us

## Slide 6: Sub-topic 1-2: Clarification on test requirements (in email thread #213)
No more clarification on UE behavior is needed in the test case. The test requirements need to be calculated based on the core requirements.

## Slide 7: Sub-topic 1-4: Clarification on test procedure (in email thread #213)
UE behavior assumption in T1 and T2
  During time duration T1, the UE has detected associatedSSB. From T2, it starts measuring CSI-RS in T2.
  Option 1: During time duration T1, the UE does not have any timing information of neighbour cell (e.g., cell 3 for EN-DC test or cell 2 in SA test case). From T2, the UE detects associatedSSB and then measure CSI-RS.
  Option 2: During time duration T1, the UE has detected associatedSSB. From T2, it starts measuring CSI-RS in T2.
  Note: Either option is allowed, and up to different test setup.