## Slide 1: WF on core part maintenance of CSI-RS based L3 measurement requirements
Apple, …
3GPP TSG-RAN WG4#98-bis-e Meeting R4-210xxxx
Electronic Meeting, Apr. 12-20, 2021 Document for: Approval
Agenda item: 5.7.1

## Slide 2: Way forward – Scheduling restriction for intra-f CSI-RS measurement in TDD band
  When UE performs CSI-RS intra-frequency measurements in a TDD band, UE is not expected to transmit PUCCH/PUSCH/SRS on configured CSI-RS resource symbols, and on 1 OFDM symbol before and after each consecutively configured CSI-RS symbols.
    1 OFDM symbol before the configured CSI-RS symbol can leave some margin to accommodate timing error and TA uncertainty between NW and UE
    It is up to UE implementation whether 1 OFDM symbol before the configured CSI-RS symbol can be scheduled.

## Slide 3: Way forward – Time domain restriction for CSI-RS configuration
All L3 CSI-RS resources in the same MO have identical periodicity.
For inter-frequency measurements, Rel-16 L3 CSI-RS requirements are defined under assumption that all CSI-RS resources in the same MO are configured in the same 5ms window
For intra-frequency measurements: Rel-16 L3 CSI-RS requirements are defined under assumption that CSI-RS resources in the same MO can be configured in up to two separated 5ms windows during one CSI-RS resource period.
  When intra-frequency L3 CSI-RS are configured in two separated windows, the minimum periodicity of the configured CSI-RS resources is 20ms.
  Measurement requirements are not impacted by separated 5ms windows.

## Slide 4: Way forward – Starting point of 5ms time window
For CSI-RS based L3 intra-frequency measurement, the starting point of the 5ms window is the slot boundary of the serving cell, where the corresponding slot contains the first configured L3 CSI-RS resource of the serving cell in the servingCellMOintra-frequency MO.
  Since it is not guaranteed that all configured L3 CSI-RS resources of the neighbor cell are always detectable for UE, the starting point can only be based on serving cell’s configured L3 CSI-RS resources.
  the definition of the starting point of 5ms window should be specified to avoid the ambiguity between NW and UE.
For CSI-RS based L3 inter-frequency measurement, there is no need to specify the starting point of 5ms window since all the measurement are MG based

## Slide 5: Way forward – UE behavior when the timing offset exceeds the threshold
  In R16 with single FFT assumption,
    Option1
      For intra-frequency measurement, the UE is not required to measure the configured CSI-RS resources of a neighbour cell if the symbol level misalignment between serving and the corresponding neighbour cell exceeds the threshold.
      For inter-frequency measurement, UE can pick up any cell as the reference cell per frequency layer. UE is not required to measure the configured CSI-RS resources of a neighbour cell if the symbol level misalignment between the reference cell and the corresponding neighbour cell belonging to the same frequency layer exceeds the threshold.
    Option2:
      No spec updates are needed.
  For UE which is not subject to single FFT limitation, it is up to UE how to handle the CSI-RS resources when timing offset exceeds the threshold.

## Slide 6: Way forward – Time validity of the detected associatedSSB
  Adding the definition of detected associatedSSB in 9.10.2.5 section: The associatedSSB is detected if it has been meeting the relevant cell identification requirement during the last 5 seconds.
  Further clarification on the time validity of the detected assocaitedSSB.
  Option 1: The associatedSSB is detected if it has been meeting the relevant cell identification requirement during the last 5 seconds.
  Option 2: If the associatedSSB which has been detectable at least for the time period TPSS/SSS_sync_intra defined in clause 9.2.5.1 becomes undetectable for a period ≤ 5 seconds and then the cell becomes detectable again, the time period is equal to 0.
  Other options are not excluded.