## Slide 1: WF on RRM requirements for FR2 Inter-band DL CA and UL CA
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #98-bis-e
E-meeting, April 12th – 20th, 2021
R4-2105785
Document for: Approval

## Slide 2: Topic #1 Inter-band DL CA enhancements Sub-topic 1-1 Deployment and UE assumptions
Issue 1-1-1: Deployment scenarios assumption for CBM
  Agreements (in GTW):
    Define MRTD and RRM requirements for CBM capable UEs based on co-located deployment scenarios only.
      There are no deployment restrictions (Non-co-located/co-located) for network to configure inter-band DL CA for CBM UEs.
      Note: this does not imply that MRTD requirements will be defined based on intra-band CA assumptions

## Slide 3: Topic #1 Inter-band DL CA enhancements Sub-topic 1-1 Deployment and UE assumptions
Issue 1-1-2: UE assumption for IBM
  FFS:
    Option 1: For an IBM capable UE, with more than 1 panel, the UE is able to actively operate with multiple panels simultaneously. (Nokia, Ericsson)
    Option 2: No further discussion is needed for inter-band IBM UE. (Qualcomm, Intel, LG, Nokia, Huawei, Xiaomi, Vivo)
    Option 3: RRM requirements specified for IBM is based on the assumption that UE is able to actively operate with single panel per time instance. The related requirements should be restrict UE from operating with multiple panels simultaneously. (Apple)

## Slide 4: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 MRTD for CBM
Issue 1-2-1: MRTD value for FR2 inter-band CA
  Agreements (in GTW):
    Candidate options
      Option 1: Do not define any requirements for CBM UEs for FR2 inter-band CA
      Option 2: Introduce UE capability to support MRTD = 260ns and MRTD = 3us (Intel, NEC)
      Option 3: MRTD = 260ns (Vivo, Apple, Intel, OPPO, Xiaomi, Qualcomm, LG, MTK)
      Option 4: MRTD = 3us (NEC, Ericsson, Nokia, Huawei, Docomo, Softbank, AT&T, Verizon, ZTE)
      Other options are not precluded
    Note 1: Decision shall be made in RAN4 #99-e
    Note 2: Companies are encouraged to bring further analysis on achievable MRTD from the network and UE perspectives and the possible impact on the implementation and performance

## Slide 5: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 MRTD for CBM
Issue 1-2-2: Symbol level alignment assumption
  Agreements:
    We come back to this issue once MRTD value in Issue 1-2-1 is agreed if needed.
Issue 1-2-3: How to derive MRTD for FR2 inter-band CA?
  Option 1: MRTD = TAE + Δ_propagation_time (Ericsson, NEC, Nokia, Huawei, Docomo)
    Option 1a: Any change in MRTD should not impact already defined BS TAE of 3 µs for FR2 inter-band CA; i.e. keep Rel-15 values for BS TAE unchanged.
  Option 2: MRTD requirements for CBM UEs should not rely on FR2 inter-band TAE requirement as it was defined for Non-co-located deployments. (Intel, Qualcomm, LG, MTK, OPPO, Apple, Xiaomi, vivo)
    Option 2a: The requirement shall be based on “BS type 1-0” for which TAE requirement is 260ns (Qualcomm)

## Slide 6: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 MRTD for CBM
Issue 1-2-4: Performance degradation due to Rx beam switching
FFS:
  Option 1: UE can switch RX beams without major performance degradation even if MRTD is larger than CP length (Ericsson, NEC, Nokia, Huawei)
  Option 1a: UE can switch RX beams (for example if it can switch during start of UL to DL transition) without major performance degradation (NEC)
  Option 1b: A beam switch could be performed safe within the DL2UL guard if properly performed (Ericsson, Nokia, Huawei)
  Option 2: Any timing impacts should be identified and should need to be accounted in the UE requirements (Nokia, Qualcomm, LG, MTK, OPPO, Xiaomi, vivo).
  Option 2a: If MRTD larger than CP length is defined for inter-band DL CA based on CBM, demodulation performance degradation should be noted due to Rx beam switch. If MRTD less than CP length is defined for inter-band DL CA based on CBM, reuse Rel-16 FR2 intra-band non-contiguous MRTD of 260ns (LG, OPPO)
  Option 2b: For CBM UEs in FR2 inter-band CA, if MRTD is larger than CP length with respect to serving cell numerology, serving cell(s) shouldn’t expect the UE to be able to receive/detect PDCCH(s) on search spaces including at least the first or last OFDM symbol of slot in a band where beam management reference resource(s) it not configured. FFS on multiple numerologies. FFS on further scheduling restrictions on PDCCH and/or PDSCH. (Qualcomm)
  Option 2c: When the MRTD is larger than CP, the demodulation performance can be significantly degraded at any DL symbol(s) due to the unpredictable UE Rx beam switching. (Xiaomi, Intel, OPPO, Xiaomi)
  Option 3: No additional scheduling restriction requirements are needed for Rx beam switching of intra-frequency measurement and layer 1 measurements, if the existing scheduling restriction requirements applied for FR2 intra-band CA are extended to FR2 inter-band CA with CBM type UE. (Huawei)

## Slide 7: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 MRTD for CBM
Issue 1-2-5: Reference signals for Rx beam switch
  Agreements:
    RX beam switch (measurements) should be based on CC configured with beam management RS.
    The CBM UE in FR2 inter-band CA would only need to be configured with DL RS for BM in one CC. And this CC would be the CC with an UL BWP.
Issue 1-2-6: Rx beam switch delay
  Agreements:
    This should be discussed in RF session

## Slide 8: Topic #1 Inter-band DL CA enhancements Sub-topic 1-3 MTTD for CBM
Issue 1-3-1: The MTTD value for FR2 inter-band CA with CBM
  FFS:
    Option 1: This is postponed until MRTD is decided (LG, Nokia, Qualcomm, Apple, Xiaomi)
    Option 2: It is not in the scope of Rel17 as it is related to CBM-based inter-band UL CA (Intel, Ericsson).

## Slide 9: Topic #1 Inter-band DL CA enhancements Sub-topic 1-4 RRM requirements for CBM
Issue 1-4-1: RRM requirements baseline
  FFS:
    Option 1: Rel-15 RRM requirements can be re-used as baseline for Rel-17 FR2 inter-band CBM UE RRM requirements (Nokia)
    Option 1a: Rel-15 CA requirements are applicable for Rel-17 FR2 inter-band CA for CBM even if the SCS different between the bands (Nokia)
    Option 2: Clarification on “baseline” is needed. (Qualcomm, Intel, Ericsson, NEC)
    Option 3: It is not urgent to make such decision (Apple)

## Slide 10: Topic #1 Inter-band DL CA enhancements Sub-topic 1-4 RRM requirements for CBM
Issue 1-4-2: Interruption requirements
  Agreements:
    The interruption requirements applied for CBM based FR2 inter-band CA need to be introduced in Rel-17, which need RF inputs on the RF architecture of CBM type UE.
  FFS:
    Option 1: The existing interruption requirements of intra-band CA can be applied
    Option 2: The existing interruption requirements for inter-band CA in R15/R16 can be reused for CBM type UE in R17
Issue 1-4-3: Scheduling restriction
  Agreements:
    The scheduling availability requirements for FR2 inter-band CA scenario shall be introduced to clarify there is scheduling restriction on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band if UE uses common beam.

## Slide 11: Topic #1 Inter-band DL CA enhancements Sub-topic 1-4 RRM requirements for CBM
Issue 1-4-4: Measurement requirements
  FFS:
    Option 1: Measurement restriction requirements need to be defined for CBM capable UE for inter-band CA scenario (Qualcomm, Intel, MTK, Apple, Xiaomi).
      Option 1a: Existing Measurement restriction requirements would be applicable (Nokia, Ericsson)
    Option 2: RAN4 not to define any measurement restrictions for CBM operation in FR2 inter-band CA (NEC, Huawei).
    Option 3: If MRTD between the two bands is larger than CP length with respect to serving cell numerology, Measurement and/or Scheduling restriction to serving cell(s) on the other band should account for the MRTD, e.g. [x] slots before and after SSB symbols and/or CSI-RS symbol(s) (Qualcomm)

## Slide 12: Topic #1 Inter-band DL CA enhancements Sub-topic 1-4 RRM requirements for CBM
Issue 1-4-5: Scell activation delay
  Agreements:
    Case 1: if PCell/PSCell and the target SCell are in a FR2 band pair with CBM and the target SCell is known, the existing SCell activation requirements can be readily be re-used for CBM capable UE in inter-band CA scenario
  FFS:
    Case 2: if PCell/PSCell and the target SCell are in a FR2 band pair with CBM and the target SCell is unknown,
      Option 1: SCell activation delay would be reduced compared to the existing SCell activation delay requirements for FR1+FR2 CA (OPPO, Qualcomm, Intel, MTK, OPPO, Nokia)
      Option 2: the existing SCell activation requirements in Case 2 with removing L1-RSRP measurement delay can be used for CBM type UE (Huawei, Qualcomm, MTK, Ericsson).
      Option 3: the SCell activation delay requirements defined for the scenario where there is at least one active serving cell in the band, apply (Nokia, Ericsson)
      Option 4: For CBM UEs, SSB samples for Rx beam sweeping shouldn’t be accounted for in SCell activation latency requirement. (Qualcomm, MTK, Ericsson)
      Option 5: SCell activation delay for CBM operation in FR2 inter-band DL CA is 3ms (NEC).

## Slide 13: Topic #1 Inter-band DL CA enhancements Sub-topic 1-4 RRM requirements for CBM
Issue 1-4-6: CSSFoutside_gap
  Agreements:
    If FR2 inter-band CA with two bands are only considered in Rel-17, then the existing requirements on scaling factor CSSFoutside_gap in Rel-16 can be applied to Rel-17.
Issue 1-4-7: Beam management
  Agreements:
    The existing BFD/CBD requirements in Rel-16 can be applied for CBM type UE

## Slide 14: Topic #2 Inter-band UL CA enhancements Sub-topic 2-1 RRM requirements for CBM
Issue 2-1-1: General
  Agreements:
    The RRM requirements for FR2 inter-band CA based on CBM shall not be pursued in Rel-17
Issue 2-1-2: DL interruption at NR SRS carrier based switching
  Agreements:
    The RRM requirements for FR2 inter-band CA based on CBM shall not be pursued in Rel-17

## Slide 15: Topic #2 Inter-band UL CA enhancements Sub-topic 2-2 RRM requirements for IBM
Issue 2-2-1: Interruption due to UL carrier RRC reconfiguration
  FFS:
    Option 1: For IBM type UE, the existing interruption and delay requirements for UL carrier RRC reconfiguration in Rel-16 can be applied in Rel-17 (Huawei, Qualcomm, Ericsson)
    Option 2: Not in the scope of UL CA.
Issue 2-2-2: DL interruption at UE Tx switching between two uplink carriers
  FFS:
    Option 1: The Rel-16 interruption requirement for UE switching between two uplink carriers can be applied in Rel-17 since it is only applicable in FR1. There is no impact due to introducing FR2 inter-band UL CA. (Huawei, Ericsson)
    Option 2: Come back next meeting.

## Slide 16: Topic #2 Inter-band UL CA enhancements Sub-topic 2-2 RRM requirements for IBM
Issue 2-2-3: DL Interruption at NR SRS carrier based switching
  FFS:
    Option 1: RAN4 investigates the interruption requirements for NR SRS carrier based switching applicable for inter-band SRS carrier switching in FR2 (Huawei)
    Option 2: Needs to consult with RF session (Qualcomm, Nokia)
    Option 3: Need further discussion (Ericsson)

## Slide 17: Topic #3 UL gaps for self-calibration and monitoring Sub-topic 3-1 General
Issue 3-1-1: General
  FFS:
    Option 1: RAN4 further discuss whether uplink gaps are captured in RRM specs or in RF specs (Vivo)
    Option 2: This can be discussed later if introduced. (Qualcomm)
    Option 3: This should be firstly discussed in RF session (Intel, MTK, Ericsson, Huawei, Apple, Vivo)
    Option 4: This depends on which type of gaps RAN4 decide to introduce (Nokia)

## Slide 18: Topic #3 UL gaps for self-calibration and monitoring Sub-topic 3-2 UL gaps for PA calibration
Issue 3-2-1: UL gaps for PA calibration
  Agreements:
    Wait for input from RF session how frequent UL gaps for PA calibration is needed

## Slide 19: Topic #3 UL gaps for self-calibration and monitoring Sub-topic 3-3 UL gaps for proximity detection
Issue 3-3-1: Network configured UL gaps
  FFS:
    Option 1: RAN4 would first agree on introduction of configurable UL gaps before detailed design is started (Nokia)
      Option 1a: RAN4 need to agree on UL gap length and periodicity in order to define UL GP (Nokia)
    Option 2: RAN4 needs to investigate the pattern design of network configured UL gaps used for self-calibration and monitoring. (Huawei)
    Option 3: RAN4 study whether the network configured UL gaps is per-UE UL gap or per-FR UL gap. (Huawei)
    Option 4: RAN4 study whether to define the applicability for UL gap pattern configurations. (Huawei)
    Option 5: For network configured UL gap, RAN4 needs to define the scheduling restriction requirements during gap duration.(Huawei)
    Option 6: Wait for RF session agreements (Qualcomm, Intel, MTK, Ericsson, Huawei)

## Slide 20: Topic #3 UL gaps for self-calibration and monitoring Sub-topic 3-3 UL gaps for proximity detection
Issue 3-3-2: UE specific UL gaps
  FFS:
    Option 1: For UE specific UL gap, RAN4 study the conditions allowing UE self-calibration with autonomous UL gaps.(Huawei)
    Option 2: For UE specific UL gap, interruption requirements, including interruption length and interruption rate, to allow UE self-calibration with autonomous UL gaps. (Huawei)