## Slide 1: WF on further RRM enhancement for NR and MR-DC - SRS antenna port switching
Apple, …
R4-2105786
3GPP TSG-RAN4 Meeting #98bis-e
Online, 12 – 20 April, 2021
Agenda item: 8.4
Document for: Approval
Agreement in 1st round
Agreement in GTW (Apr. 16th)
Agreement in 2nd round

## Slide 2: Sub-topic 1-1: Scope of SRS antenna switching requirement (1/3)
Issue 1-1-1: whether delay requirement would be defined in RRM for SRS antenna port switching
  Agreements:
    Do not define SRS antenna port switching delay requirement in RRM
    FFS whether and how to define the scheduling restriction before and after SRS transmission for the cell with SRS antenna port switching
      There are no further scheduling restrictions for SRS symbols in addition to the restrictions defined in RAN1 specifications
Issue 1-1-2: RAN4 defines the requirement only for SRS antenna port switching in FR1 or in both FR1 and FR2
  Agreement
    Define the RRM requirements at SRS antenna switching only for FR1 unless the transient period in FR2 gets clarified in RF session (the scope of “RRM requirements” here depends on the conclusions from issue 1-1-1)

## Slide 3: Sub-topic 1-1: Scope of SRS antenna switching requirement (2/3)
Issue 1-1-3: Impact of SRS antenna port switching to other RRM requirements
  FFS
    Option 1 (CATT): No RRM requirement would be impacted by SRS antenna port switching.
    Option 2 (Apple, OPPO, Ericsson): Regarding the impact of SRS antenna port switching to other RRM requirements, RAN4 would clarify the relaxation or applicability in those RRM requirements whose wanted DL RS or UL RS could be interrupted by SRS antenna port switching, e.g., the delay requirement could be extended if SRS antenna port switching happens during the UE procedure, or the requirement only applies when SRS antenna port switching is not colliding with the reference signal.
    Option 3 (QC, Apple, vivo, Xiaomi):
      No impact to NR measurement requirements relevant to measurements based on SSB/CSI-RS due to NR SRS antenna switching, as NR measurements are always prioritized.
      In EN-DC and NE-DC operation,
        NR SRS antenna switching colliding with E-UTRA measurement
          Interruptions on E-UTRA measurement in the interrupted carrier group are allowed due to NR SRS antenna switching, but NOT allowed due to NR SRS antenna switching for the carriers not in the interrupted carrier group.
          Additional delay can be expected on E-UTRA measurement in the interrupted carrier group when UE is configured to perform NR SRS antenna switching.
          NR SRS antenna switching is allowed to be dropped when colliding with E-UTRA measurement in the interrupted carrier group.
        E-UTRA SRS antenna switching colliding with NR measurement: FFS
    Option 4 (NEC): For impact on other RRM requirements due to SRS antenna port switching, RAN4 shall consider SRS carrier switching as the baseline. RAN4 should first discuss and agree on timing misalignment value before discussion of SRS antenna port switch impact on gNB measurements.
    Option 5(Nokia): Add one note indicating the DL may be affected due to SRS antenna switching if txSwitchImpactToRx is configured.
    Option 6 (Ericsson): Further look into performance impact on timing-based measurements from SRS antenna port switching, and if needed, identify how to mitigate performance degradation (e.g. by avoiding switching during timing-based measurements).
    Option 7 (vivo, Huawei, CATT): Do not consider impact to timing measurements in R17 SRS antenna port switching.
    Option 8 (Nokia, NEC) : TBD after the interruption of SRS antenna port switching is clarified

## Slide 4: Sub-topic 1-1: Scope of SRS antenna switching requirement (3/3)
Issue 1-1-4: Impact of SRS antenna port switching to positioning related requirements
  FFS
    Option 1 (Huawei, Apple, OPPO, Xiaomi, QC, vivo, CATT, Ericsson): Discuss the impact of SRS antenna switching on positioning related measurement in Rel-17 position session.
    Option 2 (Nokia, Ericsson): Discuss the impact of SRS antenna switching on positioning related measurement in this Rel-17 FeRRM.

## Slide 5: Sub-topic 1-2: Interruption requirement applicability (1/2)
Issue 1-2-1: Interruption requirement applicability
  Agreement: The interruption requirement should be defined based on the band combination capability reported by UE, i.e., txSwitchImpactToRx or txSwitchWithAnotherBand.
    FFS: SRS antenna switching interruptions on both DL and UL applies to the band combinations signaled in txSwitchImpactToRx or txSwitchWithAnotherBand.
Issue 1-2-2: whether same interruption requirement applies to different SRS antenna port
  FFS:
    Option 1 (CATT, Apple, OPPO, vivo, Huawei, Xiaomi, QC, Intel, MTK): use same set of requirements for different SRS antenna switch patterns
    Option 2 (LGE): The interruption could be different according to ‘resourceType’.
  Issue 1-2-3: Would the interruption requirement based on different SCS?
  Agreement
    Interruption requirement is based on the aggressor CC and victim CC SCS.
  Issue 1-2-4: Would the interruption requirement differentiate between sync and async cases?
  FFS:
    Option 1 (MTK, Apple, Intel, vivo, OPPO, Xiaomi, QC): No; one single requirement to cover the synchronous and asynchronous scenarios with or without UL TA.
    Option 1a (Apple, Xiaomi, QC): No, interruption requirement is based on the async case for the minimum requirement.
    Option 2 (CATT, Ericsson, LG, Nokia, NEC): Yes, the interruption requirement can differentiate between sync and async cases.

## Slide 6: Sub-topic 1-2: Interruption requirement applicability (2/2)
Issue 1-2-5: Interruption requirement for UE with or without per-FR MG capability
  FFS:
    Option 1 (MTK, CATT, HW, vivo, Ericsson, Intel, QC): Interruption requirement of SRS antenna port switching will not depend on for per-UE or per-FR gap capability.
    Option 2 (Apple, OPPO, Xiaomi): No need to differentiate the requirement for the UE with or without capability of per-FR gap for SRS antenna port switching in RAN4. But in the interruption requirement applicability condition, RAN4 shall clarify that the indication of txSwitchImpactToRx or txSwitchWithAnotherBand is not allowed to indicate any band combination cross FR1 and FR2 if UE is capable of per-FR MG.
    Option 3 (OPPO): Different impact should be considered for UE capable of per UE gap or per FR gap if FR1+FR2 SRS antenna port switching was to be specified.
    Option 4 (Ericsson, Nokia, NEC): Potential impact of UE capability for per-FR gap on interruption requirements can be further studied once the other aspects influencing the interruption time have been settled.

## Slide 7: Sub-topic 1-3: Interruption requirement design (1/3)
Issue 1-3-1: The interruption requirement is defined based on slot level or symbol level
  FFS:
    Option 1 (MTK, Xiaomi, CATT, Apple, QC, vivo, OPPO, Huawei, Intel): based on slot level
    Option 2 (CMCC): if the interruption time only includes transient periods before and after SRS transmission, and considering that the transient period specified in FR session is 15us, it is suggested to specify the interruption requirements based on symbol level.
    Option 3 (LGE, Huawei, Ericsson): The interruption requirement can be defined based on slot level for full uplink symbols within a slot and based on symbol level for flexible symbols within slot.
    Option 4 (NEC, Ericsson, HW, CMCC, Nokia): based on symbol level

## Slide 8: Sub-topic 1-3: Interruption requirement design (2/3)
Issue 1-3-2: The components within interruption time of SRS antenna port switching in FR1
  FFS:
    Option 1 (MTK, Intel, vivo, Apple, Huawei, Ericsson): includes antenna switching time and SRS transmission time
      Option 1a(Ericsson): The interruption time for SRS antenna port switching comprises at least antenna switching time and SRS transmission time.
    Option 2 (Xiaomi): The guard period defined in TS 38.214 is considered as the antenna switching time when defining the interruption requirement.
      If the signalling of txSwitchWithAnotherBand is reported, the interruption requirement at SRS antenna switching should be the guard period defined in TS 38.214 for the aggressor CCs in the band combination.
      If the signalling of txSwitchImpactToRx is reported, the interruption requirement should include the guard period defined in TS 38.214 and SRS transmission time for the aggressor CCs in the band combination.
    Option 3 (CATT): The interruption time of SRS antenna port switching in FR1 includes all guard symbols, all SRS symbols transmitted on other antenna port, and only one switching time.
    Option 4 (Apple, OPPO, QC, vivo, Intel, MTK): The components within interruption time of SRS antenna port switching in FR1 include:
      SRS antenna port switching time (transient time)
      SRS transmission time
      Transient time before and after SRS transmission occasion
    Option 5 (CMCC):
      Since UE stay connection with the serving CCs, the interruption time for SRS antenna port switching delay includes transient periods before and after SRS transmission, and it is not necessary to consider SRS transmission time.
    Option 6 (NEC):
      If victim CC and SRS transmission on aggressor CC are transmitted on the same antenna, interruption requirement shall include SRS antenna switching in delay/TP, SRS transmission, GP, SRS antenna switching back delay/TP.
      If victim CC and SRS transmission on aggressor CC are transmitted on the different antenna, interruption requirement shall include SRS antenna switching in delay/TP, SRS antenna switching back delay/TP only.
    Option 7 (LGE):
      The components within interruption time is
        Time to antenna switching before SRS transmission and SRS transmission time for ‘aperiodic’ SRS-ResourceSet
        Time to antenna switching before SRS transmission for ‘periodic’ or ‘semi-persistent’ SRS-ResourceSet
        Additionally, the time to switch back after SRS transmission depending on UE ehaviour
    Option 8 (Nokia):
      The interruption at SRS antenna switching shall be defined at least within the guard period in Table 6.2.1.2-1 of [TS38.214].
        The interruption requirement shall be defined when the SRS resources of a set in a slot are configured on the symbols which separated by exactly the minimum guard period.
        RAN4 shall discuss if the interruption requirements are defined when the SRS resources of a set in a slot are separated by a length larger than a minimum guard period.

## Slide 9: Sub-topic 1-3: Interruption requirement design (3/3)
Issue 1-3-3: if option 1 or option 4 is adopted in issue 1-3-2, details of the interruption time in FR1
  FFS:
    Option 1 (MTK, QC, Apple, LG, OPPO, Huawei, vivo): Interruption time is specified based on 2 transient period (2*15us) and 6 symbol time
    Option 2 (Apple): Interruption time is specified based on 2 transient period (2*10us) and 6 symbol time
    Option 3 (OPPO): Interruption time is specified based on SRS Transmission time (up to 7 symbols), SRS antenna switching time (15us *2) and transient period (10us*2)
    Option 4 (Ericsson, CATT, Nokia, NEC): depends on the conclusions from other issues.
Issue 1-3-4: If option 2 in issue 1-1-2 is adopted, the components within interruption time of SRS antenna port switching in FR2
  Agreement:
    Based on the conclusion in issue 1-1-2, this issue can be skipped.
    Issue 1-3-5: Interruption requirement proposals
  FFS: options could be found in section 1.2.3 for issue 1-3-5 of email summary document R4-2105686 (this tdoc number would be updated after 2nd round)

## Slide 10: Sub-topic 1-4: others
Issue 1-4-1: if option 2 in issue 1-1-1 is adopted, how to define the SRS antenna port switching delay requirement
  FFS:
    Option 1 (vivo): For SRS antenna port switching delay, RAN4 should consider to specify UE capability to differentiate the needed minimal separation between SRSs and/or between SRS-PUSCH/PUCCH, similar to the transient period capability defined in R16
Issue 1-4-2: LS to RAN1 to check the prioritization rule for SRS antenna switching
  FFS:
    Option 1 (vivo): Send LS to RAN1 to check the prioritization rule for SRS antenna switching, especially for the case in CA/DC operation.
      RAN4 respectfully ask RAN1 that for CA/DC scenarios, whether SRS transmission for antenna port switching in one of the active serving cell can be prioritized over the following transmissions/receptions on any other active serving cells
        SSB/CSI-RS for L1/L3 measurements
        PUSCH/PUCCH transmission with priority index 1 or DL pre-emption transmission
        PUSCH/PUCCH transmission carrying HARQ-ACK/positive SR/RI/CRI/SSBRI and/or PRACH
        PUSCH transmission carrying aperiodic CSI (if periodic/semi-persistent SRS resources are configured)
    Option 2 (OPPO, QC): do not send this LS in option 1.
    Option 3 (Apple, HW, QC, Ericsson, Nokia): needs more discussion.